## Slide 1: VHT Sounding Feedback
Date: 2017-06-11
Authors:

## Slide 2: Recap – VHT Sounding Protocol
Protocol is completely unscheduled
  When medium is idle, initiator can send NDP-A followed by NDP
  If available, responder replies with NDP within SIFS
  After “SIFS+X” LMR is fed back to initiator
SIFS+X
NDP-A
Initiator
NDP
Responder
SIFS
NDP
SIFS
LMR

## Slide 3: Open Questions
What is in the Location Measurement Report (LMR)
  Ideally includes t2 (ToA) and t3 (ToD). similarly to legacy FTM protocol
  Could also include raw CSI and t2’ and t3, where t2 can be derived from FFT window start t2’ and CSI (find first path)
What does “SIFS + X” mean
  Ideally X=0, the initiator has all it needs and can go off channel
  X>0 could be needed for some implementations to finish calculating t2 or even to get the CSI ready

## Slide 4: Discussion
Case for ToA report within SIFS
  Possible for responders with ToA algorithm in hardware
  Ideal case for initiators, half the work already done
  Full transactions is finished within one TxOP, no need for buffers at responder or need for initiator to wait/come back
Case for CSI Feedback
  Low cost responder might not have the computational muscle or implementation complexity to accurately calculate ToA
  Can completely outsource this task to initiator
  CSI should be easily available after SIFS, or shortly thereafter

## Slide 5: Which is the Mandatory Mode?
ToA Feedback within SIFS
  Any initiator who can accept CSI feedback can also accept ToA (ultimately CSI is used to calculate ToA)
  Limitation on the responder, how accurate a ToA can be calculated within SIFS, any?
  Not all responders can be expected to implement this
CSI Feedback
  A responder who already supports ToA within SIFS might not want to offer also CSI feedback
  Not every initiator has the ability to process CSI
  Since this CSI format is new, making it mandatory adds huge cost

## Slide 6: Need for a Mandatory Mode
The mandatory LMR mode needs to include ToA
The responder needs enough time to calculate ToA
Base it on current FTM
  ToA is assumed ready for transmit at next FTM packet
  MinDeltaFtm can be between 1-255 in 0.1 ms increments
  Typically 0.5-1.5 ms is used
This is implementable
How about efficiency?

## Slide 7: Implementation
FTM Setup/Negotiation
  Responders declares MinToaReady similar to MinDeltaFtm
    Tells the initiator when to expect LMR
    After this interval the responder will try to send the LMR to the initiator (use RTS/CTS to see if initiator is there)
  Responder also declares MaxToaAvailable
    Tells the initiator how long LMR will be stored
    The initiator can “pull” the LMR from the responder by starting a new sounding sequence (staggered feedback) or by sending a PS poll
Sounding
Time [ms]
LMR Availability
MinToaReady
MaxToaAvailable

## Slide 8: Case 1: Stay on Channel
If MinToaReady < 3 ms
  Makes sense for initiator to camp on channel
  Activate power save for programmed time
  Responder will send LMR after MinToaReady, once channel is idle
If MaxToaAvailable < 10 ms
  The responder could choose a small MaxToaAvailable to encourage initiators to stay on channel
  This reduces need for large buffers
  Possibly attempt transmitting LMR once more at MaxToaAvailable (RTS-CTS)

## Slide 9: Case 2: Go off Channel
If MinToaReady > 10 ms
  Makes sense for initiator to go off channel
  Come back before MaxToaAvailable expires
  Pull LMR explicitly or start new sounding

## Slide 10: Summary
ToA should be mandatory
  All 11az STA should be able to provide some sort of ToA
  Low cost STA can advertise CSI feedback capability to increase possible accuracy when acting as responder
  High performance APs will offer ToA feedback after SIFS as responder by setting MinToaReady and MaxToaAvailable to 0