## Slide 1: 11az STA Polling for MU NDP Ranging
Date: 2017-07-10
Name | Affiliation | Address | Phone | Email
Liwen Chu |  |  |  | 
Christian Berger |  |  |  | 
Niranjan Grandhe |  |  |  | 

## Slide 2: MU NDP Ranging SP
  MU NDP Ranging SPs are established through STA-AP negotiation
    AP knows the STAs’ SPs (service period) for ranging.
    Individual TWTs are used to define the SPs for NDP MU ranging.
    In TWT SP for measurement NDP exchange, two stages STAs’ polling, NDP exchange
      Before MU NDP exchange, STAs’ readiness need to be polled.
EFTM Request
EFTM Response
EFTM Request
EFTM Response
EFTM NDP
Ranging SP
EFTM NDP
Ranging SP
EFTM NDP
Ranging SP
AP poll STA’s availability at the beginning of EFTM SP
EFTM SP Interval

## Slide 3: STA’s Polling without OFDMA Random Access
  Different STAs with different ranging requirement, e.g. security requirement or non-security requirement can be grouped to different TWT SP and polled separately.
  Basic Trigger with specific AIDs of STAs in User Info fields can poll STAs’ readiness before NDP ranging measurement.
    9, 18, 37, 74 STAs can be polled in 20MHz, 40MHz, 80MHz, 160/80+80MHz respectively without UL MU MIMO operation.
  11ax features or 11ax feature with minor changes can be used here.

## Slide 4: STA’s Polling OFDMA Random Access
  Different STAs with different ranging requirement, e.g. security requirement or non-security requirement can be grouped to different TWT SP and polled separately.
  If many STAs are grouped together in one TWT SP,
    OFDMA random access can be used for STAs to report their readiness.
    STAs can contend the random RUs for transmitting PS-Poll or QoS Null
  Basic Trigger with specific AID 2045 in User Info fields can poll STAs’ readiness before NDP ranging measurement.
  11ax features or 11ax feature with minor changes can be used here.

## Slide 5: Straw Poll
  Do you agree that the polling part of the measurement MU Ranging phase shall use MAC based frame feedback using scheduled OFDMA and OFDMA RA?

## Slide 6: Motion
  Move to add the following text to 11az SFD:
    the polling part of the measurement MU Ranging phase shall use MAC based frame feedback using scheduled OFDMA and OFDMA RA.