## Slide 1: Resource Allocation for Unassociated STAs – Follow Up
Date: 2017-07-12
Authors:
Chittabrata Ghosh, Intel

## Slide 2: Abstract
In this presentation, we discuss about the MU negotiation phase (transmission of iFTMR followed by iFTM) for unassociated STAs
  This is a follow-up presentation from our May 2017 contribution (11-17-0802r1)
Chittabrata Ghosh, Intel
July 2017
        doc.: IEEE 802.11-17/1126r0

## Slide 3: Introduction
11az amendment has agreed upon the following procedure on MU negotiation for unassociated STAs:
  The resource allocation for initial FTM Request in MU negotiation for unassociated STAs to be based on OFDMA random access
  The Ranging ID of the STAs are indicated in the iFTM frame
However, SU or MU mode of iFTM frame transmission by the Responding STA is still open for discussion
  Content corresponding to Ranging ID also needs to be discussed
Chittabrata Ghosh, Intel
July 2017
        doc.: IEEE 802.11-17/1126r0

## Slide 4: Illustration of iFTM frame Transmission in MU Mode
Trigger frame for
random access
DL M-BA
Contention-based UL OFDMA
iFTMR from STA1
ACK/BA to STA1
iFTM for STA 1
FTM response (MU format)
iFTMR from STA2
iFTM for STA 2
iFTM for STA N
iFTM for STA M
Since unassociated STA do not have Ranging IDs yet (Ranging ID in MAC payload of iFTM), MU mode of iFTM is not feasible
  For DL MU PPDU, the ID of the STAs assigned RUs are indicated in the HE-SIG-B of the HE modulated preamble
  In absence of Ranging ID knowledge, unassociated STAs will not be able to decode either the RU or the SS in which the MAC payload of the DL MU PPDU may be transmitted for the intended STA
One option of iFTM in MU mode is that the Responding STA uses the same RU for iFTM on which it has received the iFTMR from the Initiating STA
  Issue: Initiating STAs required to store the OFDMA-RA RUs used for their iFTMRs in their previous on-channel activity
Chittabrata Ghosh, Intel
July 2017
        doc.: IEEE 802.11-17/1126r0

## Slide 5: Proposed iFTM Transmission in SU Mode
We propose to define a SU (broadcast) mode of iFTM transmission from the Responding STA in response to MU iFTMR within the MU negotiation phase
We also define the Ranging ID element to be included in the iFTM frame :
Chittabrata Ghosh, Intel
Trigger frame for
random access
DL M-BA
Contention-based UL OFDMA
FTM Request from STA1
ACK/BA to STA1
FTM response (SU format)
FTM Request from STA2
July 2017
        doc.: IEEE 802.11-17/1126r0

## Slide 6: Ranging ID Lifetime for Unassociated STAs
An unassociated STA with assigned Ranging ID might not complete association with the Responding STA that has assigned the Ranging ID
  In order to release the Ranging ID assigned to an unassociated STA, we propose to define Ranging ID lifetime
  The Ranging ID may be defined by the Responding STA as a common value for a subset of unassociated STAs with the following common metrics:
    Set of Initiating STAs capable of performing HEz-based MU measurements
    Set of STAs with common negotiated TWT SPs or at least the starting TWT SP
  Once the value indicated in the Ranging ID lifetime expires, the ID is automatically released
  The Ranging ID value shall not be used between the unassociated STA and the Responding STA in any UL or DL frame exchange after the ID expires
Chittabrata Ghosh, Intel
July 2017
        doc.: IEEE 802.11-17/1126r0

## Slide 7: Proposed Ranging ID Element in iFTM
The Ranging ID element in iFTM includes the following fields:
  Ranging ID Lifetime: This field indicates the dynamic range similar to RevMC Burst Period (units of 100ms, 16 bits)
    The Ranging ID Lifetime is identical for the set of STAs identified by the Ranging ID-MAC Address pairs in the same Ranging ID element
    Ranging ID lifetime is in units of 100ms
    Ranging ID Lifetime within a Ranging ID element should be at least greater than the duration of the first TWT SP negotiated by set of STAs identified by the Ranging ID-MAC Address pairs
  Count of Ranging ID-MAC Address Pairs: This field indicates the number of Ranging ID-MAC Address pairs included in the current Ranging ID element
  Ranging ID: This field indicates the ID assigned to the unassociated STA from which the Responding STA has received an iFTMR containing the MAC address
There might me multiple Ranging IE Elements within a single iFTM frame
Chittabrata Ghosh, Intel
July 2017
        doc.: IEEE 802.11-17/1126r0

## Slide 8: Ranging ID Lifetime Renewal
Renewal is implicit, no explicit mechanism proposed
Renewed when Initiator responds with the UL NDP solicited by the Trigger frame for UL sounding within the MU measurement phase
  Reset the Ranging ID lifetime to 0 until it expires
When the Responding STA does not hear from the STA (even though the lifetime did not expire), Ranging ID lifetime does not expire till the end of the expiration of the lifetime value
Chittabrata Ghosh, Intel
July 2017
        doc.: IEEE 802.11-17/1126r0

## Slide 9: Ranging ID Lifetime Management
Chittabrata Ghosh, Intel
July 2017
        doc.: IEEE 802.11-17/1126r0

## Slide 10: Summary
We discussed about the possible SU and MU mode of iFTM transmission by the Responding STAs in response to iFTMRs from Initiating STAs
We prefer the SU mode of iFTM transmission over the MU mode
We define Ranging ID element within the iFTM frame containing the Ranging IDs assigned to the unassociated STAs that have sent iFTMRs to the Responding STA using OFDMA RA RUs
Chittabrata Ghosh, Intel
July 2017
        doc.: IEEE 802.11-17/1126r0

## Slide 11: Straw Poll 1
Do you support the SU mode of iFTM transmission by the Responding STA in response to MU iFTMR from unassociated STAs?
Chittabrata Ghosh, Intel
July 2017
        doc.: IEEE 802.11-17/1126r0

## Slide 12: Straw Poll 2
Do you support the definition of Ranging ID element in iFTM as in Slide 7?
Chittabrata Ghosh, Intel
July 2017
        doc.: IEEE 802.11-17/1126r0

## Slide 13: Appendix
July 2017
Chittabrata Ghosh, Intel
        doc.: IEEE 802.11-17/1126r0

## Slide 14: Motion
Move to adopt the following text to the SFD and instruct the SFD editor to include it in TGaz SFD under Subsection 3.2 and grant editorial license to SFD Editor
  The resource allocation for initial FTM Request in MU negotiation for unassociated STAs to be based on OFDMA random access as depicted in Slide 3?
Moved by: Ganesh Venkatesan
Seconded: Chittabrata Ghosh
Y:12 N:0 A: 4
Motion passes
May 2017
        doc.: IEEE 802.11-17/0802r1
Chittabrata Ghosh, Intel