## Slide 1: Comment resolution on BSR CID 8426
Date: 2017-07-10
Authors:
Name | Affiliation | Address | Phone | Email
Zhou Lan | Broadcom Ltd. |  |  | Zhou.lan@broadcom.com
Chunyu Hu |  |  |  | 
Matthew Fischer |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 2: CID 8426
CID | Commenter | clause | Comment | Proposed Change | Resolution
8426 | Robert Stacey | 25.34 | The two methods for reporting queue size (Queue Size field in QoS Data and BSR A-Control) are not compatible with each other. The Queue Size in QoS Data is reported per TID while Queue Size in BSR A-Control is reported per AC. An AP collecting Queue Size per TID would not know how to partition the BSR information (since it is the sum of the queue size for two TIDs). An AP that collects queue size per AC may make inaccurate allocations to STAs that do not support multi-TID aggregation or if the AP itself cannot receive multi-TID A-MPDUs. | Change the BSR so that it either reports queue size per TID or simplify it so that it just indicates which Acs have traffic. | Revised – Agree in principle. Refer to IEEE 802.11-17/1132r1 for discussions TGax editor to make the changes shown in 11-17/1131r0

## Slide 3: Abstract
CID 8426, 8427 point out the incompatibility issue of QoS Control and BSR Control
TGax adopted contribution 11-17/0607r0 [1] in May meeting to resolve CID 8427
  Increase scaling factor to 32K for QoS Control.
However the fundamental issue of incompatibility of QoS Control and BSR Control has not been resolved.
This contribution proposes a resolution for CID 8426:
  an alternative BSR Control encoding to facilitate 11ax UL MU scheduling

## Slide 4: Incompatibility of QoS Control and BSR Control
Contribution 0477r0 [2] pointed out the incompatibility issue of supporting two buffer status report mechanisms
  The Queue Size in QoS Data is reported per TID while Queue Size in BSR A-Control is reported per AC
  BA agreements are established based on per TID info
  Eventually the per AC Queue size needs to be separately recorded and converted to per TID Queue size
QoS Null frame that has both QoS control and BSR Control present is used for solicited BSR report
  Can AP reconcile buffer size in the QoS control with that in the BSR control ?
Most implementations will likely only use QoS control for UL MU scheduling, instead of BSR Control.
Providing buffer size info per AC does not provide significant benefit but complicates the implementation and adds extra overhead
  For best scheduling performance AP needs per-TID information

## Slide 5: Increasing scaling is not a remedy
Increasing the scaling factor of QoS Control and BSR Control increases the reportable range but reduces the accuracy of the report as discussed in contribution 11-17/0766r1 [3] (related discussion also available in the Annex of this doc.)
  Over 1ms air time may be wasted due to coarse resolution (i.e. several hundred data symbols may be wasted)
  Very hard for AP scheduler to make smart decision based on inaccurate Queue size report
 | 16 K octets | 32 K octets | 64 K octets
121.9Mbps @(BW=20 NSS=1) | 1.1ms | 2.2ms | 4.4ms
243.8Mbps@(BW=40 NSS =1) | 0.52ms | 1.04ms | 2.08ms
243.8Mbps@(BW=20 NSS =2) | 0.52ms | 1.04ms | 2.08ms
487.5Mbps@(BW=40 NSS =2) | 0.26ms | 0.52ms | 1.02ms

## Slide 6: Making BSR usage more practical
Two pieces of information are critical for UL MU operation
  Buffers status report
  Headroom for power control (MCS selection)
A modified BSR Control can contain all necessary information for scheduling
  Combining these two factors within a single BSR will increase the efficiency of the UL MU procedure
  AP doesn’t have to separately gather multiple pieces of information for its decision making

## Slide 7: Proposal
Replace the per AC Queue size in the BSR Control with per TID Queue size as follows
  Increasing the Queue Size from 8 bits to 14 bits increases the range of BSR to 4M octet with a resolution of 256 bytes (i.e. a reasonable range to support 256 BA with good resolution to maintain efficiency)
  The QoS control field can be used to report a second TID with queue size up to 2 M octet
  AC is a reduced form of TID intended to make EDCA simpler to implement, TID is the appropriate choice for a scheduling function to ensure QoS
UL power headroom is included to assist in determining the complete trigger specification
B0 B3 | B4 B17 | B18 B19 | B20 B24 | B25
TID | Queue Size | Scaling factor | UL power headroom | Maximum Transmit Power flag
4 bits | 14 bits | 2 bits | 5 bits | 1 bit

## Slide 8: Straw poll
Which option do you support for the BSR modification to resolve CID 8426
    Per TID with headroom
    Per TID only
  Option 1
  Option 2
  Abstain
B0 B3 | B4 B17 | B18 B19 | B20 B24 | B25
TID | Queue Size | Scaling factor | UL power headroom | Maximum Transmit Power flag
4 bits | 14 bits | 2 bits | 5 bits | 1 bit

## Slide 9: Straw poll
Do you support to
    Adopt document IEEE 802.11-17/1131r1 as the resolution of CID 8426
  Yes
  No
  Abstain

## Slide 10: Back up slides

## Slide 11: Problem of Supporting 256 BA
Queue Size High and Queue Size All in BSR Control is limited in size of 4.1M octets with 1.6K octets scaling factor
To support 2 TIDs with 256 BA agreement, Queue Size High needs to indicate at least 6M octets.
  The maximum MPDU size is 11454 octets
  To support 256 BA, need 11454*256 = 2932224 octets
Queue Size All subfield fails to support more than 2 AC that has TID with 256 BA
No reserved bits to further extend the range

## Slide 12: Consideration of scaling factor
Higher scaling factor increases the range of the Queue Size Report, however fails to provide accurate information as input for scheduler
Current BSR Control supports 4 scaling factor: 16, 128,1024,16384
What happens if scaling factor is over 16k octets……
Very likely over 1 ms will be wasted or filled with padding due to queue size report with scaling factor bigger than 16k Octets
64k scaling factor may cause the waste of over 300 OFDM symbols
  4.4ms/12us = 343
Scaling factor over 32k Octets is not preferred
 | 16 k octets | 32 k octets | 64 k octets
121.9Mbps @(BW=20 NSS=1) | 1.1ms | 2.2ms | 4.4ms
243.8Mbps@(BW=40 NSS =1) | 0.52ms | 1.04ms | 2.08ms
243.8Mbps@(BW=20 NSS =2) | 0.52ms | 1.04ms | 2.08ms
487.5Mbps@(BW=40 NSS =2) | 0.26ms | 0.52ms | 1.02ms

## Slide 13: Another problem of higher scaling factor
A big range of Queue Size report will have to use coarse resolution of 64 k Octets
UL MU scheduler will have difficulty of deciding the RU allocation based on this coarse resolution
1024 | 64 k Octets resolution
0 octets
64 000 octets
4096000 octets
1024 | 32 k Octets resolution
0 octets
64 000 octets
2048000 octets
98% cases will use 64 k Octet resolution

## Slide 14: Problem statement (cont.)
Current BSR Control in Draft spec 1.2 is limited in size of 4.1M octets with 1.6K octets scaling factor in both Queue Size High and Queue Size All fields
Per baseline spec, the maximum MPDU size is 11454 octets, in order to support 256 BA window the required buffer size is 11454*256 = 2932224 octets
If the STA supports 2 TIDs with 256 BA agreement, 3*2= 6 M octets is needed in the Queue Size High field
If the STA supports two ACs each supporting two TIDs with 256 BA agreement, 12 M octets is needed in the Queue Size All field
The current BSR Control can not support the above use cases and there is no reserved bits available for further range extension
No reserved bits to further extend the range

## Slide 15: Problem statement
Contribution 0477r0 [1] pointed out the incompatibility issue of supporting two buffer status report mechanisms
  The Queue Size in QoS Data is reported per TID while Queue Size in BSR A-Control is reported per AC
  All the BA agreements are established based on per TID info
  Eventually the per AC Queue size needs to be separately recorded and converted to per TID Queue size
In addition, QoS Null frame that has both QoS control and BSR Control present is used for solicited BSR report
  AP will get confused if the buffer size in the QoS control conflicts with that in the BSR control
As a results, most implementation will end up with only using QoS control for UL MU scheduling while ignoring the BSR Control.
Providing buffer size info in a different format (i.e. per AC) doesn’t provide significant benefit while complicating the implementation and adding extra overhead

## Slide 16: Problem statement (cont.)
The current BSR Control fails to support Multi-TID aggregation due to similar reasoning as presented in the previous slide
  Draft spec. 1.2 support Multi-TID aggregation with 256 BA window
  The current BSR Control will not be able to support Multi-TID aggregation with more than two TID supporting 256 BA window
  In order to support TWT operation, a STA may need to buffer UL data to wait for the next service period
  Assuming the STA is scheduled in a 996 RU with Nss =1 and MCS 11 for 1024QAM
  Assuming the STA is under a TWT agreement of 5ms wake interval
  4M Octets total Queue size for all AC may not be sufficient to support TWT operation