## Slide 1: Scalable Location Protocol
Date: 2017-08-30
Authors:

## Slide 2: Summary
In this presentation we are outlining a practical realization of transmissions between anchor stations such as to enable a client station to calculate its location while only listening to these transmissions.
We realizing this localization method by to the maximum extent reusing ranging functionality anyways being standardized for 802.11az such as to minimize the extra functionality required to realize scalable location.

## Slide 3: Fixed Wi-Fi Devices
Any venue is likely to contain a large number of fixed Wi-Fi devices. We can use these devices to facilitate scalable location.

## Slide 4: Client Centric Scalable Location
Client to be located
Access Point
Access Point
Example Scenario
Anchor Client
Anchor Client
Anchor Client

## Slide 5
Example Frame Exchange Protocol

## Slide 6: Reuse Ranging Protocol
Reuse ranging protocol
Can use SU or MU ranging
MU ranging has the inherit benefit of being scheduled
  Facilitates clients listening to transmissions
  No need to add new protocol for the scheduling of the ranging

## Slide 7: TGaz SFD UL MU Ranging Sounding

## Slide 8: MU ranging with Extra Frame Exchanges
NDP
Trigger
Frame
AP Station
Anchor Client
Anchor Client
Anchor Client
NDP
NDP
NDP
NDPA
Green arrows – Regular ranging frame exchanges
Blue arrows – Extra ranging exchanges
Trigger
Frame
Trigger
Frame
Note: No new transmissions or protocol required. It is simply up the anchor stations to listen to the NDP transmissions, calculate their TOA and report them.

## Slide 9: MU Ranging Operation
Green arrows - Already planned exchanges in a single MU ranging operation
Blue arrows – More possible exchanges in a single MU ranging operation
Anchor
Client
AP
Anchor
Client
Anchor
Client
In one shot we can communicate with all other STAs!

## Slide 10
Access point
Anchor Client 1
iFTM request
iFTM (response)
Negotiation and assignment to periodic measurement interval
Anchor Client 2
MU Poll
MU Poll Response
MU Poll Response
Trigger Frame
UL NDP
UL NDP
DL NDPA
DL NDP
Unencrypted measurement in periodic measurement interval
AP Meas. Feedback
AS Meas. Feedback
AS Meas. Feedback
Unencrypted measurement feedback
Unencrypted reverse measurement feedback - Proposed optional
Example Protocol with MU Ranging

## Slide 11
Client Location Calculation

## Slide 12: TDOA - Hyperbolic Navigation
Source: http://asadahmedansari6395.blogspot.ca/2016_04_01_archive.html
Recap from [3]:

## Slide 13: Propagation paths and time stamps
AP
Anchor Client
Client
to be located
Illustrating timing diagram showing double sided feedback of time-stamps:
t2
t1
t4
t3
DL NDP
UL MU NDP
t5
t6
t2, t3
t1, t4
‘AP to STA feedback’
‘STA to AP feedback’
- optional
Recap from [3]:

## Slide 14: Double-Sided Differential Distance Calculation
The client listens to the exchanges between the AP and the anchor client and records the time t5 when it receives the UL MU NDP from the fixed client and the time t6 when it receives the DL NDP from the AP.
The client also listens to the relayed t2 and t3 from the AP and the relayed t1 and t4 in the feedback from the anchor client.
The differential distance between the client and the AP vs. the anchor client can now be calculated as follows:
  D_01 = [t6 – t5 – (t3 – t2 + T_12)] * c
  Using T_01 = [(t4 – t1) – (t3 – t2)]/2
  We get D_01 = [t6 – t5 – (t3 – t2 + 0.5*t4 – 0.5*t1 – 0.5*t3 + 0.5*t2)]*c
  Or finally:
Note that the above expression for the differential distance D_12 does not depend on the ToF, T_12, between the AP and the anchor client. Thus this method of calculating D_12 is insensitive to LOS obstructions between the AP and the anchor client.
D_12 = [t6 – t5 – 0.5*t3 + 0.5*t2 – 0.5*t4 + 0.5*t1]*c
Or just use single sided differential distance calculation [3].
Recap from [3]:

## Slide 15: Differential Distance Location Estimation Calculations
DTOF12 = t6 – t5 – 0.5*t3 + 0.5*t2 – 0.5*t4 + 0.5*t1
Client
(x0,y0)
Unknowns:
Client coordinates x0,y0
2 unknowns
Equations:
Differential ToF equations
  DToF12 = (R01-R02)/c
  DToF13 = (R01-R03)/c
  DToF23 = (R02-R03)/c
3 equations, non-linear
Rij
R02(x0,y0)
In two dimensions with three anchors:
(x3,y3)
t1
t5
t2
t3
t4
t6
Anchor 2
Anchor 1
Anchor 3
See Appendix A for how to solve for location!

## Slide 16
Client Listening

## Slide 17: Client Listening
Client listens to ranging exchanges
AP announcement of the ranging schedule can facilitate the clients listening
  Knows when and where to listen

## Slide 18
Ranging Schedule

## Slide 19: Schedule Content
Two levels of schedule complexity:
  AP conveys scalable ranging operations in its own channel
  AP conveys scalable ranging operations also for neighboring APs channels
Content:
  Times of ranging
  Ranging format parameters (e.g. number of antennas)
  Anchor Clients LCI information
Additional content for neighboring APs operations:
  BSS channels and bandwidths
  Clock mappings
Recap from [3]:

## Slide 20: Schedule Conveying
For example:
  Periodically broadcast in an APs beacons
  Counter in every beacon to count down to presence schedule

## Slide 21
Protocol to Add

## Slide 22: Protocol Aspects to Add
Bit in iFTM request indicating desire for unencrypted ranging and is willingness to share LCI
Protocol for periodic announcement of scalable location ranging schedule
Optional:
  Bit in iFTM request indicating desire for double sided ranging measurement feedback
    And the extra frames for the reverse ranging measurement feedback
    This double sided feedback also have uses other than for scalable location
  ToA feedback from extra listening opportunities in MU ranging
Only limited additions needed!

## Slide 23
Conclusions

## Slide 24: Conclusions
Any venue is likely to contain a large number of fixed Wi-Fi clients
Can use such ‘Anchor Clients’ to enable scalable location
Use regular ranging protocol to provide time-stamped transmissions to use for client location
Minimal additions required to protocol for regular ranging

## Slide 25
Appendix A:
Calculation of Client Location

## Slide 26: TDOA - Hyperbolic Navigation
Source: http://asadahmedansari6395.blogspot.ca/2016_04_01_archive.html

## Slide 27: Propagation paths and time stamps
AP
Anchor Client
Client
to be located
Illustrating timing diagram showing double sided feedback of time-stamps:
t2
t1
t4
t3
DL NDP
UL MU NDP
t5
t6
t2, t3
t1, t4
‘AP to STA feedback’
‘STA to AP feedback’
- optional

## Slide 28: Double-Sided Differential Distance Calculation
The client listens to the exchanges between the AP and the anchor client and records the time t5 when it receives the UL MU NDP from the fixed client and the time t6 when it receives the DL NDP from the AP.
The client also listens to the relayed t2 and t3 from the AP and the relayed t1 and t4 in the feedback from the anchor client.
The differential distance between the client and the AP vs. the anchor client can now be calculated as follows:
  D_01 = [t6 – t5 – (t3 – t2 + T_12)] * c
  Using T_01 = [(t4 – t1) – (t3 – t2)]/2
  We get D_01 = [t6 – t5 – (t3 – t2 + 0.5*t4 – 0.5*t1 – 0.5*t3 + 0.5*t2)]*c
  Or finally:
Note that the above expression for the differential distance D_12 does not depend on the ToF, T_12, between the AP and the anchor client. Thus this method of calculating D_12 is insensitive to LOS obstructions between the AP and the anchor client.
D_12 = [t6 – t5 – 0.5*t3 + 0.5*t2 – 0.5*t4 + 0.5*t1]*c
Or just use single sided differential distance calculation [3].

## Slide 29: Differential Distance Location Estimation Calculations
DTOF12 = t6 – t5 – 0.5*t3 + 0.5*t2 – 0.5*t4 + 0.5*t1
Client
(x0,y0)
Unknowns:
Client coordinates x0,y0
2 unknowns
Equations:
Differential ToF equations
  DToF12 = (R01-R02)/c
  DToF13 = (R01-R03)/c
  DToF23 = (R02-R03)/c
3 equations, non-linear
Rij
R02(x0,y0)
In two dimensions with three anchors:
(x3,y3)
Solve for location, e.g. with Newton iterations – described in following slides.
t1
t5
t2
t3
t4
t6
Anchor 2
Anchor 1
Anchor 3

## Slide 30: Newton’s method for solving non-linear equation
x
x1
x3
x2
etc.
Solve equation:

## Slide 31: Solving of non-linear system of equations
Use Newton’s method for multiple variables:
Iterate according to:
Non linear system of equations:
Linearization:
where
Over-determined non-linear system of equation to solve for Dx:
Least squares solution for iterative step:
- solve for x*

## Slide 32: Our derivatives
To simplify the equations, measure time in light seconds - the distance light travels in one second.

## Slide 33: Iterative solution for client position (x0,y0)
Iterations:
Step calculation. LS solution to:
Note: Time in units of light seconds

## Slide 34: References
[1] “Client Positioning using Timing Measurements between Access Points”, Erik Lindskog, Naveen Kakani, Raja Banerjea, Jim Lansford and Jon Rosdahl, IEEE 802.11-13/0072r1.
[2] “A Low Overhead Receive Only Wi-Fi Based Location Mechanism”, Erik Lindskog, Hong Wan, Raja Banerjea, Naveen Kakani and Dave Huntingford, Proceedings of the 27th International Technical Meeting of The Satellite Division of the Institute of Navigation (ION GNSS+ 2014), Tampa, Florida, September 2014, pp. 1661-1668.
[3] “Passive Location”, Erik Lindskog, Naveen Kakani and Ali Raissinia, IEEE 802.11-17/0417r0.

## Slide 35
Thank You!