## Slide 1: Communicating Wake-up Operating Parameters
Date: 2017-09-13
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
Wake-up operating parameters are used to govern WUR mode operation.
Example wake-up operating parameters:
  WUR Beacon interval,
  Minimum wake-up duration,
  Basic unit,
  STA identifier,
  Time required for turning on PCR,
  Duty cycle schedule of the WURx,
  …
Background

## Slide 3
Wake-up operating parameters can be classified into two types:
  Common: applicable to all of WUR STAs
    indicated by AP, e.g.,
      WUR Beacon interval
      Minimum wake-up duration
      Basic unit
  User-specific: applicable to a particular WUR STA.
    Some can be negotiated between STA and AP, e.g.,
      Duty cycle schedule of the WURx
    Some are indicated by AP, e.g.,
      STA identifier for unicast wake-up frame
    Some are indicated by STA, e.g.,
      Time required for turning on PCR
Some wake-up operating parameters are related. For example,
  Before WUR STA negotiates duty cycle schedule with AP, it shall be able to know the minimum wake-up duration and basic unit from AP
Observation

## Slide 4
Proposal
Common wake-up operating parameters shall be indicated in Beacon frame, Probe Response frame and/or (Re)association Response frame.
  User-specific wake-up operating parameters shall be communicated in WUR Action frame and/or (Re)association Request/Response frame.
    Negotiation of user-specific wake-up operating parameters may be done during the association procedure.

## Slide 5: Reference
11-17-0575-03-00ba-spec-framework
11-17-0342-04-00ba-wur-negotiation-and-acknowledgement-procedure-follow-up

## Slide 6: SP
Do you support adding the following to 11ba SFD?
  Common wake-up operating parameters shall be indicated in Beacon frame, Probe Response frame and/or (Re)association Response frame; and user-specific wake-up operating parameters shall be communicated in WUR Action frame and/or (Re)association Request/Response frame.
  Note: common wake-up operating parameters are applicable to all WUR STAs while user-specific wake-up operating parameters are applicable to a single WUR STA only.