## Slide 1: Follow-up on Signaling Method for Data Rates
Date: 2017-09-10
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Jinyong Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
We discussed the signaling method for multiple data rates in last f2f July meeting.
  In [1], we have shown that Signature Sequence was advantageous in terms of performance and overhead when a 2-bit indication for data rate is assumed.
Some members have questioned such as following issues.
  due to the sequence detection which is performed by using the correlation, it required the much power consumption.
  A sig field can consist of information for data rate without including CRC.
Also, we have decided supporting of two data rates (i.e. 62.5kbps and 250kbps) for WUR PPDU in the previous meeting.
  Supporting of other data rates is TBD.
  So, we may consider a 1-bit indication for data rate to minimize the overhead.
Therefore, in this contribution, we discuss the several consideration points and investigate more the performance of Signature sequence and signal field.

## Slide 3: Recap of Signature sequence [1]
Design for Signature Sequence
  Multiple signature sequences are used for multiple data rates
    Herein, One signature sequence indicates one specific data rate.
  Signature sequence is designed to have a Hamming distance with equal error correction capability.
    For the Signature sequence, a pseudo-random sequence can be used.
Performance when 2bit indication for data rates is assumed
channel | TGnD( targeted SNR at 1% PER : -3.7dB) |  |  | UMi( targeted SNR at 1% PER : -2dB ) |  | 
 | SS(6,3) | SS(9,5) | SS(12,7) | SS(6,3) | SS(9,5) | SS(12,7)
Data rate | 62.5Kbps | 62.5Kbps | 62.5Kbps | 62.5Kbps | 125Kbps | 125kbps
Length | 96us | 144us | 192us | 96us | 72us | 96us
SNR at 1% PER | -3dB | -4.8dB | -6dB | -3dB | -2.6dB | -4dB

## Slide 4: Consideration points (1/2)
Considering on Power consumption
  As like as transmission of WUR payload, a signature sequence is modulated with OOK and Manchester coding can be applied.
  So, after the synchronization of WUR PPDU, WUR receiver is able to perform the envelop detection for received signature sequence signal.
    Assuming a signature sequence of length 5, following sequence can be obtained after envelop detection.
      For example, decoded signature sequence( i.e. decode_ss) = 1 0 1 0 1
  And then, WUR receiver can detect the signature sequence by using the simple logic operations such as XOR.
    For example, STA selects the sequence which has a minimal output value by applying the following operation.
      Rx_SS = min( sum( XOR( Decode_SS, SS_i)))
        Where SS_i is one of sequence among the signature sequences
  Therefore, a detection of signature sequence does not consume much power because it does not use any correlation operation which requires large power consumption.

## Slide 5: Consideration points (2/2)
No CRC in sig field ( assuming a 2-bit indication for data rate)
  Due to absence of CRC bit in Sig-field, WUR receiver can not stop the decoding of WUR PPDU when SIG field has an error.
    It can occur the more power consumption due to needless decoding of WUR payload.
  And, even if CRC bits are not included in Sig-field, we can not achieve the targeted SNR when the lowest data rate (i.e. 62.5kbps) is applied.
    Assuming support for both TGnD channel and Umi channel(it’s performance is described in Appendix A), it may be required to have the lower data rate than 31.25kbps.
Data rate | SNR at 1% PER | Length
125kbps | -0.4 dB | 16us
62.5kbps | -2.1 dB | 32us
31.25Kbps | -3.8 dB | 64us
Targeted SNR = -3.7 dB at 1% PER

## Slide 6: Simulation Assumption
13 subcarriers (4 MHz) are used for a WUR symbol
Data rate for signature sequence and sig field
  31.25Kbps
    32us OOK symbol with Manchester coding (4us ON+ 4us OFF + 4us ON+ 4us OFF + 4us ON+ 4us OFF + 4us ON+ 4us OFF vice versa)
  62.5Kbps
    16us OOK symbol with Manchester coding (4us ON+ 4us OFF + 4us ON+ 4us OFF vice versa)
  125Kbps
    8us OOK symbol with Manchester coding (4us ON+ 4us OFF and vice versa)
Example for signature sequence to indicate the 1-bit information
  For HD =3, { 0 0 0 , 1 1 1}
  For HD =5, { 0 0 0 0 0 , 1 1 1 1 1 }
20MHz sampling rate
TGnD and UMi NLoS channels in 2.4GHz
No impairments
SNR is defined considering 20MHz bandwidth

## Slide 7: Performance of 1 bit indication(1/3)
Signature sequence in TGnD
  As shown in results, we can easily achieve the targeted SNR by using the lowest data rate (i.e. 62.5Kbps) and we also confirmed that by using sequence with HD=3 the targeted SNR can be attained.
  Also, results in simulation show that we can reduce the overhead due to signature sequence by applying the higher data rate (i.e. 125kbps) than lowest data rate.
 | HD =3 | HD =5
125kbps | -3.7 dB | -5 dB
62.5kbps | -4.6 dB | -6.6 dB
Targeted SNR = -3.7 dB at 1% PER
 | HD =3 | HD =5
125kbps | 24us | 40us
62.5kbps | 48us | 80us
Length

## Slide 8: Performance of 1 bit indication (2/3)
Signature sequence in Umi
  We can check the similar trend with that of TGnD channel.
 | HD =3 | HD =5
125kbps | -2.7 dB | -3.5 dB
62.5kbps | -2.5 dB | -4.7 dB
Targeted SNR = -2 dB at 1% PER
 | HD =3 | HD =5
125kbps | 24us | 40us
62.5kbps | 48us | 80us
Length

## Slide 9: Performance of 1 bit indication(3/3)
Sig field w/o CRC
  In TGnD channel, we can’t obtain the desired performance by using the 62.5kbps data rate.
    To achieve the targeted SNR, it requires the lower data rate than 62.5kbps.
  In UMi channel, we can achieve the targeted SNR by using the 62.5kbps data rate as described in appendix B.
  But, to achieve the targeted SNR at both channels (TGnD and UMi), the required the data rate should be a lower data rate than 62.5kbps.
Data rate | 125kbps | 62.5kbps | 31.25kbps
Received SNR | -1.9 dB | -3.6 dB | -5.1
Targeted SNR = -3.7 dB at 1% PER
Overhead
Data rate | 125kbps | 62.5kbps | 31.25kbps
length | 8us | 16us | 32us

## Slide 10: Conclusion
In the receiver, the detection of signature sequence doesn’t require more power consumption because we don't need to operate the correlation for detection.
  The detection for signature sequence can be performed with envelop detection and simple logic operation such as XOR.
From the verification of signature sequence and sig-field, we can check the following.
  Even if Sig-field doesn’t include the CRC, the lower data rate than 62.5kbps should be applied to satisfy the targeted SNR.
  So, it needs to define the new data rate for preamble or to apply the additional processing such as repetition to support the lower data rate than 62.5kbps.
  In contrary, Signature sequence can achieve the performance by using the low data rate of WUR PPDU without additional things and the difference of length between SS and sig-field is minor.
    And, As shown in [1], by applying the Manchester coding on signature sequence, we can obtain the enhanced performance and minimize overhead.

## Slide 11: Straw Poll 1
Do you agree to add following into 11ba SFD?
The data rate for WUR payload is signaled by using the signature sequence.
  Signature sequence is included in the WUR preamble.
    Detail for Signature sequence is TBD
Y/N/A :

## Slide 12: Straw Poll 2
Do you agree to add following into 11ba SFD?
  Manchester code shall be applied on Signature sequences.
Y/N/A :

## Slide 13: Reference
[1] IEEE 802.11-17/963r0, Signaling method for multiple data rates
[2] IEEE 802.11-17/575r2, Spec framework

## Slide 14: Appendix A : No CRC in sig field
For 2 bit indication
  In UMi channel, we can check that it can not achieve the targeted SNR even if the 31.25kbps data rate is applied at SIG-field without CRC.
Data rate | SNR at 1% PER
125kbps | 1.8 dB
62.5kbps | -0.4 dB
31.25Kbps | -1.7 dB
Targeted SNR = -2 dB at 1% PER

## Slide 15: Appendix B : No CRC in sig field
For 1-bit indication
  Umi channel
Data rate | 125kbps | 62.5kbps | 31.25kbps
Received SNR | -1.2 dB | -2.7 dB | -4.1
Targeted SNR = -2 dB at 1% PER
Overhead
Data rate | 125kbps | 62.5kbps | 31.25kbps
length | 8us | 16us | 32us