## Slide 1: WUR Operating Channel
Date: 2017-09-xx
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Robert Stacey |  |  |  | 
Azizi Shahrnaz |  |  |  | 
Ehud Reshef |  |  |  | 
Dan Bravo |  |  |  | 
Yaron Alpert |  |  |  | 

## Slide 2: Abstract
There has been many presentations that discuss the operating channel of WUR [1-6]
We provide our thought and consideration for this topic in this presentation

## Slide 3: Consideration for the Operating Channel of PCR and WUR
We think the operating channel of PCR and WUR may not be the same due to the following reasons
  Due to extremely high false detection rate [1], if the operating channel of PCR is in a DFS channel, then AP has to use a different channel for WUR operation if WUR operation is needed
  The range in 5 GHz band may not be met [7], and a dual-band concurrent AP can use 2.4 GHz band and channel as the operating channel of WUR
  STA may only support WUR in 2.4 GHz band for low power/cost implementation, and a dual-band concurrent AP can use 2.4 GHz band and channel as the operating channel of WUR even if PCR operating channel is in 5 GHz band

## Slide 4: Consideration of Different Operating Channel for PCR and WUR
Channel Switch at the AP
  Channel switch maybe required if AP is not dual-band concurrent
  CTS-to-self transmission may be required on the operating channel of PCR to stop the transmission of Intra-BSS STA
  Developing new mechanism like Notice of Absence may not work because legacy STAs may not support it
  We recognize that there is no ideal solution. Hence, we think it should be up to AP to decide if it wants to do channel switch or just reject any WUR request from the STA
Different Range
  Operating range of WUR should not be much less than the operating range of PCR. For example, operating WUR in 5GHz band when PCR is in 2.4 GHz band may not work.
  If Operating range of WUR is larger than the operating range of PCR, then STA’s self recovery scheme, which we expect to be implementation specific, should take care of the mobility issue
In summary, we think most of the inconvenience is on AP side, and since AP knows its capability, AP should have the flexibility to decide the WUR operating channel.

## Slide 5: Consideration for Future
We see there are some interests to use WURx as a low power receiver for other applications like AP discovery [8-9]
  Similar to the usage of BLE for Wi-Fi discovery
  A common channel may be required for simplifying the scan requirement
We see there are some interests to have multi-user WUR transmission [5-6]
  Different STA in one BSS may operate on different channels for WUR reception
There maybe more ideas …
Design for all these proposals may not happen now, but preventing the possibility of all these proposals may not be ideal as well.
A compromise is that we let AP decide the channel, then all these ideas may be accommodated in the future.

## Slide 6: Proposal
We propose that AP decides the WUR operating channel
  AP can decide a WUR operating channel different from PCR operating channel if PCR operating channel is in DFS
  AP can decide a WUR operating channel in 2.4 GHz band if AP is dual-band concurrent and PCR operating channel is in 5 GHz band
  AP can indicate this in beacon if all the associated STA in WUR mode should use the same WUR operating channel or AP can indicate WUR operating channel in individual WUR negotiation
    Note that if we agree on multi-user transmission of WUR, different associated STA can use different WUR operating channels
  Additional WFA program or vendor specific application can configure AP to uses a recommended channel for discovery

## Slide 7: Consideration on STA Side
We do not see too much value for STA to suggest channel
  Most of the considerations are on the AP side
  AP may see tons of suggestions and still needs to do final decision based on its constraints
We recognize that STA may have specific band capability
  STA’s WURx may only be able to operate in 5 GHz band or 2.4 GHz band
    Note that WURx for 2.4 GHz only operation may cost less
  STA can simply announce its band capability if any, and AP can do the final decision during negotiation.

## Slide 8: Conclusion
We propose that AP decides the WUR operating channel
  WUR can still be done if PCR is in a DFS channel
  AP can use 2.4 GHz band for WUR operation if PCR operates in 5 GHz band, and AP is dual-band concurrent
  AP can reject WUR request for whatever reason including not support channel switch
  Consideration for future extension like discovery application or multi-user transmission can be accommodated it these concepts are agreed
  STA can announce band capability if support for 2.4 GHz band and 5 GHz band is not mandatory

## Slide 9: Straw Poll 1
Do you support that AP decides the WUR operating channel in the band(s) supported by the associated non-AP STA operating in WUR Mode?

## Slide 10: Motion
Move the following to the 11ba SFD:
AP decides the WUR operating channel in the band(s) supported by the associated non-AP STA operating in WUR Mode

## Slide 11: Reference
[1] 11-17-0377-00-00ba False Radar Pulse Detection on WUR Signal
[2] 11-17-0380-00-00ba WUR channel switch
[3] 11-17-0031-00-00ba Channel issue in WUR
[4] 11-17-0432-00-00ba Receiver Architecture, Operational Channels, Power Consumption and Frequency Offset for 11ba
[5] 11-17-0028-00-00ba On Waking-Up Multiple WUR Stations
[6] 11-17-0697-00-00ba Multi Sub-band Scheduling
[7] 11-17-0990-02-00ba WUR Data Rates
[8] 11-17-0068-00-00ba AP Discovery Discussion
[9] 11-17-0042-00-00ba Power Efficient WUR AP Discovery Follow Up