## Slide 1: TWT SP initiation and termination and legacy PS
Date: 2017-09-01
Authors:

## Slide 2: Abstract
This submission is related to CID5958 and CID5971. CIDs and resolutions are provided in submission 11-17-1337r0.
This submission studies the TWT SP initiation and TWT SP termination when a TWT SPs ongoing, an U-APSD SP is ongoing or a STA has transmitted PS_Poll frame.
Target is to ensure high throughput and efficient power save for 802.11ax power saving STAs.

## Slide 3: Legacy Power save
Legacy power save mechanisms operate in parallel with TWT mechanisms
  A non-AP STA may transmit a frame which Power Management field in the MAC headers indicates whether the STA operates in active mode or in power save mode
  A non-AP STA may transmit an APSD trigger or PS-Poll frame

## Slide 4: Multiple TWT agreements
A TWT requesting STA may have multiple TWT agreements and each agreement defines a schedule for TWT SPs
  A TWT SP may start when other SP is ongoing
  A TWT SP may end when other SP is ongoing
Broadcast TWT and individual TWT may be ongoing at the same time

## Slide 5: Discussed issues in the presentation
In annex of the submission all combinations of the service periods and PS_Poll frame transmissions are shown
The analysis found two issues:
  Issue 1, Announced TWT SP initiation
  Issue 2, TWT SP termination signaling

## Slide 6: Issue 1, Announced TWT SP initiation
  The announced TWT SP initiation is not clearly specified:
  Currently, in announced TWT SP a TWT responding STA may transmit data to the TWT requesting STA if it receives a PS_Poll frame or an APSD trigger frame during the announced TWT SP
  It is unclear whether an ongoing SP or a PS_Poll frame transmitted before the announced TWT SP allows the TWT responder to transmit data in announced TWT SP

## Slide 7: Issue 1, Proposal
A TWT responding STA that receives a PS-Poll frame or an APSD trigger frame from a TWT requesting STA in PS mode during an announced TWT SP, has other SP ongoing with the requesting STA in PS mode, or the STA has transmitted a PS_Poll frame and not received DL MPDU within the beacon interval shall follow the rules defined in 11.2.3.6 (AP operation during the CP)
The normative text is provided in submission 11-17-1337r0

## Slide 8: Issue 2, SP termination signaling
In some TWT SP combinations, the TWT SP termination does not allow the STA to return doze:
  If U-APSD SP termination is needed, the AP needs to send a frame with EOSP field set to 1
  A PS_Poll may need a DL frame transmission
TWT SP may be terminated with:
  Transmission of a frame with EOSP =1or More Data=0, if the frame does not have EOSP
  Transmission of an EOSP=1 or More Data=0 in a ACK or BA frame
  Transmission of Cascade Indication=0 and no addressed RU in Trigger frame
  If AP has transmitted no frames, the expiration of the Nominal Minimum Wakeup Time of the TWT SP,

## Slide 9: Issue 2, Proposal
Proposal: For simplicity a STA should be allowed to return doze after all TWT SPs are terminated
  This means that AP does not send pending DL data frame for the received PS-Poll frame
  The AP terminates also the possible ongoing U-APSD SP when the TWT SP is terminated. No need to send a separate frame with EOSP=1 for the U-ASPD SP
Only the termination of TWT SPs is clarified, no change to legacy STAs U-APSD SP termination or response to PS-Poll
The normative text is provided in submission 11-17-1337r0

## Slide 10: Issue 2, Advantages of proposal
There are advantages to terminate all SPs and pending PS_Poll data transmissions with TWT signaling:
  The TWT requesting STA and TWT responding STA do not need to keep a record which frame it should receive/transmit in order to allow the TWT requesting STA to return doze
  The synchronization requirements, i.e. to know whether the frame was transmitted during Nominal Minimum Wake Duration is relaxed. The operation expected operation does not depend on the time when the frame was received
  Complicated error situations due to transmission errors, e.g. a non-AP STA expects a response from the AP, while the AP assumes that it has already terminated the SP, are mitigated
  The signaling overhead may be reduced

## Slide 11: Summary
The submission studies simultaneously ongoing SPs
The following proposals are made to improve system throughput and power save efficiency:
  In announced TWT SP, the TWT responding STA may to immediately transmit data to the TWT requesting STA in PS mode without receiving PS-Poll or APSD trigger, if it knows that the TWT requesting STA is awake
  The termination of the last TWT SP allows the TWT requesting STA in PS mode to go to doze
Submission 11-1337r0 defines the resolutions to CID5859 and CID 5971 and proposed normative text

## Slide 12: Annex, Listing different service period start and termination cases
  In the SP initiation the special focus is set whether the TWT responding STA is allowed to send data
  In the SP termination the special focus is set to describe whether early TWT SP termination terminates all ongoing SPs are

## Slide 13
Ongoing SP or received frame | Starting new SP or received frame | How many SPs are ongoing after the new SP starts? Rules for TWT responding STA? | How long the TWT responding STA may transmit data? | Does early TWT SP termination allow TWT requesting STA to go to Doze?
Announced , APSD trigger or PS_Poll not transmitted | Announced | The TWT Responding STA shall get a PS-Poll or an APSD Trigger before it may transmit DL frames. | If APSD or PS_poll is received, DL data may be sent until both TWT SPs are terminated. If no early termination until the end of the last SP. | Yes
Announced , APSD trigger or PS_Poll not transmitted | Unannounced | The TWT Responding STA may send DL data when Unannounced TWT SP starts. | Until the announced and Unannounced TWT SPs are terminated. If no early termination until the end of the last SPs. | Yes
Announced , APSD trigger or PS_Poll not transmitted | U-APSD trigger frame received | Only the announced TWT SP is started. TWT responding STA may send data when U-APSD trigger is received. | Until the Announced TWT SP is terminated. | Yes
Announced , APSD trigger or PS_Poll not transmitted | PS_Poll frame received | Only the announced TWT SP is started. TWT responding STA may send data when PS_Poll is received. | Until the Announced TWT SP is terminated. | Yes
Announced , APSD trigger or PS_Poll is transmitted | Announced | Two announced TWT SPs are ongoing. It is unclear should a STA transmit a PS_Poll or APSD trigger to receive DL traffic when the second announced TWT starts. | Until both announced TWT SPs are terminated. If no early termination until the end of the last SP. | Yes
Announced , APSD trigger or PS_Poll is transmitted | Unannounced | The announced and unannounced TWT SPs are ongoing. | Until both TWT SPs are terminated. If no early termination until the end of the last SP. | Yes
Announced , APSD trigger or PS_Poll is transmitted | U-APSD trigger frame received | The announced TWT SP and U-APSD SP are ongoing | Until both TWT and U-APSD SPs are terminated. | No, U-APSD SP termination is needed.
Announced , APSD trigger or PS_Poll is transmitted | PS_Poll frame received | The announced TWT SP is ongoing and the AP transmits at least one DL frame | Until the announced TWT SP is terminated and at least one DL frame is transmitted. | No, a DL frame transmission is needed.

## Slide 14
Ongoing SP or received frame | Starting new SP or received frame | How many SPs are ongoing after the new SP starts? Rules for TWT responding STA? | How long the TWT responding STA may transmit data? | Does early TWT SP termination allow TWT requesting STA to go to Doze?
Unannounced | Announced | The unannounced and announced TWT SPs are ongoing. It is unclear should a TWT requesting STA transmit a PS_Poll or APSD trigger to receive DL traffic when the announced TWT starts. | Until both TWT SPs are terminated. If no early termination until the end of the last SP. | Yes
Unannounced | Unannounced | Two unannounced TWT SPs are ongoing. | Until both TWT SPs are terminated. If no early termination until the end of the last SP. | Yes
Unannounced | U-APSD trigger frame received | The unannounced TWT SP and U-APSD SP are ongoing. | Until the TWT and U-APSD SP are terminated. | No, U-APSD SP termination is needed.
Unannounced | PS_Poll frame received | The unannounced TWT SP is ongoing and the AP transmits at least one DL frame. | Until the TWT SP is terminated and at least one DL frame is transmitted. | No, a DL frame transmission is needed.
U-APSD | Announced | U-APSD SP and announced TWT SP are ongoing. It is unclear should a TWT requesting STA transmit a PS_Poll or APSD trigger to receive DL traffic when the announced TWT starts. | Until the TWT and U-APSD SP are terminated. | No, U-APSD SP termination is needed.
U-APSD | Unannounced | The unannounced TWT SP and U-APSD SP are ongoing. | Until the TWT and U-APSD SP are terminated. | No, U-APSD SP termination is needed.
U-APSD | U-APSD trigger frame received | Not possible. Only a single U-APSD SP is ongoing at a time. | Until the U-APSD SP is terminated. | No, U-APSD SP termination is needed.
U-APSD | PS_Poll frame received | U-APSD SP is ongoing and depending on U-APSD configuration a frame may need to be transmitted. | Until the U-APSD SP is terminated and the configured DL frame is transmitted. | No, U-APSD SP termination is needed. Depending on U-APSD configuration a DL frame may be needed.

## Slide 15
Ongoing SP or received frame | Starting new SP or received frame | How many SPs are ongoing after the new SP starts? Rules for TWT responding STA? | How long the TWT responding STA may transmit data? | Does early TWT SP termination allow TWT requesting STA to go to Doze?
PS_Poll from TWT Requesting STA received by TWT responding STA | Announced | Announced TWT SP are ongoing. It is unclear should a STA transmit a PS_Poll or APSD trigger to receive DL traffic when the announced TWT starts. Also may AP transmit a single frame or for the whole duration of the announced TWT SP. | Until announced TWT SP is terminated or a single DL MPDU is transmitted . | No, a DL frame transmission is needed.
PS_Poll from TWT Requesting STA received by TWT responding STA | Unannounced | Unannounced TWT SP is ongoing | Until unannounced TWT SP is terminated or a single DL MPDU is transmitted . | No, a DL frame transmission is needed.
PS_Poll from TWT Requesting STA received by TWT responding STA | U-APSD trigger frame received | U-APSD SP ongoing | Until U-APSD SP is terminated and the configured DL frame is transmitted. | No, U-APSD SP termination is needed. Depending on APSD configuration a DL frame may be needed.
PS_Poll from TWT Requesting STA received by TWT responding STA | PS_Poll frame received | A DL frame needs to be transmitted. | Until one DL frame is transmitted. | No, a DL frame transmission is needed.