## Slide 1: Packet Format of 11ba
Date: 2017-08-10
Authors:
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek | 2840 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | 

## Slide 2: Format of wake-up radio (WUR) packet
A WUR packet is a wake-up signal that can be received and resolved by wake-up receivers of WUR stations. A typical format of a WUR packet is shown as the following figure.
  Preamble: contains on-off keying sequences for automatic gain control and frequency/timing synchronization. The timing synchronization can be done through a signature sequence matching.
  Control Information contains the identification of AP (such as, BSS color), the identification of the target station/group (such as assigned ID for the station/group) and wake-up control field.
Signature Sequence
Information

## Slide 3
Preamble Design of WUR packet
The preamble serves a few purposes:
  Timing Synchronization:
    To obtain the correct sampling time to minimize the non-coherent detection error.
  Packet detection:
    To identify the WUR packet is received.
  Boundary detection
    To detect the boundary of preamble and control information
  Rate indication: information can be transmit using different data rates.
  Timing Synchronization, Packet detection, Boundary detection and rate indication can be realized by insert signature sequences into the preamble.

## Slide 4: WUR signature sequence design
Since the control information can be transmit with different data rate for different coverage, WUR signature sequence is used also as an indicator of the data rate of WUR packet.
  Data rate is PHY information, it is better to carries in the preamble instaed of information fields.
  WUR receiver needs to know the data rate for detection and decoding.
  Introduce two signature sequences and each signature sequence indicates one specific data rate.
    We prefer two data rates:
      11ba serves a simple switch. No need to make it complicated.
      The simpler, the easier for the market taking off.
  Avoid changing the rate in the information field :
    All the mandate fields can be regarded as the header;
    Simple design: no need to change the rate for some fields because all the mandate fields are equally important. Any mandatory field error cause the failure of wake up.

## Slide 5: Summary
We prefer to use the signature sequences to indicate rate.