## Slide 1: 11ba PHY Frame Format Proposal
Date: 2017-09-11
Authors:

## Slide 2: Overview
Different functions may create different levels of requirements on 11ba PHY design.
The original goal of 11ba PHY is simply and low power—don’t have to overload all the functions into a single PHY format
Categorize 11ba PHY frame formats for two data rate modes.
  The low data rate may only apply the most basic operations with short packet length.
  Simplify the implementation complexity.
  Enabling a staging HW/SW product enabling process, e.g. to start from the simple and basic operations and validation the power consumption, etc.

## Slide 3: Proposed PHY Format
I. Low Data Rate
LSTF
LLTF
LSIG
Data Field
BPSK
Symbol
SYNC-1
II. High Data Rate
LSTF
LLTF
LSIG
Data Field
BPSK
Symbol
SYNC-2
250Kbps, all possible functions
(frame types)
62.5Kbps, only the most
fundamental functions (frame types)

## Slide 4: Low Data Rate Mode
Data field using only 62.5Kbps
Only allows the most basic frame type(s) with the shortest possible lengths, e.g. simple unicast/broadcast wake-up, WUR beacon (short).
  Every bit counts for 16us duration, therefore cannot afford frame types with large number of bits.
  Need frame type indication if more than one types are allowed in this mode
  (TBD) Possible to define fixed length in Data field (unify the length of different frame types: WUR beacon, and simple wake-up)

## Slide 5: High Data Rate Mode
Data field using only 250Kbps.
Have a Frame Type indication at the beginning of Data field to signal ALL the allowed Frame Types.
  Include more advanced (non basic) features.
  (TBD) WUR Beacon may only use the low data rate, therefore may be excluded from the high data rate.

## Slide 6: Straw Poll 1
Do you agree that 11ba has two data rates: 62.5Kbps and 250Kbps?
  No other rate(s) are defined

## Slide 7: Straw Poll 2
Do you agree to use two different WUR SYNC sequences for different data rates, as shown in slide 3?
  The SYNC sequences are located after the legacy portion preamble as shown in slide 3.

## Slide 8: Straw Poll 3
Do you agree that there is no additional PHY header field inserted between the WUR SYNC field and WUR Data field, as shown in slide 3?

## Slide 9: Straw Poll 4
Do you agree that:
  The low data rate mode only carries the most basic WUR functions (frame types), i.e. not necessarily all the 11ba functions.
  The high data rate mode contains all possible functions (frame types).
    (TBD) WUR beacon may be excluded from high data rate.

## Slide 10: Straw Poll 5
Do you agree to design the WUR dual SYNC sequences with different durations?
  The SYNC sequence for the Low Data Rate mode is with longer duration than that for the High Data Rate mode.

## Slide 11: Motion
Move to add to the TGba SFD:
  11ba has only two data rates: 62.5Kbps and 250Kbps.
  Mover: Hongyuan Zhang
  Seconder: Jianhan Liu