## Slide 1: Higher Data Rates
Date: 2017-09-11
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
We agreed to use the data rates of 62.5Kbps and 250Kbps
In this contribution, we further investigate benefits of using higher data rates such as 500Kbps and 1Mbps
To this end, based on the PER performance, link budget, goodput and overhead are examined for the TGnD channel

## Slide 3: PER performance

## Slide 4: Link Budget
Target PER : 10%
Supportable distance [m]
 | 2.4GHz | 5GHz
62.5 | <= 92 | <= 60
250 | <= 72 | <= 46
500 | <= 56 | <= 37
1000 | <= 44 | <= 28

## Slide 5: Goodput
Case 1 : two data rates used
(62.5, 250)
Case 2 : three data rates used
(62.5, 250, 500)
Case 3 : three data rates used
(62.5, 250, 1000)
Case 4 : four data rates used
(62.5, 250, 500, 1000)
Select a data rate which has the largest goodput with PER <= 10%
Goodput = (1-PER)*data rate
In range 1, all cases have the same goodput
In range 2, case 2 and 4 have the maximum goodput
In range 3, case 3 and 4 have the maximum goodput
92m 72m 56m 44m for 2.4GHz
60m 46m 37m 28m for 5GHz
Range 1
Range 2
Range 3

## Slide 6: Overhead
Case 1 : two data rates used
(62.5, 250)
Case 2 : three data rates used
(62.5, 250, 500)
Case 3 : three data rates used
(62.5, 250, 1000)
Case 4 : four data rates used
(62.5, 250, 500, 1000)
Assume 48bits for the WUR payload
Plot only the payload length
Consider only PER <= 10% (supportable at SNR >= -2.5dB)
In range 1, all cases have the same overhead
In range 2, case 2 and 4 have the minimum overhead
In range 3, case 3 and 4 have the minimum overhead
92m 72m 56m 44m for 2.4GHz
60m 46m 37m 28m for 5GHz
Range 1
Range 2
Range 3

## Slide 7: Conclusion
If 11ba supports only two data rates, many benefits will be lost
  WUR packet sent to STAs which are located near the AP (within about 56m/37m from the AP in 2.4GHz/5GHz) or have a good link quality (received SNR higher than about 5dB) should be also computed by using 62.5Kbps or 250Kbps although its throughput and overhead can be further enhanced by applying a higher data rate.
In other words, by allowing 11ba to support higher data rates, we can significantly increase the throughput and reduce the overhead which results in low power consumption
  Note that in indoor environment, high MCS levels are selected with high probability for the main radio system [2] that implies the received SNR can be better than 20dB (or even 30dB) as shown in Appendix C
  Thus, we can infer that it is highly probable that WUR STA has a received SNR (or a received SINR when considering some interference such as OBSS interference) higher than 5dB in spite of the maximum received SNR difference of 15dB between the main radio and WUR due to the noise figure and the power regulation in the 5GHz band

## Slide 8: Straw poll #1
Do you agree to add the following to the 11ba SFD?
  IEEE 802.11ba supports data rates higher than 250Kbps?
Y/N/A :

## Slide 9: Straw poll #2
Do you agree to add the following to the 11ba SFD?
  IEEE 802.11ba supports the data rate of 500Kbps
Y/N/A :

## Slide 10: Straw poll #3
Do you agree to add the following to the 11ba SFD?
  IEEE 802.11ba supports the data rate of 1Mbps
Y/N/A :

## Slide 11: References
[1] IEEE 802.11-14/882r4 IEEE 802.11ax channel model document
[2] IEEE 802.11-15/1070r3 1024 QAM proposal

## Slide 12: Appendix

## Slide 13: Appendix A - Simulation Assumptions
48 symbols in payload
CFO [3], Phase noise [4] applied
No timing error
Butterworth filter
  2.5MHz cut off frequency, second order
20MHz sampling rate
TGnD and UMi NLoS channels in 2.4GHz and 5GHz
SNR defined in 20MHz

## Slide 14: Appendix B - Link Budget Setting
Received SNR
Rx_SNR = Tx_Pwr - PL - 3*Shadowing - NF - N0
Transmit power : Tx_Pwr = 20dBm
Noise figure : NF = 15dBm
Noise floor : N0 = -174dBm + 10log10BW
Bandwidth : BW = 20MHz
Path loss: PL in [1]
No interference
No penetration loss

## Slide 15: Appendix C – PER Performance for 11ax