## Slide 1: Discussion on WUR mode
Date: 2017-09-11
Authors:

## Slide 2: Introduction
Since the July F2F, we have had a number of discussions on WUR mode [1-5]
In this contribution, we discuss issues regarding WUR mode that came up at the last F2F and ARC SC telecon[6]
  Clarifications on WUR mode definition
  WUR mode coexistence with power management mode
  Further consideration on WUR mode

## Slide 3: Clarification on WUR mode definition
In the passed motion[1]:
  If a non-AP STA is in WUR mode, then
    the non-AP STA’s WURx follows the duty cycle schedule (including WURx always on) agreed between AP and non-AP STA if the non-AP STA is in the doze state
  In other words, when STA is in WUR mode:
    The STA uses WURx when it’s in the doze state
    But, if the STA is in the awake state, the STA doesn’t have to use WURx
WUR mode is a PCR MAC protocol
  If a STA indicates that it uses WUR mode, the AP must transmit WUP when the STA is supposed to be in the doze state
  Enabling/disabling WUR mode is triggered by PCR MAC
  Signaled by an explicit PCR frame

## Slide 4: WUR mode and power management mode
Can a STA use WUR mode and power save mode simultaneously?: Yes
  Both WUR mode and power management mode are managed by the PCR MAC
  WUR mode is independent from Power Management modes
    Different signaling is used for each mode
    Each mode has different purpose
This is already aligned with the motion text
  If a non-AP STA is in WUR mode, then
    the non-AP STA’s WURx follows the duty cycle schedule (including WURx always on) agreed between AP and non-AP STA if the non-AP STA is in the doze state
  STA enters the doze state only when it is using power save mode
Does WUR mode require a specific power management mode?: No
  A STA may enter WUR mode in active mode, but the STA simply won’t use WURx as it has to be in the awake state

## Slide 5: WUR operation example
AP
STA
WUR mode request
(Enter)
Ack
WUR mode
PM mode
Data
PM:1
Ack
Active
Off
On
PS: Doze
WUP
trigger frame
PM:1
Ack
WUR mode request
(Exit)
Ack
PS: Awake
Off
PS: Doze
PCR
WURx
PCR

## Slide 6: Further consideration on WUR mode
According to the passed motion text, a STA in WUR mode may suspend any negotiated SPs (e.g., TWT, WNM sleep)
  Allowing PCR to sleep much longer
There is another requirement that might prevent PCR to take long-term sleep
  11.2.3 Power management in a non-DMG infrastructure network
    A STA operating in PS mode that is not in WNM sleep mode shall periodically listen for Beacon frames
  As such periodic wake-up events can be replaced by WUP transmission, we can further relieve this requirement
Proposal: the non-AP STA may not listen for Beacon frames when it is in PS mode

## Slide 7: Conclusion
We have provided the clarification on WUR mode
  Using WUR mode, a STA may change its operating radio depending on its power state
    The AP should transmit WUP when a STA using WUR mode is supposed to be in the doze state
We have proposed that
  A STA in WUR mode may not listen for Beacon frames if the STA is in PS mode
    In order to allow the STA in WUR mode to take longer sleep

## Slide 8: Strawpoll
Do you agree to add the following to 11ba SFD:
  If a non-AP STA is in WUR mode, then
    the non-AP STA’s WURx follows the duty cycle schedule (including WURx always on) agreed between AP and non-AP STA if the non-AP STA is in the doze state
    the non-AP STA may not listen for Beacon frames if the non-AP STA is in PS mode
    the existing negotiated service period between AP and non-AP STA for the non-AP STA’s PCR schedule (e.g. TWT, schedule for WNM Sleep Mode) is suspended
      STA is not required to wake up during the service period if the service period is suspended
      The parameters of the negotiated service period for the non-AP STA’s PCR schedule is still saved by the AP and non-AP STA when the negotiated service period is suspended

## Slide 9: Reference
[1] https://mentor.ieee.org/802.11/dcn/17/11-17-0972-02-00ba-definition-of-wur-mode.pptx
[2] https://mentor.ieee.org/802.11/dcn/17/11-17-1000-01-00ba-wur-coexistence-with-existing-power-save-mode.pptx
[3] https://mentor.ieee.org/802.11/dcn/17/11-17-0992-01-00ba-power-save-mode-for-wur.pptx
[4] https://mentor.ieee.org/802.11/dcn/17/11-17-0984-01-00ba-wur-mode-transition-mechanism.pptx
[5] https://mentor.ieee.org/802.11/dcn/17/11-17-0953-00-00ba-wur-mode-discussion.pptx
[6] https://mentor.ieee.org/802.11/dcn/17/11-17-1246-01-0arc-11ba-arch-discussion-part-2.pptx