## Slide 1: Duty cycle mode STA’s PS follow-up
Date: 2017-09-10
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Taewon Song |  |  |  | taewon.song@lge.com

## Slide 2: Recap (17/0978r1) [1]
Duty cycle mode in 11ba SFD [2]
  STAs in duty cycle mode can receive WUR packet from AP during their On-durations
WUR STA receiving Wake-Up frame turns on its PCR to receive WLAN frame
AP can also send Broadcast Wake-Up Frame(B-WUF) to STAs during their On-Durations for the STAs to receive Beacon for the system parameter update
If STAs in duty cycle mode wake up right after receiving B-WUF, the STAs will waste their power unnecessarily before Beacon
On
On
On
On
B
AP
S1
S2
B
B
B
Broadcast
Wake-up frame
On
On duration in WUR duty cycle
B
WLAN Beacon
Awake state in PCR
Unnecessary
Power consumption
….
….
….

## Slide 3: System parameter update (1/4)
A value of Type field of WUR frame indicates the Broadcast WUR frame for Beacon reception
WUR STA receiving the B-WUF for Beacon reception may enter the doze state until the end of the next TBTT
  That is, the STA may wake up at the next TBTT and attempt to receive the Beacon
The STA may return to the WUR immediately after receiving Beacon
On
On
On
On
B
AP
S1
S2
B
B
B
B-WUF for Beacon reception
On
On duration in WUR duty cycle
B
WLAN Beacon
Awake state in PCR
Doze state

## Slide 4: System parameter update (2/4)
AP may send the same B-WUF indicating Beacon reception during other STAs’ On-Durations and send the same B-WUF several times during a period for reliability of the B-WUF
  In this case, the always-on WUR STAs will receive the same B-WUF several times and wake up several times unnecessarily
AP need to include in B-WUF the information to avoid the unnecessary wake-up of the WUR STAs by receiving the same B-WUF

## Slide 5: System parameter update (3/4)
Option 1: AP includes the sequence number(SN) field in B-WUF
Whenever AP send a B-WUF which is different from the previously sent B-WUF, it increases the sequence number by 1
When a WUR STA receives a B-WUF including the SN with the same value as the value of SN included in the previously received B-WUF, the STA can ignore the currently received B-WUF

## Slide 6: System parameter update (4/4)
Option 2: AP includes the Check Beacon field in B-WUF
  A value of Check Beacon field is increased when a critical update occurs to any of the element inside Beacon according to the rule defined in 11.2.3.17 TIM Broadcast [3]
WUR STA attempts to receive the next Beacon frame when it receives Check Beacon field that contains a value that is different from the previously received Check Beacon field
WUR STA can ignore a received B-WUF if the B-WUF includes the Check Beacon field with the same value as the value of Check Beacon field included in the previously received B-WUF

## Slide 7: Conclusion
To avoid the unnecessary wake-up of WUR STA by receiving the B-WUF, the AP should include the information for WUR STA to avoid the unnecessary wake-up when the STA receives the B-WUF
Option 1: AP includes the Sequence Number field in B-WUF
Option 2: AP includes the Check Beacon field in B-WUF

## Slide 8: References
[1] 11-17-0978-02-00ba, Power saving operation for WUR STAs in duty cycle mode
[2] 11-17-0575-04-00ba-spec-framework
[3] 802.11-2016

## Slide 9: Straw Poll 1
Do you agree the following?
  11ba shall define a mechanism for a WUR STA to avoid unnecessary wake-up after receiving duplicate broadcast wake-up frames sent by an AP
    The detailed information included in the broadcast wake-up frame (e.g., check beacon or sequence number of the WUR frame) is TBD.

## Slide 10: Straw Poll 2
Which option do you prefer as the information included in the broadcast wake-up packet (The size of the information is TBD)?
  Option 1: Sequence number of the packet
  Option 2: Check Beacon

## Slide 11: Straw Poll 3
Do you agree the following?
  For option 1: A sequence number (SN) is included in a broadcast wake-up frame
    A value of SN field is increased when a broadcast wake-up frame is different from the previously sent broadcast wake-up frame
  For option 2:A Check Beacon field is included in a broadcast wake-up frame for system parameter update of WUR STAs
    A value of Check Beacon field is increased when a critical update occurs to any of the element inside Beacon according to the rule defined in 11.2.3.17 TIM Broadcast [2]
One of both options will be removed by the result of SP2

## Slide 12: Straw Poll 4
Do you agree the following?
  For option 1: When a WUR STA receives a B-WUF including the SN value that is different from the previously received SN, the STA can ignore the currently received B-WUF
  For option 2: WUR STA attempts to receive the next WLAN Beacon frame when it receives Check Beacon field that contains a value that is different from the previously received Check Beacon field. In this case, a WUR STA may enter the doze state until the next TBTT
One of both options will be removed by the result of SP2