## Slide 1: PAR Verification Multiple BSS Simulation Follow-up
Date: 2017-09-10
Authors:

## Slide 2: Comment of 11ax D1.0
CID | Commenter | P.L | Clause | Comment | Proposed Change
5011 | Carol Ansley |  |  | I am concerned that the current draft has not been shown to provide the level of performance improvement specified in the PAR. While a lot of work has gone into this draft, it seems premature to stop work on the technical aspects if there are any other improvements that could be added to help this amendment reach its avowed goal. | 

## Slide 3: Summary
In this presentation, throughputs of 11ac and 11ax in mixed UL/DL multiple BSS scenarios (3 BSSs) are presented
  3 uplinks (3u)
  2 uplinks and 1 downlink (2u1d)
  1 uplink and 2 downlinks (1u2d)
Observations
  11ax has better system throughputs and 5% percentile throughputs than 11ac in all 3 scenarios
  In both 11ac and 11ax, the uplink BSS(s) have higher system throughput than the downlink BSS(s)
  As the number of stations increases, in 11ac, downlink throughput ratio of the total throughput decreases dramatically, but in 11ax, the downlink throughput is more stable

## Slide 4: Topology
Open area with 3 APs
The distance between any two APs is 30 meters
AP is at the center of 15-meter radius circle
STAs are randomly placed within the circle
Three different scales
  13, 26, 52 STAs for each BSS
  39, 78, 156 total STAs

## Slide 5: Simulation Parameters
PHY parameters | 
Center frequency and BW | Operation Channel: 5GHz with 80 MHz channel
MCS | MCS5
GI | Long GI
STA TX power | 15 dBm
AP TX Power | 20 dBm
AP #of TX antennas | 1
AP #of RX antennas | 1
STA #of TX antennas | 1
STA #of RX antennas | 1
MAC parameters | 
Access protocol parameters | EDCA with default parameters according to the access category
UDP packet size | 100 bytes
Aggregation | 64 MPDU per AMPDU
Max # of retries | 10
RTS/CTS | enabled or disabled
Association | All STAs are associated to the designated AP

## Slide 6: Simulation Setting
STA Access category (AC) setting in each BSS
  1/3 STAs are AC_VO (7, 15)
  1/3 STAs are AC_VI (15, 31)
  1/3 STAs are AC_BE (31, 1023)
OFDMA scheduling
  For each available RU, AP selects an associated STA randomly
For the BSS with UL traffic
  STAs send 100 bytes UDP traffic to AP every 0.1ms
  HE STAs are waiting for trigger frames to transmit UL data
For the BSS with DL traffic
  AP sends 100 bytes UDP traffic to each station every 0.1ms
  STAs only send acknowledgement to AP

## Slide 7: System Throughputs (Mbps) RTS/CTS Enabled
39 STAs
78 STAs
156 STAs
 | 1u2d | 2u1d | 3u
11ac | 78.85 | 72.60 | 49.47
11ax | 102.36 | 104.95 | 112.14
Gain | 29.82% | 44.56% | 126.67%
 | 1u2d | 2u1d | 3u
11ac | 73.45 | 85.59 | 58.71
11ax | 95.52 | 103.23 | 116.72
Gain | 30.05% | 20.61% | 98.80%
 | 1u2d | 2u1d | 3u
11ac | 69.94 | 93.06 | 69.96
11ax | 85.75 | 101.58 | 120.58
Gain | 22.61% | 9.15% | 72.34%
11ax has ~20% to ~120% system T-put gain over 11ac

## Slide 8: Downlink Throughputs (Mbps) RTS/CTS Enabled
39 STAs
78 STAs
156 STAs
 | 1u2d | 2u1d
11ac | 17.65 | 3.15
11ax | 60.16 | 24.42
Gain | 240.89% | 675.28%
 | 1u2d | 2u1d
11ac | 3.15 | 0.95
11ax | 51.33 | 22.62
Gain | 1527.34% | 2286.63%
 | 1u2d | 2u1d
11ac | 2.38 | 0.38
11ax | 41.75 | 18.05
Gain | 1651.64% | 4639.08%
Extremely low DL T-put
11ac AP has to contend
with many many UL
11ac STAs

## Slide 9: Uplink Throughputs (Mbps) RTS/CTS Enabled
39 STAs
78 STAs
156 STAs
 | 1u2d | 2u1d | 3u
11ac | 61.20 | 69.45 | 49.47
11ax | 42.19 | 80.53 | 112.14
Gain | -31.05% | 15.96% | 126.67%
 | 1u2d | 2u1d | 3u
11ac | 70.30 | 84.64 | 58.71
11ax | 44.19 | 80.61 | 116.72
Gain | -37.14% | -4.76% | 98.80%
 | 1u2d | 2u1d | 3u
11ac | 67.56 | 92.68 | 69.96
11ax | 44.00 | 83.53 | 120.58
Gain | -34.88% | -9.87% | 72.34%
11ax loses in UL T-put but gets balanced DL/UL T-put

## Slide 10: Throughput vs. Station Position (11ac)
Throughputs are dominated by some STAs
  Closer to AP
  Higher AC

## Slide 11: Throughput vs. Station Position (11ax)
Throughput among stations are more balanced than 11ac
  Stations closer to AP have higher throughputs
  UL BSSs have higher system throughputs than DL BSS

## Slide 12: Uplink and Downlink Throughputs
For 11ac
  UL throughputs are much higher than downlink throughput
    AP has to contend with UL stations in nearby BSS
    As the number of stations increases, AP has to contend with more stations
For 11ax
  UL throughput and DL throughput are more balanced
    UL traffic is triggered by AP
    Contention happens among APs
  UL Throughput is slightly higher than DL throughput
    Based on the spec.[1], the contention window will not increase when there is no response to trigger frame
    Sending trigger frame has lower backoff time and thus has higher chance to access the channel

## Slide 13: Uplink and Downlink Ratio with different AC of AP
2u1d case
For 11ac
  AP with higher priority AC has higher DL ratio to whole system throughput
  If AP’s AC is BE and there are many UL STAs, the DL throughput is almost gone
For 11ax
  Balanced throughputs in all cases
  Higher Priority AC, lower downlink ratio
    Collision among APs happens more frequently
Chart: Uplink and Downlink Ratio (39 STAs)
| 11ac (BE) | 11ac (VI) | 11ac (VO) | 11ax (BE) | 11ax (VI) | 11ax (VO)
downlink | 1.5507 | 7.5349 | 15.9461 | 27.1203 | 28.9035 | 24.2595
uplink | 61.3576 | 51.9496 | 49.3555 | 80.3491 | 79.6101 | 89.6744
Chart: Uplink and Downlink ratio (156 STAs)
| 11ac (BE) | 11ac (VI) | 11ac (VO) | 11ax (BE) | 11ax (VI) | 11ax (VO)
downlink | 0.18987 | 1.7336 | 2.9776 | 18.1827 | 16.8923 | 13.9933
uplink | 91.1456 | 89.2291 | 89.8 | 83.5264 | 92.1374 | 95.9269

## Slide 14: System Throughput vs. RTS/CTS
RTS/CTS does help improve throughput in 11ac, but does not have strong impact on throughput in 11ax
11ac 78 STAs
11ax 78 STAs
██ RTS/CTS ON
██ RTS/CTS OFF
Chart: Throughput
| 3ap-78sta-11ac-1u2d | 3ap-78sta-11ac-2u1d | 3ap-78sta-11ac-3u | 3ap-78sta-11ax-1u2d | 3ap-78sta-11ax-2u1d | 3ap-78sta-11ax-3u
RTS/CTS enabled | 73.4536 | 85.5915 | 58.7104 | 95.5232 | 103.2296 | 116.7173
RTS/CTS disabled | 24.6565 | 62.7107 | 51.5467 | 96.5971 | 104.6901 | 116.3549

## Slide 15: Data Analysis of 11ac (78 STAs, 2u1d)
Throughputs are dominated by some STAs
Similar behaviors are also observed in other 11ac scenarios
Throughputs are from some STAs
40% stations have very low throughputs

## Slide 16: Data Analysis of 11ax (78 STAs, 2u1d)
STAs have more balanced throughputs
Small gap between uplink throughputs and downlink throughputs (AP needs to contend with other UL STAs)
Downlink
Uplink
Much better 5% percentile
throughputs

## Slide 17: Discussion
System throughputs
  In 11ac, some STAs dominates the system throughputs
  In 11ac, RTS/CTS does help improve system throughputs when contention is serious
  AP’s AC makes impact on DL throughputs
5% percentile throughputs in dense environments
  Many STAs in 11ac are not able to transmit any data because they cannot access the channel
  In dense environments, 11ax is able to provide more balanced throughputs
    Contention only happens among APs
    For both UL and DL, also much better 5% percentile throughputs

## Slide 18: References
      IEEE P802.11ax/D1.4, subclause 10.22.2.2

## Slide 19: backup

## Slide 20: System Throughputs (Mbps) RTS/CTS Disabled
39 STAs
78 STAs
156 STAs
 | 1u2d | 2u1d | 3u
11ac | 44.43 | 62.27 | 50.98
11ax | 102.50 | 105.30 | 111.07
Gain | 130.70% | 69.11% | 117.88%
 | 1u2d | 2u1d | 3u
11ac | 24.66 | 62.71 | 51.55
11ax | 96.60 | 104.69 | 116.35
Gain | 291.77% | 66.94% | 125.73%
 | 1u2d | 2u1d | 3u
11ac | 71.39 | 60.57 | 48.94
11ax | 87.61 | 102.18 | 117.02
Gain | 22.72% | 68.69% | 139.13%

## Slide 21: Downlink Throughputs (Mbps) RTS/CTS Enabled
39 STAs
78 STAs
156 STAs
 | 1u2d | 2u1d
11ac | 32.01 | 5.80
11ax | 60.45 | 26.78
Gain | 88.86% | 361.51%
 | 1u2d | 2u1d
11ac | 24.64 | 1.11
11ax | 53.13 | 23.23
Gain | 115.62% | 1996.44%
 | 1u2d | 2u1d
11ac | 2.61 | 0.98
11ax | 46.44 | 19.60
Gain | 1682.76% | 1892.44%

## Slide 22: Uplink Throughputs (Mbps) RTS/CTS Disabled
39 STAs
78 STAs
156 STAs
 | 1u2d | 2u1d | 3u
11ac | 12.42 | 56.47 | 50.98
11ax | 42.05 | 78.53 | 111.07
Gain | 238.55% | 39.06% | 117.88%
 | 1u2d | 2u1d | 3u
11ac | 0.02 | 61.60 | 51.55
11ax | 43.47 | 81.46 | 116.35
Gain | 258649.21% | 32.23% | 125.73%
 | 1u2d | 2u1d | 3u
11ac | 68.78 | 59.59 | 48.94
11ax | 41.17 | 82.58 | 117.02
Gain | -40.15% | 38.58% | 139.13%
Abnormal case, under investigation

## Slide 23: Uplink and Downlink Ratio with different AC of AP
2u1d case
Chart: Uplink and Downlink Ratio (39 STAs)
| 11ac (BE) | 11ac (VI) | 11ac (VO) | 11ax (BE) | 11ax (VI) | 11ax (VO)
downlink | 1.5507 | 7.5349 | 15.9461 | 27.1203 | 28.9035 | 24.2595
uplink | 61.3576 | 51.9496 | 49.3555 | 80.3491 | 79.6101 | 89.6744
Chart: Uplink and Downlink Ratio (78 STAs)
| 11ac (BE) | 11ac (VI) | 11ac (VO) | 11ax (BE) | 11ax (VI) | 11ax (VO)
downlink | 0.28133 | 3.5341 | 7.3563 | 22.4085 | 22.0851 | 19.0456
uplink | 98.3611 | 61.9293 | 58.7779 | 82.9296 | 83.1221 | 94.3829
Chart: Uplink and Downlink ratio (156 STAs)
| 11ac (BE) | 11ac (VI) | 11ac (VO) | 11ax (BE) | 11ax (VI) | 11ax (VO)
downlink | 0.18987 | 1.7336 | 2.9776 | 18.1827 | 16.8923 | 13.9933
uplink | 91.1456 | 89.2291 | 89.8 | 83.5264 | 92.1374 | 95.9269