## Slide 1: WUR Synchronization
Date: 2017-09-11
Authors:

## Slide 2: Introduction
This submission discusses a partial timestamp field in WUR Beacon frames for a WUR synchronization

## Slide 3: WUR Synchronization
A TSF value to adjust a timer error of a WUR STA should be encoded to the partial timestamp in WUR Beacon frames [1]
In this document, ±500 PPM is assumed for a TSF timer accuracy of a WUR STA
  802.11 main radio’s TSF timer accuracy is ±100 ppm
  But, in a lower power device (e.g., NAN device), ±500 PPM could be a reasonable assumption [2]

## Slide 4: WUR Synchronization
The following table shows the number of a required bits for a partial timestamp field depending on various WUR Beacon Intervals, when 10 maximum missed WUR Beacon is supported
WUR Beacon Interval (s) | TSF Timer Error (ms) | Partial Timestamp Bits (1us unit)
1 | 10 x ±0.5 | 14
2 | 10 x ±1 | 15
4 | 10 x ±2 | 16
8 | 10 x ±4 | 17
10 | 10 x ±5 | 17

## Slide 5: WUR Synchronization
WUR Beacon Interval of 1 s is usually recommended
However, in an aspect of a protocol design, the supported WUR Beacon Interval in a WUR BSS should consider a maximum capability, even though some parameter is not frequently used

## Slide 6: WUR Synchronization
But, if we optimize the protocol design (in a context of power consumption) for a WUR Beacon Interval of 1 s, 8 us unit can be a best option
  48 us WUR Rx power consumption is decreased by removing 3 bits (occupy the 12 symbol at 62.5 Kbps data rate) from the partial timestamp field
  36 us WUR Rx Power consumption is increased by waking 4us earlier for compensating the TSF timer error

## Slide 7: WUR Synchronization
With 8 us unit, the following table shows the number of a required bits for a partial timestamp field depending on various WUR Beacon Interval, when 10 maximum missed WUR Beacons is supported
WUR Beacon Interval (s) | TSF Timer Error (ms) | Partial Timestamp Bits (8 us unit)
1 | 10 x ±0.5 | 11
2 | 10 x ±1 | 12
4 | 10 x ±2 | 13
8 | 10 x ±4 | 14
10 | 10 x ±5 | 14

## Slide 8: Conclusion
Considering an overhead of a WUR Beacon frame, it seems that a partial timestamp field between 12 and 14 bits is reasonable
Our preference is 12 bits partial timestamp with 8 us unit
The partial timestamp in WUR Beacon is set to the AP’s TSF[3:14] of the AP’s TSF value rounded to the nearest 16 integer

## Slide 9: References
[1] https://mentor.ieee.org/802.11/dcn/17/11-17-0575-03-00ba-spec-framework.docx [2] “Enabling always on service discovery: Wifi neighbor awareness networking”, IEEE Wireless Communications ( Volume: 22, Issue: 2, April 2015 )

## Slide 10: SP1
Do you support that a partial timestamp has 12 bits with 8 us unit?