## Slide 1
WUP CCA Problem
Date: 2017-09-10
Authors:

## Slide 2: Introduction
WUP consists of full-bandwidth legacy preamble part and narrow band 11ba specific part[1]
  R.3.1.A: A 20MHz non-HT preamble is prepended in any WUR PPDU, including L-STF, L-LTF and L-SIG fields. A 20MHz OFDM symbol, with tone spacing 312.5 KHz and BPSK, and duration of 4 us, is present immediately after the L-SIG field and right before the narrow band portion of any WUR PPDU.
  We have determined narrow-band tone population for unicast WUP in the last meeting
WUR payload uses OOK for its 11ba specific part[1]
  Use OOK for modulation of the payload portion of the wake-up packet. The Preamble design is TBD. The operation in DFS channels is TBD.
  The OOK waveform of wake-up packet is generated by populating 13 802.11 OFDM subcarriers for unicast WUP

## Slide 3: PSD of WUP and CCA problem
PSD of narrow band signal is much higher than 20MHz signal but legacy CCA is performed based on 20MHz[2]

## Slide 4: Ideal scenario for WUP CCA
Even though legacy STAs may not detect WUR signal part, L-preamble part (-82dB) can protect overall WUP
In order to use L-SIG protection, legacy STAs are required to decode L-preamble part

## Slide 5: Mid packet CCA on WUP
CCA problem on WUP packet only occurs if L-preamble is not received and decoded correctly
If a WUP uses 4MHz band, at most 7 dB of CCA misjudgment could occur to legacy STAs
L-preamble
Narrow band signal
Receive signal from here

## Slide 6: Mid packet CCA scenarios for WUP
Busy by one BSS signal(1)
Because WUP can be overlapped by one BSS signals(1), STAs could not received L-preamble part of WUP
Or, STAs could wake up after L-preamble part by its power saving protocols(2)
L-preamble
Transmission
Primary of two BSSs
Narrow band signal
Or (2)Wake-up after L-preamble part

## Slide 7: Mid packet CCA scenarios for WUP
Secondary channel CCA is performed during PIFS duration only, so any STAs cannot sense narrow-band signal part could interfere and be interfered by WUP in secondary channel
L-preamble
Transmission
Primary CH
Secondary CH
(OBSS Primary CH)
Narrow band signal

## Slide 8: Possible solution – FDM WUP
Lowering PSD could be a solution to the CCA problem
FDM structure[3] of WUP could be a solution
Dummy signal could be used for unicast WUPs even though there are no more STAs to wake up
L-preamble
Narrow band signal
Narrow band signal
Narrow band signal

## Slide 9: Possible solution – Extended WUP
Lowering PSD could be a solution of the CCA problem
Full-band WUP may not cause the CCA problem and WUR could receive it with narrow bandwidth because the WUP is OOK modulated
Specific extended tone sequence or WUR Rx bandwidth could be either standard issue or not
L-preamble
Extended band signal
Narrow band signal
Extended band signal
WUP Tx Bandwidth
WUR Rx Bandwidth

## Slide 10: Conclusions
Narrow band signal part of WUP can cause CCA problem due to its narrow signal bandwidth
Especially, the CCA problem could be observed frequently in wideband and OBSS scenario
In order to minimize CCA problem, duration of WUP narrow band signal part shall be minimized
Full-band WUP structure could prevent CCA problem
FDM WUP or expanded WUP can be considered as a Full-band WUP structure

## Slide 11: References
[1] 11-17-0575-01 “Specification Framework for TGba”
[2] 11-17-1013-01 “Considerations on WUP bandwidth and CCA”
[3] 11-17-1017-02 “Variable signal bandwidth of the wake-up signal for enhanced WUR performance”