## Slide 1: Addressing the RAC/Random Comments
Date: 2017-09-11

## Slide 2: Abstract
This document suggests a way forward to prevent conflict that 802.11 networks may pose on L2 networks administered according to 802c

## Slide 3: Framing the Problem
The problem is about using the local address space, not about taking 2 more bits to randomize MAC addresses
802c presents an optional architecture for network administrators who wish to impose some structure usage of the local address space on their networks
The AAI quadrant in 802c’s SLAP may be used to support STAs that randomize 44 bits of local address
  What if the administrator wants to administratively assign addresses in the AAI quadrant differently and not randomly?
  What if the administrator uses a different quadrant of the SLAP and does not want AAI addresses on his or her network?
We still have a problem even if we just randomize 44 bits!

## Slide 4: Framing the Problem
If an administrator wants to use 802c to impose structure on his or her administered network, either:
  All devices (e.g. 802.11 STAs) need to know what this structure is and agree beforehand to conform to it and behave properly; or
  The administrator needs a way to prevent devices (e.g. 802.11 STAs) that do not follow the proscribed structure– either intentionally or unintentionally– from obtaining access to the L2 network
Provisioning every 802.11 STA with knowledge of how a network it is not connected to is administered does not scale
Kicking 802.11 STAs off the network without some informative reason will not work either

## Slide 5: What’s Needed?
A way for the AP to signal to STAs, pre-association, what sort of administration is being done on the DS
A new Element!
  Absence of this element in Beacons and Probe Responses is the status quo– no specialized structure is imposed on the DS– a STA may optionally randomize 46 bits of local address if it so desires, or it can just connect with it’s machine MAC address
  This element, when present in Beacons and Probe Responses, indicates* the structure that the administrator is placing on the DS that the STA will have to abide by in order to stay connected
  Need to define STA behavior when compliance is not possible
Need some help on how this would look and work… point to 802.1cq?... indicate the SLAP quadrant with a bitmask? … some other idea?

## Slide 6: References