## Slide 1: Security for location determination at a Public Domain
Date: 2017-09-11
Authors:

## Slide 2: FRD Comment
Comment:
The 11az FRD does not cover security without prior shared secret.
Proposed resolution:
Under section 2.1.6 (Security and Privacy) add the following requirement: “The 11az protocol shall support a shared key generation between Responding-Station and Initiating-Station when no previous shared secret was pre-configured”.

## Slide 3: Background/Motivation
Past submissions discussed how to add security to the 11az and 802.11-2016 FTM protocols.
In these submissions, the proposed security eco-system is based upon shared secret or shared cloud resource between the initiator and the responder.
This shared resource is used during the execution of the the location measurement protocol for:
  Authentication
  Privacy

## Slide 4: The Problem
Current FRD doesn’t cover security without prior shared secret or resource => “Public Domain”.
Initiators will not always want or be able to have a shared secret/resource with the AP(s) deployed in the Public Domain:
  May require the client to be active by entering a password or by installing an application
    Not user-friendly.
The Responder may be totally unknown to the Initiator
  No shared secret or shared side connection possible.
Examples for possible use cases in the public domain
  Indoor navigation in mall/airport – the initiator may be disconnected (no access to the cloud/internet) or without the mall application installed.
  Use of Private Responder APs for estimating Initiator’s location
  Indoor E911 – Emergency Services in the indoor.

## Slide 5: The Solution
Adding support for security in 11az without shared resource or secret will allow client without prior shared secret to have privacy and keep the measurement phase safe.
A Share Key (or resource) is needed to mutually authenticate the initiator and the responder
The 802.11az protocol should therefore provide a mechanism to generate a shared key whenever it does not already exist

## Slide 6: Motion
Move to add the following requirement to section 3.1.6 (Security and Privacy) of the 802.11az FRD and grant the FRD Editor editorial license :
The 11az protocol shall support a shared key generation between Responding-Station and Initiating-Station when no previous shared secret has been pre-configured
Moved: Ganesh Venkatesan
Seconded: SK Yong
Yes: 9 No: 0 Abstain: 1
Result: Motion Passes

## Slide 7: References
16/1643r0: Pre-Association Negotiation of Management Frame Protection