## Slide 1: Revised shorter presentation to TGax relating to coexistence efforts in Coexistence SC
13 Sept 2017
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com

## Slide 2: Collaboration is required with ETSI BRAN to ensure 802.11ax achieves its potential as next gen Wi-Fi
Situation
Complication
Answer
Call to action:
Please actively participate in the Coexistence SC to help 802.11ax achieve its full potential!
ETSI BRAN has developed EN 301 893, which regulates operation in the 5 GHz band in Europe …
… but the current version of EN 301 893 is problematic for 802.11ax performance & spatial reuse, globally
… although the planned revision of EN 301 893 provides an opportunity to better enable 802.11ax

## Slide 3: ETSI BRAN has developed EN 301 893, which regulates operation in the 5 GHz band in Europe
  For the last two years, ETSI BRAN has been revising EN 301 893 to align it with the RE-Directive in Europe, particularly Article 3.2:
    Radio equipment shall be so constructed that it both effectively uses and supports the efficient use of radio spectrum in order to avoid harmful interference
  The latest version of EN 301 893 is now in operation, and promotes coexistence between multiple technologies in 5 GHz by specifying:
    LBT similar to EDCA
    … and TxOPs similar to EDCA
    … with an ED-only (-72dBm) mechanism applicable to all technologies
    … or an PD/ED (-82dBm/-62dBm) mechanism applicable to 802.11
  Note: the 802.11 exception does not apply to 802.11ax

## Slide 4: The current version of EN 301 893 is problematic for 802.11ax performance & spatial reuse, globally
  The current version of EN 301 893 will probably result in reasonable coexistence between 802.11a/n/ac and LAA
  However, EN 301 893 has some potential serious problems in the context of 802.11ax
    Some people believe EN 301 893’s PD/ED requirements mean that 802.11ax will have less performance than 802.11ac
      802.11ax is required to use an ED of -72 dBm
      Whereas 802.11ac can use an ED of -62 dBm
    EN 301 893’s PD/ED requirements mean that 802.11ax will be unable to use its new colour based spatial reuse mechanism
      There are no exceptions to the rule for a PD of -82 dBm
  Even worse, the impact of EN 301 893 is not just limited to Europe, with many countries adopting the European rules

## Slide 5: The upcoming revision of EN 301 893 provides an opportunity to better enable 802.11ax
  ETSI BRAN has just adopted a WI to revise EN 301 893, with anything related to Article 3.2 of the RE-Directive within scope
    There is also a desire to end up with a “technology neutral” standard
  The revision provides the IEEE 802.11 WG with an opportunity to propose refinements to EN 301 893
    IEEE 802.11 WG has already asked ETSI BRAN to allow 802.11ax (and any other technology) to use the same ED/PD mechanisms as 802.11ac, thus solving the performance issue
    Coexistence SC has started discussing ways to enable spatial re-use without diminishing the “fair” coexistence enforced by EN 301 893
  Alternatively, IEEE 802.11 WG could ask ETSI BRAN to significantly loosen the requirements in EN 301 893
    This approach is preferred by some in the Coexistence SC because it enables less constrained innovation … albeit with an additional risk to coexistence

## Slide 6: Call to action: Please actively participate in the Coex SC to help 802.11ax achieve its full potential!
Please participate in Coexistence SC if you are …
  Interested (in the short term) in engaging with ETSI BRAN on the EN 301 893 revision, to either:
    Refine the rules to enable 802.11ax … with a “fair” coexistence bias
    Loosen the rules to enable 802.11ax … with an innovation bias
  Interested (in the longer term) in promoting “fair” coexistence in multi-technology environments in collaboration with other SDOs/ITAs
    eg 3GPP for LAA, eLAA, feLAA & NR; MulteFire Alliance for MulteFire
If the Coexistence SC does not proactively address these issues …
… there is a risk 802.11ax will not achieve its potential as the basis of the next generation of Wi-Fi!