## Slide 1: Initial Considerations for LC SG
Date: 2017-08-14
Author:

## Slide 2
This presentation provides our initial considerations on potential tasks of LC SG in preparing the PAR and CSD, including:
Form of standardization
Spectrum
Design targets
Interoperability/coexistence issues
Usage models
Possible timeline
Abstract

## Slide 3
  Whether the PAR should target an amendment or a new series has been discussed in LC-TIG
  TIG report [1]: The decision of whether LC should be a standalone standard (i.e., 802.11.3) or an amendment (802.11xx), should be left to the Study Group. However, the benefits of inheriting the upper portion of the 802.11 MAC and services it provides are seen as key enablers for the commercial success of the technology and therefore the LC TIG recommends that LC should be considered to become an 802.11 amendment rather than a standalone standard.
  LC-SG need to further discuss the issue. The decision should be left to the WG.
Form of Standardization
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 3

## Slide 4: Form of Standardization
  Amendment
  Easier for chipset design: existing standard could be referenced as a basis
  Market has been trained how to decipher the 802.11abgn code [2]
  Adopted technologies may be restricted, as it should be compatible with current or slightly modified MAC standard
  New series
  MAC may be designed from scratch to be compatible with LC operations
  Efforts are needed to educate the market about the new code, e.g. 802.11.x
  No precedent in 802.11 that targets at a new standalone standard has resulted in successful specifications

## Slide 5
Should LC SG only focus on visible light band ?
  Pros of including the infrared band
    IR may be an appropriate uplink solution. There would be no glare from the mobile equipment if infrared is implemented in the uplink;
    IR has the potential to provide high data rate due to the wide modulation bandwidth of IR LED [3].
  Cons of including the infrared band
    May increase complexity of the specification, i.e. may lead to a FDD system which need extra standard efforts
    Additional cost and complexity
    The Infrared (IR) PHY specification (Clause 15) in IEEE802.11-2012 has been removed. So people may wonder whether it is necessary to define a IR PHY again in 802.11 spec
Spectrum
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 5

## Slide 6
Multiple modulation bandwidth support
  Modulation bandwidth of LEDs varies widely
    The modulation bandwidths of off-the-shelf LEDs range from several MHz to tens of MHz. With equalizations and filtering, the modulation bandwidth can be improved to GHz level
  Proposal 1: the PAR/CSD should target to specify technologies to enable inter-operation between devices with different modulation bandwidths
Design Target: Modulation Bandwidth
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 6

## Slide 7
  Potential target throughput metrics
  Aggregated throughput (measured at the MAC data service access point):
  Maximum single link throughput (measured at the MAC data service access point):
  Average throughput per station (measured at the MAC data service access point)
  Any other metrics should be considered for LC?
  Proposal 2: the PAR/CSD should target maximum single link throughput of hundreds of Mbps
Design Target: Throughput
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 7

## Slide 8
  Due to the nature of light, the coverage of a single LC-AP can be limited into several square-meters. Multiple LC-APs maybe needed to ensure coverage in a spacious room.
  The coverage of a single LC-AP may also need to be defined in the design targets.
  Fast transition between neighboring LC-APs is desirable to support continuous user experience.
  Proposal 3: the PAR/CSD should target to enable fast transition between neighboring LC-APs
Design Target: Fast Transition
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 8

## Slide 9
Coexistence with 802.11 legacy devices is not a issue for LC SG/TG because of different spectrum usages.
Should the issue of coexistence with 802.15.13/802.15.7r1/G.vlc be addressed by LC SG?
Coexistence Issues
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 9

## Slide 10
Should hybrid operation of RF and LC be considered by LC SG?
  Hybrid operation of RF and LC may support fast transition between LC-PHY and 802.11 2.4GHz / 5GHz / 60GHz PHYs to extend network coverage.
  LC link may be used for offloading purpose, especially for the downlink.
Hybrid RF / LC
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 10

## Slide 11
  Four general use cases are included in the LC TIG report [1]：
  Enterprise
  Home
  Retail
  IoT
  It is expected that a more comprehensive document of usage models is necessary for further study.
Usage Models
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 11

## Slide 12
Possible timeline for LC SG:
  2017.09
    Outline of basic goals and issues that need to be addressed by the LC SG;
    Call for contributions on the above issues
  2017.11
    Contributions on the above issues;
    Contributions required to establish basis for PAR & CSD
  2018.01
    Draft PAR & CSD
  2018.03
    Finalize PAR & CSD and supporting documents required to gain approval of PAR & CSD by 802.11 WG, 802 EC, and NesCom.
  2018.05
    Task group established
Possible Timeline for LC SG
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 12

## Slide 13: Summary
This presentation provides our initial considerations on potential tasks of LC SG in preparing the PAR and CSD, the following are proposed
  Proposal 1: the PAR/CSD should target to specify technologies to enable inter-operation between devices with different modulation bandwidths
  Proposal 2: the PAR/CSD should target maximum single link throughput of hundreds of Mbps
  Proposal 3: the PAR/CSD should target to enable fast transition between neighboring LC-APs

## Slide 14
References
11-17/0023r9 “Light Communications (LC) for 802.11: Use Cases and Functional Requirements: Guidelines for PAR and CSD Development”, Nikola Serafimovski (pureLiFi), Dobroslav Tsonev (pureLiFi), Abdullah S. Nufaii (Saudi Aramco), Ahmed J. Ghamdi (Saudi Aramco), Murat Uysal (Ozyegin University), Vinko Erceg (Broadcom), Tuncer Baykas (Istnabul Medipol University), Michael McInnis(Boeing), Alphan Sahin (InterDigital, Inc.), Rui Yang (InterDigital, Inc.), John Li (Huawei), Barnaby Fryer (Co-op Group Ltd.), Volker Jungnickel (Fraunhofer HHI)
11-08/0525r0, “Recommendation for 60GHz PAR to be an Amendment to the 802.11 Standard”, Mark Grodzinsky (Wilocity), Gal Basson (Wilocity), Matt Smith (Atheros), Amer Hassan (Microsoft)
http://irdajp.org/irdajp.info/gigair.html