## Slide 1: EDMG Segmentation and Reassembly
Authors:
Name | Affiliations | Address | Phone | email
Oren Kedem | Intel |  |  | oren.kedem@intel.com

## Slide 2: Motivation for Segmentation
11ad Max MSDU size is 7920B.
MSDU size limits the size of the MTU ( Maximum Transmit Unit ) that is reported to upper layer in WLAN systems
Hence, any application that utilizes bigger datagrams is required to segment its datagrams between originator and consumer.
Segmentation done by the upper layer involved with:
  Adding new L3/L4 header,
  Calculating new checksum
  Significant CPU utilization resource allocated for handling the high number of datagram segments
Enabling higher MTUs to upper layer will improve the following:
    CPU cost saving
    Power consumption
    TPT and Efficiency

## Slide 3: Segmentation improvement
  In order to evaluate the expected improvement in CPU Utilization the below test was conducted:
    Ethernet network adapter was operated with and without LSO.
    Implications of LSO feature are similar to those of segmentation in terms of CPU frame processing.
    Test results showed that offloading LSO from upper layer yield performance improvement of ~15-30% in CPU utilization.
    Differences might be expected with relation to 11ay expected improvement as result of the differences in MPDU size and frame processing tasks that the adaptor is required to perform.
Oren Kedem (Intel)

## Slide 4: MSDU Size vs. MPDU/MSDU Modulo size Value Assignment Examples
Maximum Segmented MSDU Exponent | MAX MSDU Size (Bytes) | Number of MPDUs required for one MSDU
13+0 | 8192 | 2
13+1 | 16384 | 3
13+2 | 32768 | 5
13+3 | 65536 | 9
13+4 | 131072 | 17
13+5 | 262144 | 34
13+6 | 524288 | 67
13+7 | 1048576 | 133
13+8 | 2097152 | 265
13+9 | 4194304 | 530
MPDU Modulo size | MSDU Modulo size | MPDU Wrap around | Maximum MSDU Size supported
6 | 8 | 64 | 262144
7 | 7 | 128 | 524288
8 | 6 | 256 | 1048576
9 | 5 | 512 | 2097152
10 | 4 | 1024 | 4194304
11 | 3 | 2048 | 4194304
12 | 2 | 4096 | 4194304
Oren Kedem (Intel)

## Slide 5: BACKUP