## Slide 1: CCA Sensitivity
Date: 2017-09-12

## Slide 2: Abstract
All OFDM-based PHYs in 2.4 GHz and 5 GHz have the same basic requirement for CCA sensitivity, though with significantly different surrounding definitions. There are some problems:
The definitions are still ambiguous, and either underspecify receiver behaviour or may be impossible to meet
As written, the current requirements are far too loose
CIDs addressed: 77

## Slide 3: Minimum Receive(r) Sensitivity
“VHT receiver specification
For tests in this subclause, the input levels are measured at the antenna connectors … . Each output port of the transmitting STA shall be connected through a cable to one input port of the Device Under Test.
Receiver minimum input sensitivity
The packet error ratio (PER) shall be less than 10% for a PSDU of 4096 octets with the rate-dependent input levels listed in Table 21-25 …
[BPSK, rate 1/2 , 20 MHz] 82 dBm”
  —TGmd draft 0.1, section 21.3.18, 21.3.18.1 (pp. 2769-70)

## Slide 4: The CCA threshold
“CCA sensitivity
… in an otherwise idle … channel …
With >90% probability, the PHY shall detect the start of a PPDU that occupies at least the primary 20 MHz of the channel under the conditions listed in Table 21-27 … within a period of aCCATime … and hold the CCA signal busy … for the duration of the PPDU.”
“The start of a 20 MHz VHT PPDU in the primary 20 MHz channel at or above -82 dBm”
  —TGmd draft 0.1, section 21.3.18.5 (p. 2772)

## Slide 5: The -82 dBm VHT CCA threshold—1/4
The basic structure goes back to 802.11a:
“CCA sensitivity
The start of a valid OFDM transmission at a receive level equal to or greater than the minimum 6 Mbit/s sensitivity (-82 dBm) shall cause CCA to indicate busy with a probability >90% within 4 μs.”
  —802.11a-1999 (R2003), section 17.3.10.5

## Slide 6: The -82 dBm VHT CCA threshold—2/4
… and reflected 1999 technology:
“Receiver minimum input level sensitivity
The packet error rate (PER) shall be less than 10% at a PSDU length of 1000 bytes for rate-dependent input levels shall be the numbers listed in Table 91 or less. The minimum input levels are measured at the antenna connector (NF of 10 dB and 5 dB implementation margins are assumed).”
  —802.11a-1999 (R2003), section 17.3.10.1

## Slide 7: The -82 dBm VHT CCA threshold—3/4
Full calculation that led to -82 dBm:
-102.1 dBm1 + 4.7 dB2 + 10 dB3 + 5 dB4 = -82.4 dBm,  -82 dBm5
Corresponding calculation if specified today:
-102.1 dBm + 4 dB(2) + 6 dB(3) = -92.1 dBm,  -92 dBm
Noise floor for 16.25 MHz
Operating point for 6 Mbps 1,000 byte packets, 10% FER, from the simulations used
Noise figure
Implementation margin
See docs. IEEE 802.11-99/023, “Comments on P802.11a draft”, M. Morikura (NTT), January 1999 (giving curves, -88 dBm for first three combined), and IEEE 802.11-99/016, “Comments received on 802.11a in Letter Ballot 16”, January 9, 1999, pp. 7-8 (-87.4 dBm for first three, proposing -82 dBm)

## Slide 8: The -82 dBm VHT CCA threshold—4/4
Additional factors
For successful CCA, we need to decode the L-SIG (4 bytes), instead of 1,000 or 4,000 bytes
For successful CCA in deployed devices, we need to decode L-SIG with frequency-selective fading rather than AWGN
For successful CCA in deployed devices, we need to decode L-SIG in presence of interference

## Slide 9: Some issues—VHT case
Does the CCA threshold requirement include a restriction that the measurement is made in a cabled setup?—Cf. 21.3.18
  If so, what is the requirement for a deployed device? Is there a requirement?
  Also if so, what does the condition “in an otherwise idle … channel” mean (21.3.18.5)?
  And further, if so, why do we choose a level that is  10-15 dB looser than should be possible with current devices?
If the CCA threshold requirement does not assume a cabled setup, and does apply to a deployed device, what is the requirement if there is interference?
  Is it even possible to guarantee >90% success at 82 dBm?
-

## Slide 10: HT CCA requirements—HT and ERP PPDUs
“CCA requirements for non-HT PPDUs in the primary channel are described in 17.3.10.6 (CCA requirements) and 18.4.6 (CCA performance).”
“For an HT STA with the operating channel equal to 20 MHz, the start of a valid 20 MHz HT PPDU at a receive level greater than or equal to the minimum modulation and coding rate sensitivity of 82 dBm shall cause the PHY to set PHY-CCA.Indication(Busy) with probability > 90% within 4 ms.”
—TGmd draft 0.1, sections 19.3.19.5.2, .3 (pp. 2579-80)
(no mention of measurement at antenna connectors)

## Slide 11: Some further issues—VHT case
Since a VHT STA is also an HT STA, the VHT STA is required to follow the clause 19 specification for HT (and ERP, etc.) PPDUs
The VHT STA cannot distinguish between VHT and HT PPDUs until well after 4 ms*, so CCA must go high until after L-SIG is decoded
  Is it possible to satisfy the requirement in the presence of interference?
* aCCATime vs. 4 ms is a topic for another day

## Slide 12: The CCA problem, and outline solution—I
Should the standard specify normative requirements for when deployed devices declare and maintain CCA?
  It’s not that clear that D0.1 does so now, at least in any consistent way
If we do so specify, how should the requirement be phrased?
  Historically  82 dBm over-the-air received energy (S + N + I)
  But this has the problem that we cannot guarantee > 90% probability of decoding L-SIG and maintaining CCA high for duration of the PPDU
    It was fine for 11a and 11g, and even 11n, when I was usually low
Thresholds and probabilities
  The historic requirement was > 90% probability of success
  But probability of success (for deployed device) depends on multipath in channel, unknown when device makes its first energy assessment

## Slide 13: The CCA problem, and outline solution—II
Candidate solution:
  Declare initial CCA (start of PPDU through L-SIG) given combination of received signal strength and autocorrelation
    Autocorrelation to take care of high background interference levels
    Level set low enough that > 90% of valid preambles can be detected, over reasonable spread of channels
  Declare CCA high for remaining duration if L-SIG is decoded
Minimum receive sensitivity
  No need to specify performance in multipath, since most receivers have same basic structure
  Level should really be lower than now, but strictly speaking only performance in decoding L-SIGs matters

## Slide 14: References
[1] IEEE doc. 11/17-0458r0, “OBSS_PD: Threshold Problems”, S. Coffey (Realtek), March 2017
[2] IEEE doc. 11/15-1139r1, “Co-chairmen notes on current status of 802.11ax Spatial Reuse ad hoc group”, G. Hiertz (Ericsson) et al., September 2015
[3] IEEE doc. 11/17-1444r0, “History of PD and ED reviewed”, G. Hiertz (Ericsson) et al., September 2017