## Slide 1: Consideration on WUR frame for Fast Scanning
Date: 2017-11-01
Authors:
Name | Affiliation | Address | Email
Li Nan | ZTE Corporation | No.9 Wu Xing Section Xi Feng Road Xi’an, Shaanxi Province P.R.China | li.nan25@zte.com.cn
Lv Kaiying |  |  | lv.kaiying@zte.com.cn
Sun Bo |  |  | sun.bo1@zte.com.cn
Wei Ning |  |  | wei.ning@zte.com.cn

## Slide 2: Background
Usage model 7 provides scenario about goods (WUR capability enabled) in delivery to be tracked and rediscovered by AP for location report[1]. This usage model is about how to scan the target AP so that the WUR STA can be discovered by the new AP.
  R.4.1.A:IEEE 802.11ba shall provide mechanisms to enable re-discovery of WUR stations by AP[2].
  Usage model 9 Smart scanning :The mobile device passively scans through multiple channels using WUR, and collects basic information about nearby APs. The collected info can be used to facilitate the devices’ roaming decisions.
We futher discuss passive scanning using wake up radio in this proposal.

## Slide 3: Introduction
An WUR STA may perform passive scanning using its wake up radio during WUR mode as background scanning to collect information about neighbor BSSs or target BSS/ESS for the purpose of AP reselection.
However, it would be very inefficient and power consuming if an WUR STA has to do WUR scanning on many WUR channels first and then do primary channel scanning.
To implement WUR scanning effectively, some details should be further considered:
  Neighbor WUR information can be provided to the STA to facilitate WUR scanning:
    WUR discovery channel, SSID/compressed SSID, and primary channel are proposed.
  Methods to advertise these information.

## Slide 4: Proposed Scheme (1/3)
Information A: WUR discovery channel location
To help a STA in WUR mode performing WUR scanning with less power consumption, WUR discovery channel(s) of neighbor BSSs or target BSS(s)/ESS(s) could be provided to the STA by its associated AP.
  Only one WUR discovery channel per BSS /ESS needs to be advertised.
  WUR scanning will be limited to specific WUR channels.
  The STA can monitor its own WUR frame on its WUR channel during ON windows and perform WUR scanning on dedicated WUR discovery channels during OFF windows of duty cycles if needed.
Delivery method:
Opt 1: delivered in a neighbor WUR parameter element by PCR in 802.11 frame such as beacon/probe response frame
  Pros: Considering the overhead, it is more efficient to sent this information by PCR
  cons: Any change about WUR channel location will be notified by waking up the STA.
Opt 2: delivered by WUR frame such as WUR beacon or a specific WUR frame
  Pros: Any change about WUR channel location can be notified without waking up the STA.
  cons: less efficient if the information of WUR channel location is large.

## Slide 5: Proposed Scheme (2/3)
Information B: SSID/ compressed SSID
In some use case, for example, in a network of warehousing system, many freight companies may share the same warehouse. A plurality of APs of a specific company forms a separate ESS for the ease of network management.
A STA may prefer to choose a candidate AP within the same ESS for fast BSS transition
SSID/compressed SSIDs can assist STA to choose candidate AP(s) within the same ESS during WUR scanning.
Delivery method:
An AP can indicate the candidate compressed SSID to help the STA select a target AP in a neighbor WUR parameter element by PCR in 802.11 frame such as beacon/probe response frame
WUR frame such as WUR beacon or a specific WUR frame such as WUR discovery frame should also advertise its compressed SSID
  A compressed SSID is used to reduced the overhead. eg. In 802.11ah , the size of a compress SSID is 4byte.

## Slide 6: Proposed Scheme (3/3)
Information C: Primary channel of PCR
Once an WUR STA has already selected some APs as candidate APs through WUR scanning, the WUR STA turns on its main radio for AP discovery. It would be more efficient if it can use the result of WUR scanning for future association.
If the STA has no information about the candidate AP(s)' primary channel, then the STA still has to perform main radio scanning on each channel to find the candidate APs, which is certainly not efficient.
It's suggested that the primary channel of a target AP should be provided to the associated STA.
Delivery method:
Opt 1:deliverd in a neighbor WUR parameter element by PCR in 802.11 frame such as beacon/probe response frame
  Any change about primary channel location will be notified by waking up the STA.
Opt 2: delivered in WUR frame such as WUR beacon or a specific WUR frame for network selection
  Any change about primary channel location can be notified without waking up the STA.

## Slide 7: Proposed Example (1/2)
Example 1:
  An AP advertises its own WUR parameter element in PCR including:
    its compressed SSID and/or BSS ID
    its WUR channel or primary WUR channel if the AP allocates more than one WUR channels
  The AP may also include a neighbor WUR parameter element in PCR to indicate the WUR configuration of target BSS(s) or ESS to assist STAs for fast WUR scanning, including:
    target compressed SSID and/or BSS ID
    (Primary) WUR channels of target BSS(s) or ESS
    Primary channel of target BSS(s) or ESS
  An WUR frame should indicate its compressed SSID and/or BSS ID to facilitate WUR STAs to scan the target BSS or ESS
    The WUR frame can be a unicast/multicast WUR packet or an WUR Beacon or a specific WUR frame for network selection
    WUR STAs scan the target WUR channels and match the scanned compressed SSID and BSS ID with the target one, and
    Turn on its PCR to scan the primary channels of target BSS(s)

## Slide 8: Proposed Example (2/2)
Example 2:
  An AP advertises its own WUR parameter element in PCR including:
    its compressed SSID and/or BSS ID
    its WUR channel or primary WUR channel if the AP allocates more than one WUR channels
  The AP may indicate in PCR the target BSS(s) or ESS to assist STAs for network selection, including:
    target compressed SSID and/or BSS ID
    target WUR channel list
  An WUR frame should indicate its primary channel and its compressed SSID and/or BSS ID to facilitate WUR STAs to scan the target BSS or ESS on the indicated primary channel
    The WUR frame can be an WUR Beacon or a specific WUR frame for network selection
    WUR STAs scan the target BSS or ESS through target WUR channels, and
    Acquire the primary channel info of the target PCR from WUR frame
    Turn on its PCR to scan the primary channels of target BSS(s)

## Slide 9: Summary
We discussed the WUR parameters of neighbor BSSs/ESS that are needed for improving power consumption with WUR scanning
  WUR discovery channel location
  BSS ID/compressed SSID
  primary channel
The method of advertising these parameters has also been discussed.
  By using 802.11 message such as Beacon frame or probe response frame
  By using wake up frame such as WUR unicast/multicast packet, WUR beacon or specific wake up frame for network selection

## Slide 10: Straw Poll 1
Do you agree that compressed SSID shall be included in a WUR frame to assist WUR scanning and network selection?
WUR channel location
  Y
  N
  A
SSID/Compressed SSID
  Y
  N
  A
Primary channel
  Y
  N
  A

## Slide 11: Straw Poll 2
Do you agree that AP may send neighbour AP WUR parameters to assist STA's WUR scanning?
  Y
  N
  A

## Slide 12: References
[1]11-17-0029-10-00ba-wur-usage-model-document
[2]11-17-0575-05-00ba-spec-framework