## Slide 1
Considerations on WUP types
Date: 2017-11-06
Authors:

## Slide 2: Introduction
TGba has defined and is considering multiple types of WUP
  Wake-up frame[1]
    Unicast Wake-up frame which requires a response frame from target STA using its primary connectivity radio
    Multicast Wake-up which does not require a response frame from target STAs and the AP can transmit broad cast/multicast frame after the preparation period
  WUR Beacon[1]
    May include WUR and PCR configuration parameters
  WUR discovery frame[2]
    May advertise BSS information without primary connectivity radio
  Vendor specific WUR frame[3]
    Variable length frame structure was considered
    Based on its purpose, it may require primary connectivity radio to wake-up or not

## Slide 3: 11ba PPDU structure
11ba is considering narrower bandwidth structure for WUR specific PPDU part
  Non-HT preamble with 20MHz is reused before WUR specific PPDU part
  WUR specific PPDU part utilizes 13 subcarriers with subcarrier spacing of 312.5kHz for narrow bandwidth WUP structure[1]
Narrow bandwidth WUP may cause mid packet CCA problem because of difference of 7dB power caused by -7dB of bandwidth[4]
  WUP with 20MHz bandwidth could solve this problem
  Specific subcarrier structure has bees discussed but more is needed (e.g., FDM structure, extended tone structure, dummy tone structure, etc.,)
However, still 7dB power spectral density is attractive for transmission range of WUP when there are no power spectral density restriction
In this presentation we want to examine this trade-off based on types of WUP

## Slide 4: Recap : FDM WUP structure
Lowering PSD could be a solution to the mid packet CCA problem
FDM structure of WUP could be a solution
Dummy signal could be used for unicast WUPs even though there are no more STAs to wake up (Dummy tone structure)
L-preamble
Narrow band signal
Narrow band signal
Narrow band signal

## Slide 5: Recap : Extended WUP structure
Full-band WUP may not cause the CCA problem and WUR could receive it with narrow bandwidth because the WUP is OOK modulated(Power detector)
Extended tone is also “ON” if the narrow band signal is “ON”, otherwise, extended tone is “OFF”, too
Specific extended tone sequence or WUR Rx bandwidth could be either standard issue or not
L-preamble
Extended band signal
Narrow band signal
Extended band signal
WUP Tx Bandwidth
WUR Rx Bandwidth

## Slide 6: PCR procedure after receiving WUP
Basically wake-up packet is considered to ‘wake’ STAs up.
Because of this property, we have agreed with the following statement in the PAR document
  The WUR is a companion radio to the primary connectivity radio and meets the same range requirement as the primary connectivity radio[5]
    In order to avoid cases that STAs wake up but cannot communicate with its PCR
    In this case, transmission range gain of narrow band structure is not so useful, only AP’s energy gain can be achieved with existence of CCA problem
    There is no trade-off between CCA problem and transmission range. Therefore, CCA problem is much more important than transmission range in this case
However, 11ba has been developing some WUR procedures using WUP which does not wake up PCR
  Some WUPs may not require any PCR procedures of target STAs after WUP transmission
  In this case, transmission range is meaningful although it causes CCA problem

## Slide 7: WUP requiring PCR operation
Unicast WUP – Case I (PCR range ≈ WUP range)
  If the distance between an AP and a STA is shorter than PCR range or WUP range, STA and AP can communicate with no problem. If the distance is larger than the range, the STA cannot be waken up by WUP

## Slide 8: WUP requiring PCR operation
For multicast(broadcast) WUP, identical problem mentioned in previous slides can occurs
It means that if a WUP requires PCR operation between AP and target STA(s) after the transmission of WUP, transmission range enhancement of WUP is not so beneficial
Therefore, transmitting an WUP with 20MHz bandwidth is better for the Wake-up frame transmission

## Slide 9: WUP requiring PCR operation
Multicast WUP – Case I (PCR range = WUP range)
  If the distance between an AP and a STA is shorter than PCR range or WUP range, STA and AP can communicate with no problem. If the distance is larger than the range, the STA cannot be waken up by WUP

## Slide 10: WUP requiring PCR operation
Unicast WUP – Case II (PCR range << WUP range)
  If the distance between an AP and a STA is larger than PCR range but smaller than WUP range, meaningless wake up and transmission occurs
  It causes power inefficiency on non-AP STAs

## Slide 11: WUP not requiring PCR operation
WUP for special purpose
  WUR beacon, WUR discovery and some vendor-specific WUP may not require PCR operation after WUP Tx&Rx
  These WUPs are considered as an information carrier or a parameter update indicator frame.
  In many cases, these frames are not transmitted frequently
  Therefore, in order to maximize information delivery rate of these frames, using long range WUP PPDU format is more beneficial even though the long range PPDU format may cause CCA problem

## Slide 12: Conclusions
Narrow band signal part of WUP can cause CCA problem due to its narrow signal bandwidth
However, narrow band WUP has advantages of long range information delivery
Long range delivery is suitable for some types of WUP that does not require PCR operation
Using full-band WUR PPDU format for for normal Wake-up packet and narrow-band(long range) WUR PPDU format for others could be a good solution

## Slide 13: References
[1] 11-17-0575-05 “Specification Framework for TGba”
[2] 11-17-1608-00 “WUR Discovery Frame for Smart Scanning”
[3] 11-17-1334-00 “Vendor Specific WUR Frame Follow Up”
[4] 11-17-1426-00 “WUP CCA Problem”
[5] 11-16-1045-09 “A PAR Proposal for Wake-up Radio”