## Slide 1: Ranging ID and its Lifetime Management
Date: 2017-11-06
Authors:

## Slide 2: Motivation/Background
Ranging Id is assigned by an AP to unassociated STAs that initiated a MU iFTMR with the AP
The assigned Ranging ID is communicated via the iFTM that the AP sends in response to iFTMR to the STA
The assignment and maintenance of the Ranging ID consumes resources in the AP
  To conserve resources AP’s would like to release resources associated with inactive Ranging IDs as soon as possible
This submission discusses Ranging ID lifetime and management

## Slide 3: Ranging ID Lifetime
AP has an implementation dependent Ranging ID lifetime
  Lifetime of all Ranging IDs assigned by the AP
  If the STA to which a Ranging ID is assigned by the AP
    does not initiate a Range Measurement Request to the AP within the Ranging ID lifetime, the Ranging ID assignment is retired
      The STA must obtain a new Ranging ID in order to initiate a Range Measurement with the AP – this requires the STA to send an iFTMR and receive an iFTM with the status set to SUCCESS
    does initiate a Range Measurement within the Ranging ID lifetime(at time = t), the subsequent Range Measurement request from rhe STA to the AP must be received by the AP before time = t + lifetime

## Slide 4: How does this work (an example)?

## Slide 5: Straw Poll
We support:
  Ranging IDs are of the same size and range as AIDs and following same rules and limitations.
  Ranging IDs and AIDs are from same space and non-conflicting.
  the assignment of Ranging IDs by a RSTA to unassociated ISTA resulting in the execution MU HEz Ranging protocol with the RSTA:
    the assigned Ranging ID is included in the HEz Specific subelement contained in iFTM.
  the RSTA may advertise a Ranging ID lifetime which defines the duration for which the Ranging ID remains valid
    the mechanism to advertise Ranging ID lifetime is TBD
    the best choice for Ranging ID lifetime value is implementation dependent
  the Ranging ID is retired at both ISTA and RSTA when the corresponding Ranging ID Lifetime expires which also terminates the FTM session.
  Ranging ID lifetime may be equal to MAX BSS IDLE PERIOD.
  When an FTM session terminates or aborts the Ranging ID expires.
  Termination may be explicit (i.e. using FTM or FTM Req) or implicit due to Ranging ID Lifetime expiration.
  Support of the Ranging ID Lifetime is optional.

## Slide 6: Motion
Move to add the following to the SFD:
  Ranging IDs are of the same size and range as AIDs and following same rules and limitations.
  Ranging IDs and AIDs are from same space and non-conflicting.
  the assignment of Ranging IDs by a RSTA to unassociated ISTA resulting in the execution MU HEz Ranging protocol with the RSTA:
    the assigned Ranging ID is included in the HEz Specific subelement contained in iFTM.
  the RSTA may advertise a Ranging ID lifetime which defines the duration for which the Ranging ID remains valid
    the mechanism to advertise Ranging ID lifetime is TBD
    the best choice for Ranging ID lifetime value is implementation dependent
  the Ranging ID is retired at both ISTA and RSTA when the corresponding Ranging ID Lifetime expires which also terminates the FTM session.
  Ranging ID lifetime may be equal to MAX BSS IDLE PERIOD.
  When an FTM session terminates or aborts the Ranging ID expires.
  Termination may be explicit (i.e. using FTM or FTM Req) or implicit due to Ranging ID Lifetime expiration.
  Support of the Ranging ID Lifetime is optional.

## Slide 7: Backup

## Slide 8: How is the Ranging ID Advertised?
In iFTM (HEz-specific sub-element)
  Probably the best way to communicate this value
  Delivered along with the Ranging ID
    The lifetime alone does not make sense
As a capability

## Slide 9: What would be the best choice for the value of the Ranging ID Lifetime?
Should allow for reuse of Ranging IDs as fast as possible
Could be as large as BSS Max Idle Period?
  Would match associated STA behavior – is this needed?
  Would tie-up Ranging IDs for too long
  Security implications of having an unused Ranging ID live longer than needed
Best to set the Ranging ID Lifetime in such a way that the Ranging ID is retired as soon as one of the following happens:
  FTM session is torn down explicitly
  The initiator does not initiate a new Ranging Measurement before the (last LMR delivery + Ranging ID lifetime)

## Slide 10: Other Issues to consider
What happens if the STA with Ranging ID is never Polled?
  Ranging ID lifetime determination should consider the worst case scenario for a STA to be polled.
What happens of the RSTA switches between SU and MU modes of ranging with a STA that is assigned a Ranging ID?
  Ranging ID lifetime be renewed when a ranging happens (irrespective of the ranging being SU or MU)