## Slide 1: IMT-2020 Usage Scenarios, Test Environments and Evaluation Configurations
Date: 2017-11-26
Authors:
Name | Affiliations | Address | Phone | email
Roger Marks | EthAirNet Associates | Denver, CO, USA | 1-802-capable | roger@ethair.net

## Slide 2: Abstract
This contribution, intended for presentation to the IEEE 802.11 Advanced Access Network Interface Standing Committee (AANI), summarizes the IMT-2020 Usage Scenarios, Test Environments and Evaluation Configurations. It does not attempt to represent the detailed environments, configurations, or technical performance requirements but only to summarize their applicability and some key parameters.
A key point is that a successful IMT-2020 proposal must cover a comprehensive and challenging set of demands.
Note: This information is reorganized from multiple sources. Errors are possible. Please bring any errors to the attention of ANNI.

## Slide 3: IMT-2020 Usage Scenarios
enhanced mobile broadband (eMBB)
massive machine type communications (mMTC)
ultra-reliable and low-latency communications (URLLC)

## Slide 4: IMT-2020 Test Environments
A test environment is defined as the combination of usage scenario and geographic environment as described in the draft new Report ITU-R M.[IMT-2020.EVAL].
  Note: The quote is from [2]; its reference is to [3].
Test Environments for eMBB [3]
  Indoor Hotspot
  Dense Urban
  Rural
Test Environment for mMTC [3]
  Urban Macro-mMTC
Test Environment for URLLC [3]
  Urban Macro-URLLC

## Slide 5: Test Environment Requirements [1]
IMT-2020 Step 2 (“Development of candidate RITs or SRITs”) [1]:
  An RIT needs to fulfil the minimum requirements for at least three test environments; two test environments under eMBB and one test environment under mMTC or URLLC.
IMT-2020 Step 6 (“Review to assess compliance with minimum requirements”) [1]:
  the evaluated proposal for an RIT/SRIT is assessed as a qualifying RIT/SRIT, if an RIT/SRIT fulfils the minimum requirements for the five test environments comprising the three usage scenarios.
  Such a qualified RIT/SRIT will go forward for further consideration in Step 7.

## Slide 6: IMT-2020 Evaluation Configurations [3]
Evaluation configurations are defined for the selected test environments. The configuration parameters shall be applied in analytical and simulation assessments of candidate RITs/SRITs.
For the cases when there are multiple evaluation configurations under the selected test environment, one of the evaluation configurations under that test environment can be used to test the candidate RITs/ SRITs. The technical performance requirement corresponding to that test environment is fulfilled if this requirement is met for one of the evaluation configurations under that specific test environment.
In addition, for the Rural-eMBB test environment, the average spectral efficiency value should meet the threshold values for the LMLC (low mobility large cell) evaluation configuration with ISD of 6000 m and either evaluation configuration with ISD of 1732 m.
  Note: This last point is discussed below.

## Slide 7: Indoor Hotspot-eMBB Evaluation Configurations [3]
(selected highlights only; see sources for full details) |  |  | 
 | Configuration A | Configuration B | Configuration C
Inter-site distance | 20 m |  | 
Device deployment | 100% indoor (3 km/h) |  | 
UE density | 10 UEs per TRxP (transmission reception point) |  | 
Carrier frequency | 4 GHz | 30 GHz | 70 GHz
Bandwidth (TDD) | 20 MHz | 80 MHz | 80 MHz
Number of antenna elements per TRxP | Up to 256 Tx/Rx | Up to 256 Tx/Rx | Up to 1024 Tx/Rx
Number of UE antenna elements | Up to 8 Tx/Rx | Up to 32 Tx/Rx | Up to 64 Tx/Rx

## Slide 8: Dense Urban-eMBB Evaluation Configurations [3]
(selected highlights only; see sources for full details) |  | 
 | Configuration A | Configuration B
Inter-site distance | 200 m | 
Device deployment | 80% indoor (3 km/h), 20% outdoor (in-car, 30 km/h) | 
UE density | 10 UEs per TRxP | 
Carrier frequency | 4 GHz | 30 GHz
Bandwidth (TDD) | 20 MHz | 80 MHz
Number of antenna elements per TRxP | Up to 256 Tx/Rx | Up to 256 Tx/Rx
Number of UE antenna elements | Up to 8 Tx/Rx | Up to 32 Tx/Rx

## Slide 9: Rural-eMBB Evaluation Configurations [3]
(selected highlights only; see sources for full details) |  |  |  | 
 | Configuration A | Configuration B |  | Configuration C (LMLC)
Bandwidth (TDD) | 20 MHz |  |  | 
UE density | 10 UEs per TRxP |  |  | 
Inter-site distance | 1732 m |  |  | 6000 m
Device deployment | 50% indoor; 50% in-car |  |  | 40% indoor, 40% outdoor pedestrian, 20% in-car
UE speeds of interest | Indoor: 3 km/h; in-car: 120 km/h; 500 km/h for evaluation of mobility in high-speed case |  |  | Indoor : 3 km/h; Outdoor pedestrian: 3 km/h; in-car: 30 km/h
Carrier frequency | 700 MHz |  | 4 GHz | 700 MHz
Number of antenna elements per TRxP | Up to 64 Tx/Rx |  | Up to 256 Tx/Rx | Up to 64 Tx/Rx
Number of UE antenna elements | Up to 4 Tx/Rx |  | Up to 8 Tx/Rx | Up to 4 Tx/Rx

## Slide 10: eMBB Mobility Requirements
Under Rural eMBB test environment, target values for both mobility of 120 km/h and 500 km/h in Table 4 of Report ITU-R M.[IMT-2020.TECH PERF REQ] shall be achieved to fulfill mobility requirements of Rural-eMBB test environment. [3]
  Note: The requirement is not limited to specified configurations.
Test environment | Normalized traffic channel link data rate (Bit/s/Hz) | Mobility (km/h)
Indoor Hotspot – eMBB | 1.5 | 10
Dense Urban – eMBB | 1.12 | 30
Rural – eMBB | 0.8 | 120
 | 0.45 | 500
TABLE 4: Traffic channel link data rates normalized by bandwidth [2]

## Slide 11: eMBB Average Spectral Efficiency [2]
for the Rural-eMBB test environment, the average spectral efficiency value should meet the threshold values for the LMLC (low mobility large cell) evaluation configuration with ISD of 6000 m and either evaluation configuration with ISD of 1732 m [3]
Test environment | Downlink (bit/s/Hz/TRxP) | Uplink (bit/s/Hz/TRxP)
Indoor Hotspot – eMBB | 9 | 6.75
Dense Urban – eMBB | 7.8 | 5.4
Rural – eMBB | 3.3 | 1.6
TABLE 2: Average spectral efficiency [2]

## Slide 12: mMTC Evaluation Configurations [3]
(selected highlights only; see sources for full details) |  | 
 | Configuration A | Configuration B
Carrier frequency | 700 MHz | 
BS antenna height | 25 m | 
Percentage of high loss and low loss building type | 20% high loss, 80% low loss | 
# of antenna elements per TRxP | Up to 64 Tx/Rx | 
#of UE antenna elements | Up to 2 Tx/Rx | 
Device deployment | 80% outdoor, 20% indoor | 
UE density | 10 UEs per TRxP | 
Inter-site distance | 500 m | 1732 m
Bandwidth | up to 10 MHz | up to 50 MHz
key special requirement:
  connection density: 1 000 000 devices per km2 [2]

## Slide 13: URLLC Evaluation Configurations: [3]
(selected highlights only; see sources for full details) |  | 
 | Configuration A | Configuration B
Carrier frequency | 4 GHz | 700 MHz
#of antenna elements per TRxP | Up to 256 Tx/Rx | Up to 64 Tx/Rx
#of UE antenna elements | Up to 8 Tx/Rx | Up to 4 Tx/Rx
Device deployment | 80% outdoor, 20% indoor | 
UE density | 10 UEs per TRxP | 
Inter-site distance | 500 m | 
Bandwidth | up to 100 MHz | up to 40 MHz
key special requirements:
  1-10-5 (five nines) success probability of transmitting a layer 2 PDU of 32 bytes within 1 ms in channel quality of coverage edge for the Urban Macro-URLLC test environment…) [2]
  1 ms user plane latency [2]

## Slide 14: Conclusions and Observations
The IMT-2020 process specifies that successful proposals must meet a challenging set of demands in a wide range of extreme conditions:
  carrier frequency of 700 MHz, etc.
  mobility of 30 km/h, 120 km/h, 500 km/h, etc.
  inter-site distance of 500 m, 1.7 km, 6 km, etc.
It may be difficult for a single RIT to meet all of the demands.

## Slide 15: Call to Action
Review this content and ensure that it is correct
  it is derived from the source documents, but it’s possible that the author has misunderstood the source
If the content is correct, imagine a set of IEEE 802.11 technologies that will satisfy the full set of IMT-2020 requirements
    Including the detailed requirements, not only the highlights herein

## Slide 16: References
[1] Revision 1 to Document IMT-2020/2 (“Submission, evaluation process and consensus building for IMT-2020”), 2017-02-27
[2] Revision 1 to Document 5/40-E (“Draft New Report ITU-R M.[IMT-2020.TECH PERF REQ]: Minimum requirements related to technical performance for IMT-2020 radio interface(s)”), 2017-02-22
[3] Revision 1 to Document 5/57-E (“Draft New Report ITU-R M.[IMT-2020.EVAL]: Guidelines for evaluation of radio interface technologies for IMT-2020”), 2017-10-17