## Slide 1: Mapping DN/CN of mmWave Distribution Network to DMG Entities
Authors:
Name | Company | Address | Phone | Email
Lochan Verma | Qualcomm |  |  | lverma@qti.qualcomm.com
George Cherian |  |  |  | gcherian@qti.qualcomm.com
Solomon Trainin |  |  |  | strainin@qti.qualcomm.com
Djordje Tujkovic | Facebook |  |  | djordjet@fb.com
Nabeel Ahmed |  |  |  | nabeel@fb.com
Payam Torab |  |  |  | ptorab@fb.com
Carlos Cordeiro | Intel |  |  | Carlos.cordeiro@intel.com

## Slide 2: Outline
DN/CN mapping to DMG entities is discussed
  Summary: No standards change needed
We propose the following:
  Standard to specify only a single hop TDD link
    Use PCP/AP to a non-PCP/non-AP relationship to specify the single hop
      DN implementation includes co-located PCP/AP and non-PCP/non-AP STA
      CN implementation includes non-PCP/non-AP STA
  Multi-hop/mesh TDD links are implementation choice. For e.g.,
    Packet forwarding can be at different Layers, e.g., IP Layer routing

## Slide 3: Single Hop TDD Link
DN implementation includes at least one PCP or AP that supports SP with TDD channel access
CN implementation includes a STA that is not a PCP and not an AP and supports SP with TDD channel access
Up to implementation to model DN as PCP or an AP
  PCP supported by all DMG STAs while AP function is not
  AP support DSS (Distribution System Service) while PCP do not

## Slide 4: Single hop TDD Link (1/2)
Implementation
  DN: collocated PCP/AP and non-PCP/non-AP STA
    Two MAC sublayers coordinated by MM-SME and same antennas and PHY shared by MAC sublayers OR
    Two separate MAC & PHY, with MAC sublayers coordinated by MM-SME, and one MAC and PHY pair dedicated to PCP/AP and non-PCP/non-AP STA entity, respectively
  CN: non-PCP/non-AP STA

## Slide 5: Single hop TDD Link (2/2)
Non-PCP/non-AP
PHY
CN
MM-SME
PCP/AP
Non-PCP/non-AP
PHY
DN
PBSS/BSS
Example: DN – DN TDD link
Example: DN - CN TDD link
MM-SME
PCP/AP
Non-PCP/non-AP
PHY
DN1
MM-SME
PCP/AP
Non-PCP/non-AP
PHY
DN2
PBSS/BSS

## Slide 6: Multi-hop/Mesh TDD Link
Implementation choice and out of scope of standard
Packet forwarding can be at a different Layer(s)
  E.g., IP Layer Routing
MM-SME
PCP/AP
Non-PCP/non-AP
PHY
DN1
MM-SME
PCP/AP
Non-PCP/non-AP
PHY
DN2
PBSS/BSS
MM-SME
PCP/AP
Non-PCP/non-AP
PHY
DN3
PBSS/BSS

## Slide 7: Summary
DN and CN are implementation manifestations of existing DMG entities
  DN implementation includes co-located PCP/AP and non-PCP/non-AP STA
  CN implementation includes non-PCP/non-AP STA
Therefore, no edits are warranted to 11ay draft in regards to definition of DN and CN entities of mmWave Distribution Network