## Slide 1: First Path FTM SFD Text
Date: 2017-12-15
Authors:

## Slide 2: Abstract
This presentation proposes the protocol and signaling needed to enable first path usage on FTM protocol.

## Slide 3: Why First Path?
In may cases the LOS path between the STAs participating in FTM is blocked or attenuated.
  The 60GHz beamforming training algorithm locks on a reflection (NLOS) path
  If location algorithms use a reflection we get wrong locations
It is possible (in many cases) to force the beamforming training algorithm to lock on the first path (hopefully LOS)

## Slide 4: What needs to be done?
Get the beamforming training to optimize for the first path
  Done in 11ay
Add a capability bit for this feature
  11ay added a capability bit for the BF training. Actual use is trivial when the antenna settings for first path is available.
  The capability bit is probably not needed.
Define signaling on when First Path is used in an FTM burst
Define when the use of the first path stops

## Slide 5: Protocol
The first path will be indicated using a new value for the trigger field in the FTM Request.
The first path should be used for both RX and TX at both the responder and initiator, starting form the first FTM exchange. It is used in all the frames in the exchange.
The Initiator and responder return to using the Best Quality path at the end of the burst (number of transmission reached or timeout).

## Slide 6: Proposed SFD text:
The following text should be added to section 4 of SFD
“The trigger field in the FTM frame shall be set to 2 to indicate that the burst triggered by this frame shall be transmitted and received using the antenna setting of the First Path. When the trigger field is set to 1, the antenna setting of the best quality path shall be used throughout the burst. The trigger field may be set to 2 only if both the initiator and the responder have indicated support for First Path BF training in their capabilities fields.
The return to best quality antenna setting, when the trigger field was set to 2, shall occur at the end of the burst, when the number of FTM exchanges is reached or when the Burst Duration is reached.”

## Slide 7: Strawpoll
Do you agree to the text changes proposed in slide 6?

## Slide 8: References