## Slide 1: Default UORA Parameters
Date: 2017-12-02
Authors:

## Slide 2: Abstract
UORA used for association procedure (AID12=2045)
  Need explicit expectations for AP and non-AP STA
  Goal for an expected typical case = minimize association latency
Define default UORA parameters to be used by AP
  E.g. frequency of UORA, number of RA RU per trigger, initial OBO window
  Recommendations for modifying these parameters
    Should the need arise per dynamic scenario
Define nature and timing of association exchange follow up triggers
Define rules for participation in UORA by non-AP STA

## Slide 3: CID 16451
16451 | Matthew Fischer | Provide default parameters for UORA operation | Provide default UORA parameters, including values for minimum UORA trigger frequency and minimum UORA allocations per trigger | Revise – Tgax editor to implement the proposed text changes found in 11-18/0029r2 that are marked with CID 16451

## Slide 4: CID 16584
16584 | Peter Loc | An HE AP has no way of knowing if there is an unassociated STA or STAs wanting to join the BSS, so it frequently allocates RA RUs with AIDs 2045 for unassociated STAs to transmit UL. This is very inefficient because most of the time, there is no STAs wanting to associate. Regardless of the setting of its dot11OFDMARandomAccessOptionImplemented, an HE STA should contend for the WM using EDCA for sending UL frames to the HE AP with which it intends to communicate, then follows the UORA procedure if its dot11OFDMARandomAccessOptionImplemented is set to true | Replace the Note with: "A non-AP STA can first contend for the WM using EDCA for sending UL frames to the AP with which it intends to communicate. " | Revise – Tgax editor to implement the proposed text changes found in 11-18/0029r2 that are marked with CID 16584

## Slide 5: Need for UORA Defaults
Association latency
  Minimize the latency
  How long must a STA wait for a UORA so that it can ASSOCREQ?
When do the follow up Triggers occur for remaining ASSOC frames?
  DTIM has competition with MCAST
  So designate broadcast TWT for this purpose, or require associating STA to remain awake
Multiple successes after a single UORA event - scheduling
  AP uses MU trigger to do the follow-up
  Need spacing of these BTWT, because AP and STAs need time between the RSNA AUTH messages to generate the next frame in the sequence
  Minimum spacing of X ms to accommodate a slow client

## Slide 6: UORA Parameters Which Need Defaults
Frequency of UORA triggers
  E.g. every Xth Beacon
OCWMIN initial backoff value
OCWMAX value
Number of RA slots specified by a single Trigger
  i.e. AID12 = 2045, i.e. unassociated STAs

## Slide 7: Rules of Behavior
BTWT or other specified timing for Association sequence exchange
Method to increase/decrease OCWMIN value
Increase/decrease in RA slots
  AP could make an assumption that Non-UORA associations are proportional to UORA associations
    Might need to consider HE subset of non-UORA associations

## Slide 8: Eligible non-AP STA
Which Non-AP STA can use UORA 2045 RA RU and for what purposes?
  E.g. based on existing parameters: Beacon and UORA Trigger RSSI values, MCS, RU allocation, Target RSSI
    AP can set these parameters to limit respondents
    Non-AP STA shall not respond if it does not expect its PPDU to be decodable based on the above parameters
  Only PREQ, Association, Authentication, pre-association Action frames allowed
    Resource request, BQR have other explicit paths
    RSNA, other post-association can be done with non-RA RU because association delivers an AID that allows a non-random allocation

## Slide 9: Proposed Values (1)
UORA Trigger with 2045 RA RU(s) occurrence
  At least once per BI, can be accompanied by non-2045 AID RUs
Association sequence Triggers
  AP to expedite subsequent Triggers for additional association exchange
    AP shall utilize DL MU responses when more than one non-AP STA has successfully transmitted an ASSOCREQ
    AP shall wait 8 ms between Triggers to allow slow STA time to compute next frame in exchange*
  Non-AP STA to remain awake for the subsequent Triggers during association exchange if it receives an acknowledgement to its ASSOCREQ
  * Delay could be a parameter in the association request

## Slide 10: Proposed Values (2)
Number of RA slots is equal to:
  Min(4, N)
    Where N is equal to 1.5 x NU_ASSOC_AVE
    Where NU_ASSOC_AVE = the average number of Non-UORA based associations within each BI during the previous 10 BI

## Slide 11: Proposed Values (3)
Default OCWMIN == 7
Default OCWMAX == 31
Modification to OCWMIN and OCWMAX
  AP can increase OCWMIN and OCWMAX using:
    OCWinc = (OCWcur + 1) x 2 – 1
  AP can decrease OCWMIN and OCWMAX using:
    OCWdec = (OCWcur + 1) / 2 - 1

## Slide 12: Proposed Values (4)
AP modification of OCWMIN and OCWMAX
  Increase OCWMIN and OCWMAX
    When the number of successfully used RA slots for a single Trigger is greater than 50% of the total number of RA slots in that Trigger
    Using previously specified increase formula
    Also allow increase at AP discretion
  Decrease OCWMIN and OCWMAX
    When the number of successfully used RA slots for a single Trigger is less than 25% of the total number of RA slots in that Trigger
    Using previously specified decrease formula

## Slide 13: Proposed Values (5)
UORA RA RU use rules
  Authentication, Association, Probe Request
  Response eligibility based on Trigger RSSI value, RU MCS, RU tone allocation, Target RSSI
    AP can set these parameters to limit respondents
    Non-AP STA shall not attempt to use an RU if it does not expect its PPDU to be decodable based on the above parameters

## Slide 14: Straw poll #1
Do you support the specification of a set of default UORA parameters and the rules for modifying and propagating those parameters and the rules for use of AID 2045 RA RUs as outlined in 11-18/0029r2 as the resolution for CID 16451 and CID 16584?
  Y
  N
  A

## Slide 15: References
[1] 802.11-2016.pdf
[2] Draft P802.11ax_D3.2.pdf