## Slide 1: ER DL Protection Sequence
Date: 2017-11-30
Authors:

## Slide 2: Abstract
Need to protect DL MU PPDU for non-AP STA that are operating at Extended Range
  E.g. AP with multiple associated STA operating at extended range due to AP/non-AP STA TX Power mismatch
STA can hear beacons, maintain association
STA can hear DL PPDU
AP has difficulty hearing STA transmissions
  Including protective CTS during MU-RTS CTS exchange
  Leads to interrupted or impossible to protect MU-RTS CTS DL MU PPDU exchanges

## Slide 3: CID xxxx
xxxx | xxxx

## Slide 4: Current Exchanges
An AP may choose to invoke either of the following two sequences:
s1: MU-RTS CTS BQRP BQR DL-MU-PPDU ETC
s2: MU-RTS CTS DL-MU-PPDU ETC
Note that both of these sequences are currently legal within the standard.

## Slide 5: Which Sequence is Right for Me?
Why would an AP choose one sequence vs the other sequence?
s2: would presumably be the normal sequence, provided that the AP decides that it already has enough information to determine the RU allocations for the DL-MU-PPDU
  i.e. already, without polling for channel info
  e.g. the AP might use pseudo-static allocations instead of desiring to have instantaneous interference information on RUs at the recipient locations

## Slide 6: Desirous of Instant Gratification
s1: would be used if the AP wants to have instantaneous interference information about recipient interference to use in creating the DL-MU-PPDU

## Slide 7: Wasted Air Reservation
Provided that the AP chooses either sequence, what happens if the AP receives no CTS in response?
Lack of receipt of CTS could be the result of many factors, including: interference at the AP; NAV set at the recipient(s); clients out of normal range, but within extended range (i.e. power difference)
Currently, within the draft, if there is no CTS received at the AP, then either sequence is aborted.
  Currently, the reception of at least one CTS is required to proceed.
If the reason for the lack of CTS response is due to extended range, then there might have been one or more CTS actually transmitted on the air, and the sequence could have proceeded, if the AP would have known this
  In fact, if one or more CTS are present, then other STAs are now shut off of the air because of NAV settings from the MU-RTS and the CTSs.
  AIRTIME IS WASTED!

## Slide 8: Improving protection for the ER case
So, how can this extended range case be improved?

## Slide 9: ER MU-RTS
AP assumes that the CTS(s) are present when the AP thinks that at least some of the recipients of the MU-RTS are ER Associates (ERA STAs)
  Note that not all of the users need to be ERA
    Assume a mix of 1 Normal Range STA and 5 ERA STA
    The NR STA might fail to send the CTS but some of the ERA STA send CTS(s) which are missed
    I.e. the sequence could still proceed if the AP had been able to know what was transmitted
  I.e. including one NR STA in the mix does not guarantee a CTS will be heard, so the allowance to proceed without hearing a CTS should not require that ALL users are ERA STA
Note that if the AP proceeds to the next PPDU in the sequence, it always does this only AFTER the expected complete CTS transmission time
  If the AP does not wait for the complete CTS transmission, it might start the next PPDU during a CTS transmission and an intended recipient will not be able to receive the BQRP or DL-MU-PPDU (or whatever is next in the sequence)

## Slide 10: MU-RTS-CTS2SELF
The AP transmits a CTS2SELF during the CTS time slot when the AP thinks that at least some of the recipients of the MU-RTS are ER Associates (ERA STAs)
  Similar to the first solution, except that the AP maintains continuous control of the medium
CTS2SELF TX power could be reduced
  E.g. as compared to the Trigger transmission
  To reduce possible interference with intended non-AP STA transmitted non-HT CTS PPDUs

## Slide 11: MU-RTS recovery with BQRP Only
Allow the AP to either abort, or to send a BQRP after a failed MU-RTS/CTS exchange, i.e. when NO CTS is received
  i.e. BQRP is sent at exactly SIFS after the end of when the CTS was expected
  Note that the AP could choose to either give up, or send a BQRP, but would not be allowed to send any other frame unless it first did a regular backoff
  i.e. the only PPDU allowed to be transmitted under these circumstances would be the BQRP, but the AP could decide to send nothing instead and give up the TXOP and resume normal backoff
We might need some limits on the BQRP recipient list
  i.e. some people might object if any BQRP were allowed with any recipient list, as opposed to being restricted to the recipients that were in the MU-RTS - if any user list were allowed some people would view this as cheating
  However, such a restriction might be too harsh, because the MU-RTS user list might be a truncated version of the originally intended DL-MU-PPDU user list

## Slide 12: Straw poll #1
Do you support the concept assumed ER STA response as described in 11-18/30?
  Y
  N
  A

## Slide 13: References
[1] 802.11-2016.pdf
[2] Draft P802.11ax_D1.2.pdf