## Slide 1: Performance Investigation on Partial OOK
Date: 2018-01-15
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In [1][2], null CP within the ON-Signal was proposed to mitigate inter- and intra-symbol interference
In [3], partial OOK which generalizes the null CP and leads to the increase in the received SNR was proposed to further enhance the performance
In this contribution, we propose possible structures of the partial OOK for low and high data rates and investigate their performance in terms of the PER

## Slide 3: Partial OOK for High Data Rate
The following structure is considered
  The length of each partial ON-signal (the length of ON duration in each 4us symbol) is denoted as t which is shorter than 2us
  We assume that partial ON-signals for both info. ‘0’ and ‘1’ are located at the same position within the 2us ON part because different positions can cause severe ISI and intra-symbol interference
    For example, consider that the partial ON-Signal for info. ‘0’ is located at the front of the symbol while the partial ON-Signal for info. ‘1’ is located at the end of the symbol
    In this case, each 4us symbol can be decoded by comparing the power between first t (duration A) and last t (duration B) parts of the symbol
    Then, performance can be degraded since duration B in the symbol for info. ‘1’ can cause severe interference in duration A in the following symbol
    Appendix A shows that partial OOK with the same position for all partial ON-signals has better performance than that with different locations according to the symbol’s information

## Slide 4: Simulation Assumption
It is assumed that each partial ON-Signal is located in the middle of each 2us ON part
  As shown in Appendix B, this partial OOK structure has similar performance with the case where all partial ON-Signals are located at the front or at the end of 2us ON parts
t is set to 1us / 0.5us
The length of the decoding window (range for measuring power) is the same as t
SYNC preamble is used for data rate signaling as well as packet detection and timing recovery
CFO and phase noise applied
Butterworth filter
  2.5MHz cut off frequency, second order
20MHz sampling rate and SNR defined in 20MHz bandwidth
TGnD and UMi NLoS channels in 2.4GHz

## Slide 5: Simulation Results
PER according to the partial ON-Signal length
TGnD Channel
UMi NLoS Channel
Partial ON-Signal can enhance the performance and the gain of the 1us partial ON-Signal is 0.9dB / 1.7dB
The shorter ON duration, the better received SNR but the more vulnerable to timing error

## Slide 6: Partial OOK for Low Data Rate (1/3)
The following options are considered
  Option 1 : two partial ON-Signals used for each 16us symbol based on the agreed symbol structure, i.e., flipping 4us ON/OFF parts
  Option 2 : only one partial ON-Signal used for each 16us symbol based on the agreed symbol structure, i.e., flipping 4us ON/OFF parts
  Option 3 : only one partial ON-Signal used for each 16us symbol based on the symbol structure with 8us ON/OFF parts similar to that of high data rate

## Slide 7: Partial OOK for Low Data Rate (2/3)
In option 1,
  The length of each partial ON-signal is denoted as T/2, i.e., the length of ON duration in each 16us symbol is T
  Similar to the high data rate case, all of the partial ON-signals are located at the same position within the 4us ON part
  For the simulation, we assume that each partial ON-Signal is located in the middle of each 4us ON part
In option 3,
  The length of each partial ON-signal (the length of ON duration in each 16us symbol) is denoted as T
  Similar to the high data rate case, all of the partial ON-signals are located at the same position within the 8us ON part
  For the simulation, we assume that each partial ON-Signal is located in the middle of each 8us ON part

## Slide 8: Partial OOK for Low Data Rate (3/3)
In option 2,
  The length of each partial ON-signal (the length of ON duration in each 16us symbol) is denoted as T
  First and last 4us parts in each 16us symbol are used for guard interval
  In addition, the partial ON-Signal for info. ‘0’ is located at the end of the second ON part while the partial ON-Signal for info. ‘1’ is located at the front of the first ON part to further mitigate the intra-symbol interference
  Any other positions can cause severe intra-symbol interference
    For example, consider that partial ON-Signals for info. ‘0’ and ‘1’ are located at the front of the second ON part and at the end of the first ON part, respectively
    Each 16us symbol can be decoded by comparing the power between duration A and B
    In this case, performance can be degraded since in the symbol for info. ‘1’, the partial ON-signal (duration A) can cause severe interference in duration B
    In Appendix C, performances are shown according to locations of partial ON-Signals in option 2

## Slide 9: Simulation Assumption
It is assumed that the following location for the partial ON-Signal is applied to each option
  For option 1, each partial ON-Signal is located in the middle of each 4us ON part
  For option 2, the partial ON-Signal for info. ‘0’ is located at the end of the second 4us ON part while the partial ON-Signal for info. ‘1’ is located at the front of the first 4us ON part
  For option 3, each partial ON-Signal is located in the middle of each 8us ON part
T is set to 4us / 2us / 1us / 0.5us
The length of the decoding window is the same as T
Others are described in slide 4

## Slide 10: Simulation Results (1/4)
PER for OP1 according to the partial ON-Signal length
TGnD Channel
UMi NLoS Channel
4us ON duration in each symbol (i.e., two 2us partial ON-Signals in each symbol) seems to be the best (gain 0.6dB / 0.6dB)
Extremely short ON durations cause severe performance degradation since it is quite vulnerable to timing error

## Slide 11: Simulation Results (2/4)
PER for OP2 according to the partial ON-Signal length
TGnD Channel
UMi NLoS Channel
2us partial ON-Signal seems to be the best (gain 1.1dB / 1.3dB)
1us / 4us partial ON-Signals also have comparable performance

## Slide 12: Simulation Results (3/4)
PER for OP3 according to the partial ON-Signal length
TGnD Channel
UMi NLoS Channel
2us partial ON-Signal seems to be the best (gain 1.3dB / 1.4dB)
1us / 4us partial ON-Signals also have comparable performance

## Slide 13: Simulation Results (4/4)
PER comparison with 2us partial ON-Signal
TGnD Channel
UMi NLoS Channel
For option 1, two 2us partial ON-Signals are considered in each 16us symbol
All of the options are better than the normal OOK
Option 3 seems the best and option 2 is comparable

## Slide 14: Conclusion
We have proposed several partial OOK symbol structures for low and high data rates and investigated their performance
Partial OOK can enhance the performance for both low and high data rates because much higher received SNR can be achieved
However, the length of the partial OOK signal needs to be properly set for better performance
  The partial OOK with extremely short length of the partial ON-Signal can aggravate the performance and have even worse performance than that of the normal OOK because it requires quite accurate timing
  1us and 2us partial ON-Signals seem to be suitable for high and low data rates, respectively
In addition, for the low data rate case, we could come up with the current symbol structure based partial OOK (i.e., option 2) which offers comparable performance

## Slide 15: References
[1] IEEE 802.11-17/1347r3 Symbol Structure
[2] IEEE 802.11-17/1390r1 Blank GI choices under Timing Errors
[3] IEEE 802.11-17/1673r1 Partial OOK – Generalizing the Blank GI Idea

## Slide 16: Appendix

## Slide 17: Appendix A – Performance Comparison According to Locations of Partial ON-Signals in High Data Rate
Options
  Case 1 : Both partial ON-Signals for info ’0’ and ‘1’ are located in the middle of the 2us ON part
  Case 2 : Partial ON-Signals for info ’0’ and ‘1’ are located at the front and at the end of the 2us ON part, respectively
  Case 3 : Partial ON-Signals for info ’0’ and ‘1’ are located at the end and at the front of the 2us ON part, respectively

## Slide 18: Appendix A – Performance Comparison According to Locations of Partial ON-Signals in High Data Rate
PER
TGnD Channel
UMi NLoS Channel

## Slide 19: Appendix B – Performance Comparison According to Locations of Partial ON-Signals in High Data Rate
Options
  Case 1 : Partial ON-Signal in the middle of the 2us ON part
  Case 2 : Partial ON-Signal at the front of the 2us ON part
  Case 3 : Partial ON-Signal at the end of the 2us ON part

## Slide 20: Appendix B – Performance Comparison According to Locations of Partial ON-Signals in High Data Rate
PER
TGnD Channel
UMi NLoS Channel

## Slide 21: Appendix C – Performance Comparison According to Locations of Partial ON-Signals in Low Data Rate
Options
  Case 1 : Partial ON-Signals for info ’0’ and ‘1’ are located at the end and at the front, respectively
  Case 2 : Both partial ON-Signals for info ’0’ and ‘1’ are located in the middle
  Case 3 : Partial ON-Signals for info ’0’ and ‘1’ are located at the front and at the end, respectively

## Slide 22: Appendix C – Performance Comparison According to Locations of Partial ON-Signals in Low Data Rate
PER
TGnD Channel
UMi NLoS Channel