## Slide 1: Options for Sync Field Bit Sequence
Date: 2018-01-12
Authors:

## Slide 2: Abstract
In another presentation [1] we showed that a 2 µs Sync Bit Duration is superior to a 4 µs duration
Here we investigate the optimum 32-bit sequence, using this 2 µs Sync Bit Duration
We consider several factors in this evaluation
  Good Correlation Properties
  Good PER Simulation Properties
  Avoid excessively long “Maximum Off Duration”

## Slide 3: Optimization with Maximum “Off Time” Constraint
The optimized 32-bit sequence found in [1] has a sequence of five “ones” leading to an maximum off time of 10 µs
Let us find a sequence that has at most three zeros or ones, such that the maximum off time is 6 µs
For reference here is the Maximum Off Time in the Data Field
  High Data Rate maximum off Time Data Field = 4 µs
  Low Data Rate maximum off Time Data Field = 8 µs
The following 32-bit sequence is proposed
S=[0, 1, 1, 1, 0, 1, 0, 1, 0, 0, 1, 0, 1, 0, 0, 1, 0, 1, 1, 0, 0, 1, 1, 0, 1, 1, 0, 0, 0, 1, 1, 0]

## Slide 4: Options for 32-bit S Sequence
Optimized 31-bit MLS with prepended zero [1]
S1 = [0, 1, 1, 1, 0, 1, 0, 1, 0, 0, 0, 0, 1, 0, 0, 1, 0, 1, 1, 0, 0, 1, 1, 1, 1, 1, 0, 0, 0, 1, 1, 0]
Our Proposal
S2 = [0, 1, 1, 1, 0, 1, 0, 1, 0, 0, 1, 0, 1, 0, 0, 1, 0, 1, 1, 0, 0, 1, 1, 0, 1, 1, 0, 0, 0, 1, 1, 0]
Sequence proposed by Justin Jia Jia and Ming Gang [2]
S3 = [1, 0, 1, 0, 0, 0, 1, 1, 0, 1, 1, 0, 1, 1, 1, 1, 0, 0, 0, 0, 1, 0, 0, 1, 1, 1, 0, 0, 0, 1, 0, 1]
Sequence proposed by Rui Cao, Sudhir Srinivasa, Hongyuan Zhang [3]
S4 = [0, 0, 0, 1, 0, 1, 1, 0, 1, 0, 1, 0, 0, 0, 1, 1, 1, 0, 1, 0, 1, 1, 1, 1, 0, 0, 1, 0, 0, 1, 1, 0]

## Slide 5: Maximum Off Time in Sync Field
S Sequence | Maximum Off Time (µs)
S1 | 10
S2 | 6
S3 | 8
S4 | 8

## Slide 6: Correlation Metrics
S Design | ACMetric(Short) | CCMetric(Short, Long) | ACMetric(Long) | CCMetric(Long, Short)
S1 | 5.3 | 5.3 | 2 | 16
S2 | 5.3 | 4 | 2 | 6.4
S3 | 8 | 4 | 2 | 8
S4 | 5.3 | 5.3 | 2 | 8

## Slide 7: Simulation – Low Rate (AWGN)

## Slide 8: Simulation – High Rate (AWGN)

## Slide 9: Simulation – Low Rate (Model D)

## Slide 10: Simulation – High Rate (Model D)

## Slide 11: Simulation Summary
S Sequence | (10% PER) SNR Low Rate AWGN(dB) | (10% PER) SNR High Rate AWGN (dB) | (10% PER) SNR Low Rate Model D (dB) | (10% PER) SNR High Rate Model D (dB)
S1 | -7.24 | -3.16 | -0.92 | 3.71
S2 | -7.31 | -3.16 | -0.97 | 3.70
S3 | -7.32 | -3.17 | -0.96 | 3.73
S4 | -7.34 | -3.17 | -0.92 | 3.89
In AWGN and Low Rate with Channel Model D the results are all very similar
In High Rate with Channel Model D
  S1, S2, and S3 are results are similar
  S4 results are slightly worse

## Slide 12: Conclusions
Sync Maximum Off Time
  S1 has a maximum off time of 10 µs
  S2 has a maximum off time of 6 µs
  S3 and S4 have maximum off times of 8 µs
Simulation Results
  Results are almost identical
  In Channel Model D at Low Rate (an important case) S2 and S3 have the best results
Recommendation
  Choose either S2 or S3

## Slide 13: Straw Poll
Do you support using the following 32-bit S sequence in Sync field?
Option 1
S2 = [0, 1, 1, 1, 0, 1, 0, 1, 0, 0, 1, 0, 1, 0, 0, 1, 0, 1, 1, 0, 0, 1, 1, 0, 1, 1, 0, 0, 0, 1, 1, 0]
Option 2
S3 = [1, 0, 1, 0, 0, 0, 1, 1, 0, 1, 1, 0, 1, 1, 1, 1, 0, 0, 0, 0, 1, 0, 0, 1, 1, 1, 0, 0, 0, 1, 0, 1]
Voting
You can Vote Yes, No, or Abstain on each Option

## Slide 14: References
Steve Shellhammer and Bin Tian, “Sync Field Bit Duration,” 802.11-18/0122r0, January 2018
Justin Jia Jia and Ming Gan, “A Simple WUR Preamble Design,” IEEE 802.11-17/1636r0, November 2017
Rui Cao, Sudhir Srinivasa, Hongyuan Zhang, “WUR Dual SYNC Design and Performance,” IEEE 802.11-17/1618r0, November 2017