## Slide 1: AP operation regarding PCR schedule
Date: 2018-01-15
Authors:

## Slide 2: Recap: PCR schedule suspension in WUR Mode
PCR scheduling schemes require PS STA to wake-up periodically
  This mandatory behavior might prevent non-AP STA in WUR Mode to stay in doze state for long duration and increase the power consumption
For this reason, we have agreed the following in the SFD:
  When a non-AP STA enters WUR Mode,
    the existing negotiated service period between AP and non-AP STA for the non-AP STA’s PCR schedule (e.g. TWT, schedule for WNM Sleep Mode) is suspended:
    STA is not required to wake up during the service period if the service period is suspended.

## Slide 3: AP operation regarding PCR schedule
In some PCR scheduling schemes, AP is required to transmit a frame for every negotiated service period
  In Trigger-enabled TWT,
    AP shall schedule for transmission of a Trigger frame for the TWT requesting STA within each TWT SP
  In TIM Broadcast,
    AP shall transmit one or two TIM frames per TIM Broadcast Interval
It is hard to expect a STA in WUR Mode to wake up for the periodic transmission
  The periodic transmission could be waste of resource

## Slide 4: Proposal
Regarding PCR schedule, it is recommended to have a clear instruction on AP’s behavior when a STA enters WUR Mode
Proposal:
  When a WUR non-AP STA is in WUR Mode, then:
    AP may not schedule for transmission corresponding to the negotiated PCR schedule of the non-AP STA
      (e.g., UL MU scheduling in trigger-enabled TWT or TIM Broadcast)

## Slide 5: Strawpoll
Do you support the following?
When a WUR non-AP STA is in WUR Mode, then:
  AP may not schedule for transmission corresponding to the negotiated PCR schedule of the non-AP STA
    (e.g., UL MU scheduling in trigger-enabled TWT or TIM Broadcast)