## Slide 1: Short WUR Frame
Date: 2018-02-28
Authors:
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | liwenchu@marvell.com

## Slide 2: Recap of WUR (Low Power Wakeup) Frame
The following WUR frames are defined for 11ba:
  Beacon.
  Waking up.
  Discovery.
  Vendor Specific.
In order to save the medium time, BSSID is not really transmitted.
  The STA and AP add the Embedded BSSID when calculating CRC.
Frame Control | Address | Embedded BSSID | TD Control | Frame Body
Compute CRC
Frame Control | Address | TD Control | Frame Body | FCS (CRC)
Transmit WUR frame

## Slide 3: Issue of WUR (Low Power Wakeup) Frame
The WUR frame is too long
  If FCS has 8 bits, the TX time of mandatory WUR frame is 40*8us+PHY Header TX time
Observation: an associated STA can figure out both BSSID and RX address if the WUR frame is addressed to it.
  The frame Tx and Rx per the Embedded BSSID doesn’t work for the frames out side of BSS.
Frame Control | Address | TD Control | Frame Body | FCS (CRC)
Transmitted WUR frame
8
12
12
8
Frame Control | Address | TD Control | FCS (CRC)
Transmitted WUR frame
8
12
12
8
Mandatory Frame
Optional Frame
variable

## Slide 4: Further Optimization of WUR (Low Power Wakeup) Frame
If a frame is inside BSS, both Address and BSSID can be removed from the WUR frame.
Frame Control | Embedded Address | Embedded BSSID | TD Control | Frame Body
Compute CRC
Frame Control | TD Control | Frame Body | FCS (CRC)
Transmit WUR frame
If a STA receives a WUR frame with Frame Control indicating a inside BSS.
  Based on Frame Control, the STA uses its allocated address (unicast, broadcast or multicast) and associated AP’s BSSID and the received frame content (header and body) to calculate the FCS, if the FCS is wrong, the STA discards the frame. Otherwise the STA accepts the frame.
The frames which are outside BSS have similar format:
Frame Control | TD Control | Frame Body | FCS (CRC)
Outside BSS Frame Format