## Slide 1: BSSID Information in FCS
Date: 2018-02-28
Authors:
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | liwenchu@marvell.com

## Slide 2: Recap of WUR (Low Power Wakeup) Frame
The following WUR frames are defined for 11ba:
  Beacon.
  Waking up.
  Discovery.
  Vendor Specific.
In order to save the medium time, BSSID is not really transmitted.
  The STA and AP add the Embedded BSSID when calculating CRC.
Frame Control | Address | Embedded BSSID | TD Control | Frame Body
Compute CRC
Frame Control | Address | TD Control | Frame Body | FCS (CRC)
Transmit WUR frame

## Slide 3: Issue of WUR (Low Power Wakeup) Frame
The WUR frame can be either frame transmitted inside BSS or outside of BSS:
  The frames inside the BSS include Beacon, Wakeup, Vendor Specific.
  The frames outside the BSS include Discovery, possibly include Vender Specific or Beacon frame.
The receivers can’t figure out the BSSID if the frames are outside of BSS.
  The frame Tx and Rx per the Embedded BSSID doesn’t work for the frames out side of BSS.
Frame Control | Address | Embedded BSSID | TD Control | Frame Body
Compute CRC
Frame Control | Address | TD Control | Frame Body | FCS (CRC)
Transmit WUR frame

## Slide 4: Refined WUR (Low Power Wakeup) Frame
If the Frame Type can be used to decide whether a frame is inside BSS or outside BSS, the Frame Type can decide whether Embedded BSSID is used for FCS calculation.
  If a frame is outside BSS, the frame format and FCS configuration is
Frame Control | Address | Embedded BSSID | TD Control | Frame Body
Compute CRC
Frame Control | Address | TD Control | Frame Body | FCS (CRC)
Transmit WUR frame
Frame Control | Address | TD Control | Frame Body | FCS (CRC)
Compute CRC and Transmit WUR frame
  If a frame is inside BSS, the frame format and FCS configuration is
If the Frame Type can’t be used to decide whether a frame is inside BSS or outside BSS, e.g. a vendor specific frame may be transmitted to an associated STA/AP or to an unassociated STA/AP, one bit in Frame Control field or other bit in the frame can decide whether Embedded BSSID is used for FCS calculation.
  If a frame is outside BSS, the frame format and FCS configuration is
Frame Control | Address | Embedded BSSID | TD Control | Frame Body
Compute CRC
Frame Control | Address | TD Control | Frame Body | FCS (CRC)
Transmit WUR frame
Frame Control | Address | TD Control | Frame Body | FCS (CRC)
Compute CRC and Transmit WUR frame
  If a frame is inside BSS, the frame format and FCS configuration is