## Slide 1: Performance Investigation on Partial OOK Follow-up
Date: 2018-03-05
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In [1], various partial OOK structures were proposed and PER performance was investigated considering the sampling rate of 20MHz
  Partial OOK outperforms the current OOK structure in terms of PER because of reduced intra- and inter-symbol interference and better received SNR
For low power consumption, the wake-up receiver needs to use much lower sampling rate such as 4MHz
In this case, the number of samples available for decoding is significantly reduced especially for the partial OOK and thus a timing error can severely aggravate the partial OOK performance
In this contribution, we investigate whether the partial OOK is still beneficial to PER even in the case with the sampling rate of 4MHz

## Slide 3: Recap on Partial OOK Structures in [1]
High data rate
Low data rate
  Option 1
  Option 2
  Option 3

## Slide 4: Simulation Assumption
High data rate
  Each partial on-signal is located in the middle of each 2us on-part
  t is set to 1us / 0.5us
  The length of the decoding window (range for measuring power) is the same as t
Low data rate
  For option 1, each partial on-signal is located in the middle of each 4us on-part
  For option 2, the partial on-signal for info. ‘0’ is located at the end of the second 4us on-part while the partial on-signal for info. ‘1’ is located at the front of the first 4us on-part
  For option 3, each partial on-signal is located in the middle of each 8us on-part
  T is set to 4us / 2us / 1us / 0.5us
  The length of the decoding window is the same as T
Sync preamble for data rate signaling as well as packet detection and timing recovery
CFO of 200ppm and phase noise for 20uW power consumption as in [5]
Butterworth filter with 2.5MHz cut off frequency, second order
4MHz sampling rate and SNR defined in 20MHz bandwidth
TGnD and UMi NLoS channels in 2.4GHz

## Slide 5: Simulation Results
High data rate
TGnD Channel
UMi NLoS Channel
At 10% PER, the gain of 1us partial on-signal is 0.3dB / 1.5dB

## Slide 6: Simulation Results
Low data rate
TGnD Channel
UMi NLoS Channel
In each option, partial OOK with 2us partial on-signal (two 2us partial on-signals for option 1) has the best performance as shown in Appendix
Figures compare the performance between the current OOK structure and partial OOK options with 2us partial on-signal
Option 2 and 3 have good performance and the gain is 0.9dB / 1dB at 10% PER

## Slide 7: Discussion
The partial OOK with the sampling rate of 4MHz can enhance the performance although it is even more vulnerable to the timing error than that with the sampling rate of 20MHz
  Similar to the 20MHz sampling rate case, 1us and 2us partial on-signals have the best performance for the high and low data rates, respectively
In [2], the required SNR was analyzed at 10% PER to guarantee the range requirement for WUR
  Even in 2.4GHz, the low data rate with the current OOK structure cannot guarantee the range
  In 5GHz, much lower SNR is required due to the harsh regulation
We need an alternative approach to further improve the performance of the current WUR
  Partial OOK can be one of the approaches

## Slide 8: Straw Poll #1
Do you agree to add the following in the TGba SFD?
  Partial OOK which shortens the on-signal duration which is defined in the SFD (4us) by a half length may be applied to the WUR Data field for the low data rate
    Power of the shortened on-signal duration can be boosted up to two times
Y/N/A : 18/25/7

## Slide 9: Straw Poll #2
Do you agree to add the following in the TGba SFD?
  Partial OOK which shortens the on-signal duration by a half length may be applied to the WUR Data field for the high data rate
    Power of the shortened on-signal duration can be boosted up to two times

## Slide 10: References
[1] IEEE 802.11-18/0071r0 Performance Investigation on Partial OOK
[2] IEEE 802.11-17/0965r2 Data Rate for Range Requirement in 11ba

## Slide 11: Appendix
PER for option 1 of the low data rate
TGnD Channel
UMi NLoS Channel

## Slide 12: Appendix
PER for option 2 of the low data rate
TGnD Channel
UMi NLoS Channel

## Slide 13: Appendix
PER for option 3 of the low data rate
TGnD Channel
UMi NLoS Channel