## Slide 1: BSS parameters update notification follow up
Date: 2018-03-01
Authors:

## Slide 2: Recap
In [1] and [2], we agreed that
  A counter subfield of a WUR Wake Up frame is defined as an unsigned integer initialized to 0, that increments when a critical update to the PCR’s BSS parameters has occurred. The size of the counter subfield is TBD.
  In this contribution, we fix TBD issues regarding Counter subfield, including
  PCR’s BSS parameters update procedure
  The location and size of counter field

## Slide 3: PCR’s BSS parameters update procedure
The AP shall increase the value of the Counter field in the next transmitted WUR Wake Up frame(s) when a critical update occurs to any of the elements inside the Beacon frame. The following events shall classify as a critical update:
  Inclusion of a Channel Switch announce element
  Inclusion of an Extended Channel Switch announce element
  Inclusion of a Wide Bandwidth Channel Switch element
  Inclusion of an Operating Mode Notification element
  Inclusion of BSS Color Change Announcement element
  Modification of the EDCA parameters
  Modification of the HT Operation element
  Modification of the VHT Operation element
  Modification of the HE Operation element
  Modification of TWT element
  An AP may classify other changes in the Beacon frame as critical updates and among these updates can be included those that are described in 11.2.2.17 (TIM Broadcast).
  The WUR STA shall be awake to receive the next Beacon frame that is transmitted at a TBTT or shall queue for transmission a Probe Request frame when it receives a Counter field that contains a value that is different from the previously received Counter field.
  AP shall not send a wake up frame a non-DFS channel to wake up the STA which operates in the DFS channel if AP includes quiet element in the beacon frame

## Slide 4: Counter field
We propose to use 4 bits for Counter field in a wake up frame instead of 1 bytes check beacon field based on the following facts
  Each WUR STA can make use of the counter field in each wake up frame, although it is not destined receiver of the wake up frame.
  Moreover, the size of wake up frame is limited
  TD control field of a WUR Wake Up frame contains Counter subfield and reserved subfield as illustrated in Figure 9-xx (TD control field of WUR Wake up frame).
B0 B3 | B3+1 B11
Counter | Reserved
4 bits | TBD
Figure 9-xx – TD control field of WUR Wake up frame | 

## Slide 5: Reference
[1] 11-17-1368-02 BSS parameters update notification
[2] Draft P802.11ba_D0.1

## Slide 6: SP 1
Do you agree the following text
AP shall not send a WUR wake up frame in a non-DFS channel to wake up a WUR STA which operates in the DFS channel if the AP includes a Quiet element in the beacon frame as defined in subclause 11.9

## Slide 7: SP 2
Do you agree the following text
The AP shall increase the value of the Counter field in the next transmitted Broadcast WUR Wake Up frame when a critical update occurs to any of the elements inside the Beacon frame. The following events shall classify as a critical update:
  Inclusion of a Channel Switch announce element
  Inclusion of an Extended Channel Switch announce element
  Inclusion of a Wide Bandwidth Channel Switch element
  Inclusion of an Operating Mode Notification element
  Inclusion of BSS Color Change Announcement element
  Modification of the EDCA parameters
  Modification of the HT Operation element
  Modification of the VHT Operation element
  Modification of the HE Operation element
  Modification of TWT element
  An AP may classify other changes in the Beacon frame as critical updates and among these updates can be included those that are described in 11.2.2.17 (TIM Broadcast).

## Slide 8: SP 3
Do you agree the following text
  The WUR STA that receives a Counter field that contains a value that is different from the previously received Counter field shall follow the procedure defined in 11.2.3.17 subject to its PCR delay constraints.

## Slide 9: SP 4
Do you agree the following text
  The TD Control field of a Broadcast WUR Wake Up frame contains a Counter subfield. The size of Counter subfield is TBD

## Slide 10: Back up

## Slide 11: Introduction
Primary functions of a WUR Beacon is proposed in [1-5] are
  Advertize the presence of AP
  Synchronize between AP and the STA when the STA’s primary connectivity radio (PCR) is off
  Provide the WUR STA the minimal necessary set of information
  Here we consider PCR’s BSS parameters update info as one minimal necessary set of information
  Some battery powered STA’s PCR may sleep for several days or months with the help of wake up receiver
  However, BSS Parameters may change during the sleep time of the STA’s PCR, such as channel and EDCA parameters

## Slide 12: Motivation
It can help the STA’s PCR make a correct transmission to provide BSS parameters update info
However, it is impossible to provide each changed BSS parameter through the WUR beacon
  Size of the WUR Beacon needs to be controlled due to low PHY rate (e.g., 250Kbps)
  Each BSS parameter occupies multiple bytes, such as 20 bytes EDCA Parameter Set element, requiring 640 us for transmission

## Slide 13: BSS parameters update notification
Generally, the STA knows all the necessary Info after association
When there are changes in some BSS parameters which can not be conveyed by using the WUR beacons due to size limitation, we propose to use a simple indication to alert the STA in WUR mode get on synch with new Info
  Propose to use a change number (CN) indication (4 or 8 bits) carried in WUP and WUR beacon
  After being informed the changed BSS parameters, the STA can either wake up to decode the 802.11 beacon at TBTT
  Or retrieve updated information by using probe request
  Some similar designs were provided for 11ah devices and TIM STAs
  Change sequence field in short beacon frame was proposed to provide 11ah STAs the change of system info
  Check beacon field in broadcast TIM frame was proposed to provide TIM STAs the critical updates on BSS parameters

## Slide 14: BSS parameters update notification
  Initialize CN to 0 at the beginning, and increase by one when a critical update occurs to any PCR’s BSS parameters
  a) Inclusion of Channel Switch announce element
  b)Inclusion of Extended Channel Switch announce element
  b) Modification of the EDCA parameters
  c) Inclusion of a Quiet element
  e) Modification of the HT Operation element
  f) Inclusion of an Operating Mode Notification element
  g) Inclusion of a Quiet Channel element
  h) Modification of the VHT Operation element …
  When the STA receives a change number that is different from the local stored change number, it may
  queue for transmission by sending a Probe Request frame when it is awake and wait for Probe Response frame which contains updated BSS parameters or receive the next beacon frame
  and update the local stored change number
Beacon
(CN=3)
Probe request
Probe response
Local CN=2
AP
STA
Ack
Ack

## Slide 15: Reference
[1] 11-16-1445-00 Overall MAC Procedure for WUR
[2] 11-16-1504-00 Discussion of WUR Packets Design
[3] 11-16-1217-00 WUR-based Broadcast Reference Signal
[4] 11-16-1501-00 AP Discovery using WUR
[5] 11-17-0343-03 ba WUR Beacon