## Slide 1: TD Control field with Response indication in WUR frame
Date: 2018-02-22
Authors:
Name | Affiliation | Address | Email
Kaiying Lv | ZTE Corp. | No.9 XiFeng Road, Xi’An, China | lv.kaiying@zte.com.cn
Bo Sun |  |  | Sun.bo1@zte.com.cn

## Slide 2: Introduction
  IEEE 802.11ba spec shall define a mechanism to wake up multiple WUR mode STAs (e.g., multi-user wake-up frame)[1]
The AP can send a Trigger Frame in 11ax to solicit response frames from one or more STAs after sending a wake-up packet to the STA(s).
IEEE 802.11ba shall define Information Element for WUR capability that include following information
  PCR transition delay from doze state to awake state after receiving wake-up frame at STA side
How to efficiently wake up WUR STAs and respond to the WUF is discussed in this proposal.

## Slide 3: Motivation
  AP should be able to make decision the way for WUR STAs to respond to the WUR packet in PCR in order to efficiently control the medium
    Solicited/ triggered response by the AP
    Unsolicited response by contending the medium using EDCA
PCR Transition Delay should be considered when wake up response in PCR is solicited by the AP
    Aligning awake time of WUR STAs with different PCR transition delay would be helpful to reduce power consumption
  Channel access efficiency should be considered when wake up response is unsolicited by contending the medium using EDCA
    Stagger channel access contention from multiple WUR STAs when sending wake up response would be helpful to reduce contention collision

## Slide 4: Analysis (1/2)
PCR transition delay should be included in the overall delay of WUF response solicited by the AP in PCR.
  An AP would not send a trigger frame until all WUR STAs solicited to wake up turn into awake state
  AP may not be able to schedule the trigger if WUR STAs with shorter PCR transition delay start channel contention before receiving AP’s trigger
  Even if indicated solicited response, WUR STAs with shorter PCR transition delay have to wait a long time to receive the trigger frame from the AP due to longer PCR transition delay of other WUR STAs.
  Therefore an AP should indicate an overall delay in an WUF to align multiple WUR STAs based on their PCR transition delay.

## Slide 5: Analysis (2/2)
A random delay before turning on its PCR should be included in the overall delay when contending to send a WUF response in PCR.
  WUR STAs may randomly delay to turn on its PCR based on overall delay requirement after receiving the WUF so that they could be randomly in awake state at different time to send the response with less channel contention [2]
  Therefore an AP should indicate a delay window in a WUF to allow multiple WUR STAs randomly turn on their PCR after receiving a WUF.

## Slide 6: Proposal (1/3)
A unicast / multicast wake-up packet may include the wake response mode indication:
  A wake up response mode indication is to indicate solicited or unsolicited response mode
    Solicited response mode: An AP will send a frame (eg. trigger frame) to solicit the wake up response from the WUR STA(s)
    Unsolicited response mode: An WUR STA will contend to send a wake up response (eg. PS-Poll, QoS Null etc.)
  1bit in TD control field in unicast/multicast WUF can be used for wake up response mode indication

## Slide 7: Proposal (2/3)
A unicast / multicast WUF may also include wake up delay information:
  A wake up delay indication is to indicate for an WUR STA to delay to turn on its PCR after receiving its WUF.
    A specific time offset of average PCR transition delay (eg.10ms) to delay after receiving WUF if the WUR STAs will be solicited by AP’s trigger to send the wake up response
    A delay window to for a WUR STA to randomly select a delay time after receiving WUF if WUR STA will contend the medium to send the wake up response
  Option 1: 2~3 bits in TD control field in unicast/multicast WUF can be used for wake up delay indication
    eg. Value “00” means no extra delay;
    eg. value “01” mean 0.5ms time offset of average PCR transition delay for solicited response
    eg. value “01” mean 0.5ms delay time window for unsolicited response
  Option 2: 1 bits in TD control field in unicast/multicast WUF can be used for wake up delay indication.
    The delay offset and delay window can be indicated as WUR operation parameter through PCR
    No overhead in WUF but it cannot delicately adjust delay parameters

## Slide 8: Proposal (3/3)
Example of wake up delay shown as below
  STA1 and STA2 have PCR transition delay of 10ms indicated in WUR capability element
  STA3 and STA4 have PCR transition delay of 8ms indicated in WUR capability element
  A multicast WUF indicates solicited response mode and 10ms delay time ( delay time offset set to “0” based on average PCR transition delay of 10ms)
    STA1 and STA2 turn on their PCR right after receiving the WUF
    STA3 and STA4 turn on their PCR 2ms after receiving the WUF

## Slide 9: Conclusion
Wake up response mode indication is proposed to indicate the solicited/unsolicited response to a WUF in PCR.
The wake up delay for solicited/unsolicited response is proposed to improve channel access efficiency.
We suggest that an AP indicate the wake up response mode and its corresponding wake up delay information in order to have better utilization of the resource and improve WUR STAs’ power efficiency.

## Slide 10: Straw Poll 1
Do you support adding the following to 11ba SFD?
A wake up response mode indication shall be carried in the unicast/multi-user WUF to indicate solicited or unsolicited response in PCR.
  Y:
  N:
  A:

## Slide 11: Straw Poll 2
Do you support adding the following to 11ba SFD ?
A wake up delay indication shall be carried in the unicast/multi-user WUF to indicate wake up delay information.
  Y:
  N:
  A:

## Slide 12: Straw Poll 3
Do you support adding the following to 11ba SFD ?
TD control field in a unicast/multi-user wake up frame can be used for indicating the delay offset / delay window to indicate wake up delay information.
  Y:
  N:
  A:

## Slide 13: References
[1] 11-17/0575r9 “spec framework”, Po-kai Huang
[2] 11-17/1359r0 “considerations for wur response”