## Slide 1: Discussion on Group ID Structure
Date: 2018-3-2
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
Background
 | Frame Control | Address | TD Control
bits | 8 | 12 | 12
MAC Header | Frame Body | FCS
Address field | WUR frame
Wake Up ID | Unicast wake up
Group ID | Multicast wake up
Transmit ID | Beacon or broadcast wake up
OUI1 | Vendor specific
R.4.2.F of 11ba SFD [2]: AP may negotiate one or more Group IDs with a STA through PCR using WUR Action frame during WUR negotiation and WUR mode signaling procedure
  The assigned Group ID is used in a wake-up frame
  The details for Group ID (e.g., ID structure, etc.) are TBD.
This submission further addresses the Group ID structure based on [3].
WUR Wake-up frame format

## Slide 3
Proposal
Example addressing space in the Address field
The value range of Group ID is a subset of consecutive values of the Address field.
  For each of Group IDs assigned by WUR AP to WUR STA during WUR negotiation and WUR signaling procedure, it is enough to signal only 8 LSBs of the Group ID in WUR Mode element, instead of 12-bit Group ID, assuming up to 256 groups are supported.
  Pros: MAC overhead is reduced especially in case of a large number of groups the WUR STA belongs to.
The value range of Group ID is configurable.
  4 MSBs of Group ID are advertised in the WUR Operation element to indicate value range of Group ID.
    Note: WUR Operation element advertises WUR parameters common to all WUR STAs [4]
  Pros: Probability of Group ID collision in the BSSs of neighboring APs can be minimized, which help WUR STA to filter multicast WUR Wake-up frames properly.

## Slide 4
Proposed Changes on WUR Mode & WUR Operation elements
WUR Mode element transmitted by WUR AP
WUR Operation element
WUR STA is able to know its assigned Group IDs from the Number of Groups field and Group ID Tuples field of WUR Mode element as well as Group ID Range Indication field of WUR Operation element.

## Slide 5: Reference
Draft P802.11ba_D0.1
IEEE 802.11-17/0575r9, 11ba Spec Framework
IEEE 802.11-18/0061r3, WUR Wake Up frame format
IEEE 802.11-18/0408r0, Spec Text for Channel Access, Duty Cycle Operation and WUR Mode

## Slide 6: SP 1
Do you support to add the following into 11ba SFD?
  The value range of Group ID is a subset of consecutive values of the Address field
  Y/N/A:

## Slide 7: SP 2
Do you support to add the following into 11ba SFD?
  The value range of Group ID is configurable.
  Y/N/A: