## Slide 1: Dynamically Changing WUR ID follow up
Date: 2018-03-02
Authors:

## Slide 2: Abstract
Battery Draining Attacks may be a threat for ultra-low power WUR STA devices.
  One way to do such an attack is address spoofing
  Two options to solve the problem initially discussed in [1]
This contribution is a follow up of [1], to further discuss of the two options how to change dynamically WUR ID for associated STAs and pros/cons of those options

## Slide 3: Option 1: “Implicit” unicast WUR ID
AP signals the initial WUR ID and a random value in WUR negotiation phase in a secure way, next WUR ID is calculated at both AP and STA: Next WUR ID = Hash(Prev WUR ID + random value) e.g. every time just before STA is going to WUR sleep
  The purpose of the random value is to make attacker hard to find the right WUR ID sequence
  Both the STA and the AP implement the 802.11ba specified hash function and run it to determine the next WUR ID
  No WUR ID signaling needed after the negotiation phase
  WUR IDs may temporarily collide due to the nature of the hash algorithm

## Slide 4: Option 1 – Overview example
AP
STA
WUR negotiation
PCR WUR
WUR PCR
WUR_ActionFrame(WID0, random value)
Calculate WID1
Calculate WID1
WUF(WID0)
Calculate WID2
Calculate WID2
WUF(WID1)
WUF(WID2)

## Slide 5: Option 2: “Explicit” unicast WUR ID
AP signals to STA the next unicast WUR ID explicitly e.g. every time just before STA is going to WUR sleep
  The complexity of WUR ID assignment is fully on AP side
  AP sends the next WUR ID (action frame through PCR) to STA

## Slide 6: Option 2 – Overview example
AP
STA
WUR negotiation
PCR WUR
WUR PCR
WUR_ActionFrame(WID0)
WUF(WID0)
WUF(WID1)
WUF(WID2)
WUR_ActionFrame(WID1)
WUR_ActionFrame(WID2)
Assign WID1
Assign WID2
Adopt WID1
Adopt WID2

## Slide 7: Option 1&2 Pros/Cons
 | Implicit | Explicit
802.11ba specifies the algorithm to generate WUR IDs | YES | NO
WUR ID signaling overhead after association | NO | YES
Increase of STA complexity | YES | NO
WUR ID collisions possible within BSS | YES | NO

## Slide 8: References
[1] 11-18-0358-00-00ba-dynamically-changing-wur-id.pptx

## Slide 9: Straw poll
Do you agree that STA WUR ID should be able to change dynamically to fight address spoofing and the solution should be based on the idea of:
  Yes for Option 1 (implicit WUR ID)
  Yes for Option 2 (explicit WUR ID)
  Yes for some other solution
  No solution needed, problem is not valid
  Abstain