## Slide 1: Evaluation of WUR sync sequence
Date: 2018-03-05
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
March 2018

## Slide 2: Introduction
In the last meeting, we discussed the many issues related to WUR sync field. And, followings were decided
  The duration of each bit in the SYNC field is 2us
  The contiguous OFF period of SYNC field is no more than 8 us
Based on those guidelines, for deciding the specific 32-bit sequence, we evaluate the 32-bit sequence for WUR sync sequence with following criteria
  Correlation property
  Performance of PER and Timing error rate

## Slide 3: Consideration for sync sequence
Maximum OFF duration
  As described in [1], the short off duration can be a help to fast AGC gain convergence. so, to prevent the long OFF time in SYNC field, the consecutive zeros may be limited as at most three in sync sequence
Correlation property and timing error performance
  Because the correlation metric is used to identify the multiple data rates, it is required the high correlation property of sync sequence for exact detection of data rate and this property also can ensure the timing error performance
    The AC Metric described in [2] may be considered for evaluation of the correlation property
Start of sequence
  For the detection of WUR signal, it is desirable that sequence does not begin with consecutive zero and sequence can start with some repetitive pattern for efficient AGC operation

## Slide 4: Options for Sync sequence
We consider the following sequences as a WUR sync sequence and evaluate the performance
  Sequence proposed in [2]
    S1= [0 1 1 1 0 1 0 1 0 0 1 0 1 0 0 1 0 1 1 0 0 1 1 0 1 1 0 0 0 1 1 0]
  Sequence proposed in [1]
    S2 = [1 0 1 0 1 0 1 0 0 1 0 1 1 0 0 1 1 0 0 1 1 0 0 1 0 1 1 0 0 1 0 1]
  Sequence proposed in [3]
    S3 = [1 0 1 0 0 1 0 0 1 0 1 1 1 0 1 1 0 0 0 1 0 1 1 1 0 0 1 1 1 0 0 0]
  Proposed sequence
    S4 = [1 0 1 0 0 1 1 0 0 0 1 0 1 1 1 0 1 0 0 1 1 1 0 0 1 1 1 0 0 1 0 0 ]

## Slide 5: Correlation Property and off duration
S3 and S4 have smaller ACM value than S1 and S2
  S3 and S4 have better correlation property
Sequence | ACMetric (first max/second max) | Max OFF duration in sequence
S1 | -6.4 | 6 us
S2 | -5.3 | 4 us
S3 | -8 | 6 us
S4 | -8 | 6 us

## Slide 6: Simulation assumptions
WUR packet structure
  WUR preamble : L-Preamble + BPSK Mark + WUR SYNC field
  WUR data field : 32 bits with 62.5kpbs for long sync, 250kpbs for short sync
No CFO and No Phase noise
Butterworth filter with 2.5MHz cut off frequency, second order
4MHz sampling rate and SNR defined in 20MHz bandwidth
TGnD and UMi NLoS channels in 2.4GHz

## Slide 7: Simulation results
TGnD
  Short sequence case
    From the PER performance aspect, the difference among the S1,S3 and S4 is within 0.1dB at 10%
    From the aspect of timing error, S3 has better performance than others at 1%. But the difference is minor except the S2

## Slide 8: Simulation results
TGnD
  Long sequence case
    The performance at 10% PER among sequences is identical
    From the aspect of timing error, S2 has slightly worse performance than others at 1%

## Slide 9: Simulation results
Particularly in low data rate case
  S1, S3 and S4 have good timing error rate
    In UMi channel, S4 has a slightly better performance than others as shown in appendix
  The PER performance is almost similar with each other
Sequence | Short case, SNR at 10% PER | Short case, SNR at 1% timing error | Long case, SNR at 10% PER | Long case, SNR at 1% timing error
S1 | -0.15 dB | 0.1dB | -2.43dB | -5.7dB
S2 | 0.22 dB | 1.4dB | -2.37dB | -4.93dB
S3 | -0.17 dB | 0.05dB | -2.31dB | -5.85dB
S4 | -0.11 dB | 0.37dB | -2.34dB | -5.75dB

## Slide 10: Summary
We investigate the performance (i.e. PER and timing error rate) of sync sequences
  The PER performance at 10%
    We check that the performance at 10% PER is almost identical among the sequences
    The difference gap between sequences is within 0.3dB
  The timing error rate at 1%
    Sequences that have good correlation property have good performance
As shown in results, because PER performance of sequences are very similar, we may consider timing error/correlation property to determine the sync sequence, and other proper criteria if any
  We need further investigation because there are various sequences with a good correlation property.

## Slide 11: Straw Poll #1
Do you agree that in SYNC field, the 32-bit sequence starts with repeated pattern of one and zero?
  For example, 1 01 0 or 0 1 0 1
  Y
  N
  abs

## Slide 12: References
[1] IEEE 802.11-17/0096r3 WUR SYNC DESIGN
[2] IEEE 802.11-17/0123r0 Options for Sync Field Bit Sequence
[3] IEEE 802.11-17/0100r1 WUR Preamble Sequence Performance Evaluation
[4] IEEE 802.11-17/0575r9 Specification Framework for TGba

## Slide 13: Appendix

## Slide 14: Simulation results
UMi-NLOS
  Long sequence case