## Slide 1: Addressing in WUR frames
Authors:
Alfred Asterjadhi,
George Cherian

## Slide 2: Introduction
WUR STAs rely on the Address field of WUR frames to identify if the frame is
  Individually addressed to them (Wake Up ID),
  Broadcasted to them (Transmit ID),
  Group addressed to a group to which the STA belongs (Group ID)
WUR STAs also rely in additional information that is
  Implicitly contained in the WUR frame (Embedded BSSID)
  Explicitly contained in the WUR frame (e.g., in TD Control field)
Which lead to increased likelihood that received addressing info. is reliable
  Minimize false wake ups due to WUR frames generated by OBSS APs
  Maximize filtering opportunities for WUR frames that are not intended to the WUR STA
We propose rules on how to select the above identifiers to ensure that
  The values selected by the AP for these identifiers are as random as possible
  The management of identifiers is as simple as possible (and inline with existing PCR architecture)
  The memory requirement for storing these identifiers is as low as possible

## Slide 3: Addressing considerations
An AP maintains the following main identifiers:
  BSSID which is the basic service set identifier of the BSS (6 Bytes)
  N-1 other BSSID identifiers that identify non-transmitted BSSIDs
  AIDs for each of the STAs that is associated with it (12 bits)
It additionally maintains a TIM bitmap that identifies:
  Existence of broadcast BU delivery for its STAs (bit 0)
  Existence of broadcast BU delivery for the non-transmitted BSSID (bits 1 to n-1)
  Existence of individual BUs for each STA (bit AID)
Every non-AP STA is required to maintain all these identifiers when its PCR is on
  PS mechanisms in the PCR heavily rely on these indications to deliver buffered BUs to the PS STAs
Every WUR STA should maintain the minimum possible identifiers:
  Transmit ID (12 bits), which has a conceptual equivalency with bit 0 of TIM bitmap)
  Wake Up ID (12 bits), which has a conceptual equivalency with bit equal to the AID of the STA of TIM bitmap
  Group ID (12 bits), which has a conceptual equivalency with bits (1 to n-1) of the TIM bitmap
    However not limited to these cases only since even within the same BSS the AP can allocate multiple groups (similar to 11ac)

## Slide 4: PCR to WUR mapping
Simplest approach would be to use the same mapping as TIM bitmap
  No architectural changes and no increased memory for AP to maintain a separate ID space
  Minimum memory required for a WUR STA to
    Store value 0 for TXID and WID: at most 3 octets (+ up to 8 bits if multiple BSSID operating)
    Store values for group IDs (with 12 bits each then # GIDs times 12 bits)
      However if GIDs are in a contiguous space then storage can significantly reduced (see next slide)
Drawback: All APs use same AID assignment (start low and go high)
  Address field values selected by all APs would be concentrated in the low end of the ID space
    Increases likelihood of collisions and false wake ups due to OBSS frames (rely only on Embed BSSID)
  Note: Issue incurred in the development of other amendments as well (11ac, 11ah, etc.)
BSSID
TIM bitmap
0, 1, …, n-1, AID n, …, AID m, …
2047
PCR
WUR
TXID 0, 1 , …, n-1, WID n, …, WID m, …
2047
Embed BSSID

## Slide 5: Proposal: PCR to WUR mapping
Proposal: Use a hash of the BSSID to randomize the assignments
  Simplest hash function is to XOR different portions of the BSSID (widely used in 802.11)
Pro 1: Allows to use the same mapping as TIM bitmap
  No architectural changes and no increased memory for AP to maintain a separate ID space
  Minimum memory required for a WUR STA to
    Store one value for TXID and one for WID: at most 3 octets (+ up to 3 bits if multiple BSSID
    Store values for group IDs (with 12 bits each then # GIDs times 12 bits)
      However if GIDs are contiguous space then storage can be significantly reduced (see next slide)
Pro 2: All identifiers are randomly distributed in the ID space
  Allowing early packet filtering, reduced collisions, etc.
BSSID
TIM bitmap
0, 1, …, n-1, AID n, …, AID m, …
2047
PCR
WUR
TXID 0, 1 , …, n-1, WID n, …, WID m, …
2047
Embed BSSID
Hash (BSSID)

## Slide 6: What if?
By some chance two APs in the same neighborhood:
  I.e., have 2 IDs (12b) that match and Embedded BSSID (16b) match as well?
    This is an extremely low probability event (28 bits to coincide)
    But if it occurs it would be good to have a countermeasure
Can either of the AP be able to change its hashing function?
  Option 1: The AP optionally advertises an alternative WUR BSSID
    Simplest approach but requires extra 6 bytes exchanged in the main radio
  Option 2: The AP optionally advertises a change in the hashing function
    Increase in computation logics but does not require change of BSSID
Option 1 is preferred since keeps WUR STA’s complexity low

## Slide 7: AP side: XOR-based options
The AP generates the identifiers as follows:
  Transmit ID =
    Option 1: = BSSID[36: 47]
    Option 2: = BSSID[0: 11] XOR BSSID[12: 23] XOR BSSID[24: 35] XOR BSSID[36: 47]
    Option 3: = Other?
  Wake Up ID = (AID + Transmit ID) mod 212
  As part of the Group ID procedure:
    Transmit ID n = (n + Transmit ID) mod 212, where n in TIM bitmap for non-TX BSSID
    Group ID = (m + Transmit ID) mod 212, where m in TIM bitmap for that group ID
Same hashing function applied to Embedded BSSID:
  Embedded BSSID =
    Option 1: = BSSID[20: 35]
    Option 2: = BSSID [0 : 15] XOR BSSID [16:31] XOR BSSID [32: 47]
    Option 3: Other?
Where BSSID is the address of the transmitting AP
  Unless the AP advertises a WUR BSSID in WUR elements it transmits

## Slide 8: STA side
When in WUR mode the STA needs to store only:
  Basic: Transmit ID (12b), Wake Up ID (up to 12b), Embedded BSSID (16b)
  Plus Multi-BSSID: Another 8 bits to identify its non-transmitted BSSID
Plus Group IDs: Depends on how it is designed
  Worst case: Random assignment of Group IDs:
    Things can go north linearly 12b X # Group IDs (e.g., 10 IDs would need 15 bytes)
To control the amount of memory required
  The AP allocates the Group IDs in a contiguous ID space:
    That can be identified by a Start ID + Group Bitmap (12 bits plus bitmap size)
  WUR STA together with Group ID support also declares bitmap size it supports

## Slide 9: Conclusion
We propose rules for address assignment that:
  Keep maintenance complexity at the AP to a minimum
  Require minimum storage at the STA side
  Ensure false wake ups and address collisions are kept to a minimum
  Provide seamless transition between PCR and WUR operation
  Maintain assignment flexibility for a wide range of use cases

## Slide 10: Straw Poll 1
Do you support to add the following to the TGba SFD?
  The Transmit ID is algorithmically obtained from the BSSID
  The Embedded BSSID is algorithmically obtained from the BSSID
Result: 16Y, 0N, 9A

## Slide 11: Straw Poll 2
Do you support to add the following to the TGba SFD?
  A STA that declares support of Group IDs is required to store at least one group ID and shall declare the Group ID bitmap size that it is capable of storing
Result: 16Y, 0N, 9A

## Slide 12: Motion 1
Move to add the following to the TGba SFD?
  The Transmit ID is algorithmically obtained from the BSSID
  The Embedded BSSID is algorithmically obtained from the BSSID
  Moved: Alfred Second: Leif
  Results: Passes with unanimous consent

## Slide 13: Motion 2
Move to add the following to the TGba SFD?
  A STA that declares support of Group IDs is required to store at least one group ID and shall declare the Group ID bitmap size that it is capable of storing
  Moved: Alfred Second: Leif
  Result: Passes with unanimous consent