## Slide 1: FCS size for WUR frames
Authors:
Alfred Asterjadhi,
George Cherian

## Slide 2: Introduction
The WUR frame has an FCS which carries the CRC of the frame
  Length and computation of the FCS is TBD [1]
During the last F2F we made some progress in one aspect [2]
  The CRC of WUR frames shall use one of the following CRC engines from IEEE 802.11
    32-bit CRC, 16-bit CRC, 8-bit CRC
In [2] there were additional discussions on the FCS length
  Pointing out the different options we have and certain benefits/drawbacks
We continue those discussions and propose to conclude the FCS topic
  Determine the FCS size and consequently all other aspects of the design
    Which CRC engine to use from the three possibilities, etc.

## Slide 3: General considerations
FCS field length has been and continues to be debated
  Several options are candidates (8, 16, 24 bits)
    Longer FCS provides better protection but higher overhead
    Shorter FCS provides lesser protection but lower overhead
  A trade-off between the two properties need to be found
    Ensuring acceptable protection and low overhead for WUR frames
To make a decision we might need to consider that we have:
  Constant length (CL) WUR frames (only 4 bytes)
  Variable length (VL) WUR frames (up to 12 or 20 bytes (TBD))
And that the FCS could carry the MIC as well [3]
MAC Header | Frame Body | FCS
 | Frame Control | Address | TD Control
Bits | 8 | 12 | 12
CRC
TBD

## Slide 4: Some numbers
Overhead (FCS length/MPDU length)
  The lower the overhead the better
  Overhead of > 25% is not desirable, but if false positives and collisions are important then 33% could be acceptable
False positive rate (worst case)
  The lower the false positive rate the better
  The actual false positive rate will be lower* since Address field has to check for frame to be addressed to the STA
Collision probability expected to be minimal* because there is
  At least 12b of Address field present in every WUR frame (each STA expected to have unique identifier within the BSS)
  Embedded BSSID information in the FCS of post-association WUR frames
    WUR frames generated by OBSS APs will very likely appear as corrupted at the WUR STA
  WUR frames transmission at scheduled times that can reduce overlap with OBSS activities
*Considerations assume random properties of identifiers in Address field and Embedded BSSID field
Overhead [%] | 8-bit FCS | 16-bit FCS | 24-bit FCS
CL WUR frame (4B) | ~20% | ~33% | ~43%
Min VL WUR frame (6B) | ~14% | ~25% | ~33%
Max VL WUR frame(20B) | ~5% | ~9% | ~13%
NOTE-Every octet costs ~0.13ms of airtime@62.5kbps, and ~0.03ms of airtime@250kbps. |  |  | 
FPR [%] | 8-bit FCS | 16-bit FCS | 24-bit FCS
1/2n , where n is the FCS size | ~4*10-3 | ~1.5*10-5 | ~6*10-8

## Slide 5: Additional considerations
Since the impact of the FCS length may vary for different frames
  We might want to consider an FCS that is:
    Shorter for the CL WUR frames (4 Bytes)
    Longer for the VL WUR frames (12 or 20 Bytes)
For example we could use a 16-bit CRC polynomial
  8 bit CRC included in the FCS (e.g., 8 MSBs of the 16-bit CRC)
    Common for all WUR frames
  Additional 8 bit CRC included in the Frame Body of VL WUR frames
    Suppressed in transmission for CL WUR frames
These considerations are only noteworthy if the group does not converge on a unified FCS design for all WUR frames
  I.e., all WUR frames contain a TBD-bit FCS field
    Where TBD could be for example 8, 16, 24, …
Based on the previous discussions the recommendation is
  Have a unified FCS design with FCS field length of 16-bits and 16-bit CRC engine

## Slide 6: Straw Poll 1
Do you support to add the following to the TGba SFD:
  The FCS field of all WUR frames has the same size

## Slide 7: Straw Poll 2
Which option do you support for the FCS field length?
  Option 1: 8 bits
  Option 2: 16 bits

## Slide 8: Straw Poll 3
Do you support to amend the following text in the TGba SFD?
  The CRC of WUR frames shall use one of the following the 16-bit CRC engines from IEEE 802.11
    32-bit CRC, 16-bit CRC, 8-bit CRC

## Slide 9: Motion 1
Move to add the following to the TGba SFD:
  The FCS field of all WUR frames has the same size.

## Slide 10: Motion 2
Move to add to the TGba SFD:
  The FCS field of WUR frames has a size of 16 bits.

## Slide 11: Motion 3
Move to amend the following text in the TGba SFD?
  The CRC of WUR frames shall use one of the following the 16-bit CRC engines from IEEE 802.11
    32-bit CRC, 16-bit CRC, 8-bit CRC

## Slide 12: References
[1] 11-17/575r9 specification framework (P.K. Huang, et. al.)
[2] 11/18/0094r1 Fixing TBDs in WUR frame (A. Asterjadhi, et. al.)
[2] 11-17/1004r4 Considerations on WUR frame format (A. Asterjadhi, et. al.)