## Slide 1: HEz Ranging for Passive Location Support
Date: 2018-03-07
Authors:

## Slide 2: Solution Principle
Re-use the HEz Ranging exchanges to support passive location
Supports all requirements:
  Reuses protocol for active ranging
  Scheduled traffic - supports efficiency, power save and deals with congestion
  Is trigger based – Supports future likely preferred/required operation.
  Elegantly enables client anchor STAs for scalable location support
    Client anchor STAs operate basically in normal HEz ranging, and
    Client anchor STAs are much more able to change channels than are AP anchor STAs
  Does enable AP to AP exchanges for scalable location support
    If an AP desires to signal an adjacent AP is can take on the initiator role in the neighboring APs HEz ranging opportunity
Client to be located listens to transmitted NDPs and reported time-stamps and computes its location.

## Slide 3: HEz-Ranging for Passive Location Support
DL
NDP
UL
NDP
TF
Responder
Initiator AS 1
Initiator
AS 2
UL
NDP
UL
NDP
DL
NDPA
Green arrows – Regular ranging frame exchanges
Blue arrows – Extra listening opportunities
Poll
TF
PR
PR
iSTA to rSTA
LMR
TF
rSTA to
iSTA
LMR
UL
NDP
TF
iSTA to rSTA
LMR
Frame
1
Frame
2
Existing TGaz SFD Protocol
Added Protocol
iSTA to rSTA
LMR
LMR broadcasting
(Details TBD)
Enables client station receiving the NDPs and LMR reporting to calculate its location using TDOA relations.

## Slide 4: Proposed Additions
Expanded time-stamp reporting in LMRs
  To enable reporting of TOAs for all received NDPs
Broadcast of LMRs – See slide 3.
  To enable passing LMR info to client to be located
Negotiation request for HEz ranging for scalable location support
  To enable AP to co-schedule these ranging exchanges
Schedule announcement
  Add AP broadcast of timing/configuration of scalable location HEz ranging opportunities
LCI announcement
  In schedule or in LMR

## Slide 5
Signaling Topology for Passive Location built on HEz Ranging
AP (RSTA)
AP
AP
AS
AS
AS
AS
AS
AS (ASTA)
Note that with scheduled HEz ranging opportunities all the neighboring APs (RSTA) and Anchor client Stations (AS/ASTA) can appear on the same channel all at the same time, which enables a very large number of ranging exchanges. Furthermore, if the client to be located also switches channels, it can listen to an even larger set of ranging exchanges, namely one such set in each APs channel.
Cross ranging exchanges between the ASs and the secondary APs generally not shown but they appear between any AP/AS-AP/AS pair.
Client to be located – Can also switch channels and listen to the corresponding ranging exchanges on each neighboring APs channel.
APs assumed to operate on different channels
AS - Client Anchor Station

## Slide 6: Straw poll 1
Do you support the following attributes for the HEz Ranging for passive location support:
The Polling part is the same as the HEz Ranging polling part.
The measurement part is the same as the HEz Ranging measurement part with the following attributes:
  Each TF Sounding solicits a single user ASTA NDP (a subset behavior of the Ranging HEz).
  The measurements frames are full BW.
  The ASTA measures the TOA of the NDP transmitted by RSTA and optionally by other ASTAs of the same sequence only.
  The listening client measures the differential time of flight of pairs of RSTA and/or ASTAs.
  The measurement sequence (UL and DL) completes in a single TxOP.
The indication of ‘Passive Location HEz Ranging type’ within the TF of the sequence is TBD.

## Slide 7: Motion 1
For HEz Ranging for Passive Location, the 11az protocol shall specify that:
The Polling part is the same as the HEz Ranging polling part.
The measurement part is the same as the HEz Ranging measurement part with the following attributes:
  Each TF Sounding solicits a single user ASTA NDP (a subset behavior of the Ranging HEz).
  The measurements frames are full BW.
  The ASTA measures the TOA of the NDP transmitted by RSTA and optionally by other ASTAs of the same sequence only.
  The listening client measures the differential time of flight of pairs of RSTA and/or ASTAs.
  The measurement sequence (UL and DL) completes in a single TxOP.
The indication of ‘passive location Ranging Hez type’ within the TF of the sequence is TBD.

## Slide 8: Straw Poll 2
Do you support that HEz Ranging for Passive Location shall support:
1. Reporting of all TOA measurements by ASTA of the same ranging opportunity (delayed or immediate),
2. Method of conveying LMR to passively locating STA,
3. Negotiation for Passive Location sessions establishment between RSTA and ASTA,
4. Schedule advertisement of HEz Ranging for Passive Location support, and
5. LCI announcement.
Y: N: A:

## Slide 9: Motion 2
Add the following text to the TGaz SFD:
For HEz Ranging for Passive Location, the 11az protocol shall support the following attributes:
1. Reporting of all TOA measurements by ASTA of the same ranging opportunity (delayed or immediate),
2. Method of conveying LMR to passively locating STA,
3. Negotiation for Passive Location sessions establishment between RSTA and ASTA,
4. Schedule advertisement of HEz Ranging for Passive Location support, and
5. LCI announcement.
Y: N: A:

## Slide 10
Thank You!