IEEE P802.11
Wireless LANs

| 802.11 [802.11az Trigger Frame Format] (relative to REVmd D0.5) |
| --- |
| Date: 2018-01-10 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Jonathan Segev | Intel Corporation |  |  | jonathan.segev@intel.com |
| Chittabrata Ghosh | Intel Corporation |  |  |  |

[Modify Section 9.3.1.23 as follows:]

The Trigger Type subfield indicates the type of the Trigger frame and the encoding is defined in Table 9-25b

(Trigger Type subfield encoding).

Table 9-25b—Trigger Type subfield encoding

| Trigger Type field value | Description |
| --- | --- |
| 0 | Basic Trigger |
| 1 | Beamforming Report Poll (BRP) |
| 2 | MU-BAR |
| 3 | MU-RTS |
| 4 | Buffer Status Report Poll (BSRP) |
| 5 | GCR MU-BAR |
| 6 | Bandwidth Query Report Poll (BQRP) |
| 7 | NDP Feedback Report Poll |
| 8 | Location |
| 89-15 | Reserved |

9.3.1.23.9 Location variant

The Location Trigger frame format is defined in Figure 9-52?? (Trigger frame).

The Trigger Dependent Common Info subfield is always present in the Location Trigger frame, and is described in Figure 9-52??.

|  | Location trigger subtype | SAC | Reserved |
| --- | --- | --- | --- |
| Bits: | 4 | TBD | 4 |

Figure 9-52?? - Trigger Dependent Common Info subfield for the Location Trigger Frame

Value of the Trigger Subtype for the Location Trigger Frame variant is defined in Table XXXX.

Table xxxx — Location Trigger subtype of the Location Trigger Dependent Common Info Field

| Trigger Subtype field value | Description |
| --- | --- |
| 0 | HEz Poll |
| 1 | HEz Uplink Sounding |
| 2 | HEz LMR |
| 3 | Location Negotiation |
| 4-15 | Reserved |

The SAC (Security Authentication Code) subfield is valid if the Trigger Subtype field value is 1, i.e., HEz UL Sounding and reserved, otherwise. The SAC field provides the SAC value of the UL or DL sounding associated with the measurement instance (see Section 11.22.6.4.2.3 HEz Range Measurement Sounding).

The Location TF sub-variants shall be transmitted with a Trigger Frame MAC Padding Duration of 16usec.

The format of the Trigger Dependent User Info field for the Location Trigger Frame is dependent on the Trigger Subtype field value in the Location Trigger Dependent Common Info field (refer to Table XXXX).

9.3.1.23.9.1 HEz Poll Trigger Sub-variant

The Per User Info field in the HE Poll Trigger sub-variant is identical to the format of the Per User Info field in the Basic Trigger Frame (see Section 9.3.1.23.1), except that the AID12 subfield carries an AID12 for an associated locating STA or an RID12 for an unassociated locating STA.

9.3.1.23.9.2 HEz Uplink Sounding Sub-variant

The Trigger Dependent User Info subfield is present when the Trigger Subtype is HEz Uplink Sounding. The User Info field for the HEz Uplink Sounding sub-variant is defined in Figure 9-52??.

|  | B0 B11 | B12 B20 | B21 B24 | B25 | B26 B31 | B32 B38 | B39 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | AID12/RID12 | RU Allocation Reserved | MCS Reserved | DCM Reserved | SS Allocation | Target RSSI | Reserved | Trigger Dependent User Info |
| Bits: | 12 | 9 | 4 | 1 | 6 | 7 | 1 | variable |

Figure 9-52??—User Info field for HEz Uplink Sounding sub-variant

The Trigger Dependent User Info subfield carries the SAC field. The length of this subfield is TBD.

9.3.1.23.9.3 HEz LMR Sub-variant

The Per User Info field in the HE Poll Trigger sub-variant is identical to the format of the Per User Info field in the Basic Trigger Frame (see Section 9.3.1.23.1), except that the AID12 subfield carries an AID12 for an associated locating STA or an RID12 for an unassociated locating STA.

# Comments

should we take value from endof list to not conflict with new 11ax featues not visible yet?

This is an unassociated mode TF. As such the AP has no visibility as to the STA capability (HE MAC capabilities). As this is a low rate frame fixed 16usec makes sense - discusion.

# Text boxes

Abstract

This submission proposes P802.11az draft amendment text for the P802.11az Negotiation Protocol. The baseline documents that this proposal depends on are:

- D0.05 of REVmd

- D8.0 of PIEEE802.11aj

- D5.0 of PIEEE802.11ak

- D13.0 of PIEEE802.11aq

History:

R0: Initial Version