## Slide 1: Additions to Group Beamforming in support of Beam Measurement for mmWave Distribution Networks
Name | Affiliation | Address | Phone | Email
Tony Xiao Han | Huawei |  |  | tony.hanxiao@huawei.com
Yan Xin |  |  |  | yan.xin@huawei.com
Chenlong Jia |  |  |  | jiachenlong@huawei.com
Mengyao Ma |  |  |  | ma.mengyao@huawei.com
Carlos Cordeiro | Intel |  |  | carlos.cordeiro@intel.com
Oren Kedem |  |  |  | oren.kedem@intel.com
George Cherian | Qualcomm |  |  | gcherian@qti.qualcomm.com
Assaf Kasher |  |  |  | akasher@qti.qualcomm.com
Djordje Tujkovic | Facebook | 1 Hacker Way Menlo Park, CA 94025 USA |  | djordjet@fb.com
Krishna Gomadam |  |  |  | kgomadam@fb.com
Pradeep Nemavat |  |  |  | npradeep@fb.com
Payam Torab |  |  |  | ptorab@fb.com
Michael Grigat | Deutsche Telekom AG | Deutsche-Telekom-Allee 7, 64295 Darmstadt, Germany | +49-6151-5833533 | m.grigat@telekom.de

## Slide 2: Background TDD individual and group beamforming
Draft 1.1 has defined an individual beamforming protocol for Distribution Networks (TDD Individual Beamforming, original contribution [4])
A follow-up contribution in January [5] proposed to extend the beamforming protocol to train multiple responders through a variable size TDD SSW frame and broadcast RA field, a procedure initially referred to as MU Beamforming and later renamed to TDD Group Beamforming
This contribution harmonizes the TDD Group Beamforming procedure with two other beamforming procedures previously introduced for Distribution Networks in [1-3], namely, Periodic Beamforming and Interference Scan
Text implementation is also available on server [6]

## Slide 3: Beamforming in Distribution Networks Periodic Beamforming and Interference Scan – TDD Beam Measurement
Periodic beamforming
  Application: Beam refinement, runtime array calibration…
  Procedure: A connected target STA sweeps its sectors synchronously with initiator, under SME control, and reports measurements to controller (SME), or optionally later to the initiator through TDD Route IE
    No beamforming packet sent by responder
Interference scan
  Application: To measure the interference from initiator on neighboring STAs
  Procedure: Neighboring STAs sweep their sectors synchronously with initiator, under SME control, and report measurements to controller (SME)
    No beamforming packet sent by responder
Aside from unicast/broadcast RA field, the two procedures have the same over the air behavior and can be unified into a “TDD Beam Measurement” operation

## Slide 4: Broadcast RA field Use cases
In addition to TDD Group Beamforming and aforementioned TDD Beam Measurement (specifically, interference scan), there is another usage for broadcast RA in TDD SSW frames – individual beamforming with an unknown or wrongly assumed MAC address
  Common field scenarios: Operation errors (e.g., wrong MAC address label on the box), installation errors (wrong box on the pole selected for responder), database errors
  Broadcast RA in this context is exercised with controlled avoidance of collision
  This is conceptually similar to A-BFT with one slot
To summarize, there are three use cases for a TDD SSW frame with broadcast RA field that would need additional context to resolve
  TDD Group Beamforming with two or more responders
  TDD Individual Beamforming with an unknown responder
  TDD Beam Measurement (interference scan)

## Slide 5: Scope of text additions TDD Group Beamforming and TDD Beam Measurement
TDD Group Beamforming
  MLME-TDD-BF-TRAINING vectorized for group results
    One confirm primitive to return multiple responders and sectors
  New TDD Group Beamforming bit in TDD Beamforming Control field to differentiate individual and group beamforming frames with broadcast RA field
  Normative behavior for initiator and responder defined in two new sections 10.39.10.4 and 10.39.10.5
TDD Beam Measurement
  MLME-TDD-BF-MESUREMENT introduced
    Request primitive applicable to both initiator and responder
  New TDD Beam Measurement bit in TDD Beamforming Control field to indicate frame is being used for measurement (can be concurrent with beamforming)
  Normative behavior for initiator and responder defined in two new sections 10.39.10.6 and 10.39.10.7

## Slide 6: TDD Beamforming Control field New fields
TDD Group Beamforming and TDD Beam Measurement fields added to TDD Beamforming Control field to resolve ambiguity
 | TDD Group Beamforming | TDD Beam Measurement | TDD Beamforming Frame Type | End of Training | Reserved
Bits: | 1 | 1 | 2 | 1 | 53
Figure 13—TDD Beamforming Control field format

## Slide 7: TDD Beamforming and TDD beam measurement Combinations of RA and TDD beamforming/beam measurement fields
TDD Group Beamforming | TDD Beam Measurement | RA Field | TDD Beamforming Procedure
0 | 0 | Unicast | TDD Individual BF with a known peer
0 | 0 | Broadcast | TDD Individual BF with an unknown peer
0 | 1 | Unicast | TDD Beam measurement – Periodic Beamforming (refinement, calibration, …)
0 | 1 | Broadcast | TDD Beam measurement – Intereference scan
1 | 0 | Unicast | Reserved
1 | 0 | Broadcast | TDD Group BF with two or more peers
1 | 1 | Unicast | Reserved
1 | 1 | Broadcast | TDD Group BF with two or more peers (per responder list); other neighboring STAs to perform TDD beam measurement (Interference scan) under SME command

## Slide 8: Straw poll
Do you support TDD beam measurement additions to TDD group beamforming?
  Yes
  No
  Abstain

## Slide 9: References
[1] 802.11-17/1019 “mmWave Mesh Network Usage Model”
[2] 802.11-17/1321 “Features for mmW Distribution Network Use Case”
[3] 802.11-17/1679 “Beamforming protocol reuse for mmWave Distribution Networks”
[4] 802.11-18/0179 “Beamforming for mmWave Distributed Network”
[5] 802.11-18/0175 “MU Beamforming for mmWave Distributed Network”
[6] 802.11-18/0547 “Draft text for additional Beamforming procedures for mmwave distributed network”