## Slide 1: MC-OOK ‘On’ Symbol Generation
Date: 2018-03-29
Authors:

## Slide 2: Background
A number of the PHY engineers met and discussed the construction of the 4 and 2 µs MC-OOK ‘On’ symbols
It was also discussed on the March 22 conference call where a straw poll was taken
Updates have been made based on those discussions
The text regarding the PAPR has been removed since that text can be placed in the requirements section
There are two version being considered with a little different wording, for further (maybe final) consideration

## Slide 3: Version #1
4 µs MC-OOK ‘On’ Symbol
For a single 20-MHz WUR channel the 4 µs MC-OOK ‘On’ symbol can be constructed using a 64-point IFFT, sampling at 20-MHz as follows:
Thirteen subcarriers are used, (-6, -5, … -1, 0, 1, 2, … 6).
The DC subcarrier is null.
The other subcarriers are selected from any of the following constellations: BPSK, QPSK, 16-QAM, 64-QAM, and 256-QAM.
The last 16 values of the 64-point IFFT output are prepended to the 64 samples generating 80 samples, representing the 4 µs MC-OOK ‘On’ symbol.
2 µs MC-OOK ‘On’ Symbol
For a single 20-MHz WUR channel the 2 µs MC-OOK ‘On’ symbol can be constructed using a 64-point IFFT, sampling at 20-MHz as follows:
Thirteen subcarriers are used, (-6, -5, … -1, 0, 1, 2, … 6). The following subcarriers are null: (-5, -3, -1, 0, 1, 3, 5).
The other subcarrier are selected from any of the following constellations: BPSK, QPSK, 16-QAM, 64-QAM, and 256-QAM.
The first 32 values of the 64-point IFFT output are selected. The last 8 samples of those 32 samples prepended to the 32 samples generating 40 samples, representing the MC-OOK 2 µs ‘On’ symbol.

## Slide 4: Version #2
4 µs MC-OOK ‘On’ Symbol
For a single 20-MHz WUR channel the 4 µs MC-OOK ‘On’ symbol can be constructed using a 64-point IFFT, sampling at 20-MHz as follows:
Thirteen subcarriers can be used, (-6, -5, … -1, 0, 1, 2, … 6).
The DC subcarrier can be null.
The other subcarriers can be selected from any of the following constellations: BPSK, QPSK, 16-QAM, 64-QAM, and 256-QAM.
The last 16 values of the 64-point IFFT output are prepended to the 64 samples generating 80 samples, representing the 4 µs MC-OOK ‘On’ symbol.
2 µs MC-OOK ‘On’ Symbol
For a single 20-MHz WUR channel the 2 µs MC-OOK ‘On’ symbol can be constructed using a 64-point IFFT, sampling at 20-MHz as follows:
Thirteen subcarriers can be used, (-6, -5, … -1, 0, 1, 2, … 6). The following subcarriers can be null: (-5, -3, -1, 0, 1, 3, 5).
The other subcarrier can be selected from any of the following constellations: BPSK, QPSK, 16-QAM, 64-QAM, and 256-QAM.
The first 32 values of the 64-point IFFT output are selected. The last 8 samples of those 32 samples prepended to the 32 samples generating 40 samples, representing the MC-OOK 2 µs ‘On’ symbol.

## Slide 5: Straw Poll
Which of the two version of the text do you prefer to be added to the SFD?
  Version #1
  Version #2
  Abstain