## Slide 1: ERP Rates
Date: 2018-04-10

## Slide 2: Abstract
For very low power, low data rate IoT applications, devices operating at 2.4GHz may choose baseline 802.11, 802.11b (HT), or 802.11g (ERP). Each poses some problems. ERP devices are required to support 1, 2, 5.5, 11, 6, 12, and 24 Mbps rates: the OFDM rates are burdensome and the data rates are overkill. On the other hand, DSSS and HT devices don’t support the 6 Mbps OFDM preamble, and require protection modes, lowering BSS throughput appreciably.
It would be useful to allow reduced functionality ERP devices, (1 and 6 Mbps, or any other subset of ERP rates).
CIDs addressed: 1599

## Slide 3: Text (partial)
“A second PHY, denoted Variant ERP (VERP), is defined by extension in this subclause. The VERP differs from the ERP in that a VERP STA may support transmission and reception of any nonempty subset of ERP data rates and associated preambles and protection modes, and no other data rates and associated preambles and protection modes. In all other respects the VERP and ERP are identical.“
VERP non-AP STA associates as an ERP STA, then sends TBD additional messaging to signal its true rates

## Slide 4: Discussion
Any idea of this type requires discussion of additional cases:
What is the AP required to do if a VERP STA associates?
What if the AP is legacy and does not understand the additional messaging?
How does coexistence work if the VERP is all single-tone or all OFDM?

## Slide 5: Discussion—II
What is the AP required to do if a VERP STA associates?
  Transmissions to the VERP are required to be one of the supported rates (if AP understands additional messaging)
  But there are no other requirements: beacons, protection methods, etc. don’t have to belong to those rates
What if the AP is legacy?
  AP thinks VERP has implemented all mandatory ERP rates
  Some ERP rates may not work because of range; VERP devices with lowest data rates in each category should still work fine
How does coexistence work with all-DSSS-CCK, all-OFDM?
  Always have energy detect; VERP suitable for low duty cycle (vendor has incentive to choose rates that work well)

## Slide 6: Straw poll
Do you support adding definitions of VERP devices, along the lines outlined in this presentation?
  Yes
  No
  Need more detail but generally supportive
  Need more detail but generally not supportive
  No opinion