## Slide 1: OOK Waveform for FDMA
Date: 2018-05-07
Authors:

## Slide 2: Introduction
In the previous meeting, FDMA transmission is proposed [1]:
  Each 20 MHz channel only contains one 4 MHz sub-channel for wake-up signal transmission
In this contribution, we propose a method based on existing QPSK Golay sequences to remedy the significant PAPR increase when WUSs are FDMed
[1]: IEEE 802.11-17/1625r6

## Slide 3: Problem Statement
CP
CP
CP
CP
CP
CP
CP
CP
CP
CP
CP
CP
CP
CP
HDR
HDR
LDR
HDR
Time
Time
Time
Time
2s
The PAPR can be significantly high since the ON signals on different channels overlap in time in case of FDMA
Intractable problem because
  There may be 1, 2, 3, or 4 active channels
  The active channel locations in frequency could be different
  LDR and HDR waveforms can also be different (e.g., CP size etc.)
many combinations for a given time period
Overlapping in time

## Slide 4: Transmitter Block Diagram (HDR)
CP
CP
0
CP
CP
CP
CP
CP
CP
CP
CP
1
CP
CP
0
Time
Time
Time
Time
2s
CP
1
CP
CP
CP
IDFT
CP+
7
Manchester-coded bit (0)
Channel 1
7
Manchester-coded bit (1)
Channel 2
7
Manchester-coded bit (1)
Channel 3
7
Manchester-coded bit (0)
Channel 4
For HDR, FDMA can be supported through a single IDFT operation
  This representation is not different than generating single-channel mask–based MC-OOK (length of 7) waveforms, shifting them in frequency, and then summing them up every 2 s
  We use this representation for the following discussions
Question: How to choose the sequences { such that the PAPR of the signal is below a certain level, e.g., 3 dB?

## Slide 5: Golay Complementary Sequences
A sequence pair is called a complementary sequence if
,
where is the length of and , and are the inverse Fourier
transforms of and , respectively
Because of the definition, the PAPR of the inverse Fourier transform of a Golay sequence is always bounded by 3 dB
The sequences and the construction methods have been known since 1961* and have been heavily-used in IEEE 802.11ad/ay
IDFT
**
*Golay, M. (April 1961). "Complementary series". IEEE Transactions on Information Theory. 7 (2): 82–8
*https://en.wikipedia.org/wiki/Complementary_sequences
**Matthew G. Parker, Kenneth G. Paterson, Chintha Tellambura, “Golay Complementary Sequences”, 2004

## Slide 6: Generating a Length 7 Sequence with nulled DC tone (Single Channel)
The Golay sequences can be generated through concatenations and zero padding of the sequences in a pair
  For example, and construct a Golay pair.
  Hence, and also construct another pair
  This property can be useful to generate a Golay sequence with a nulled DC tone, e.g.,
We can use the same construction method to remedy the PAPR problem
Frequency
3
3
1

## Slide 7: Concatenating Golay Sequences (Multiple Channels) 1/2
The figure above shows some examples of several channelization
  The PAPR is always less than or equal to 3 dB even if there is a non-contiguous mapping
Frequency
Channel 1
Channel 2
Channel 3
Channel 4
Frequency
Frequency
A Golay sequence
A Golay sequence
A Golay sequence

## Slide 8: Concatenating Golay Sequences (Multiple Channels) 2/2
Other cases can also be generated with several Golay construction methods*
Frequency
Frequency
Channel 1
Channel 2
Channel 3
Channel 4
A Golay sequence
A Golay sequence
*Matthew G. Parker, Kenneth G. Paterson, Chintha Tellambura, “Golay Complementary Sequences”, 2004

## Slide 9: Handling FDMed LDR and HDR WUSs
CP
CP
CP
CP
Time
Time
CP
CP
CP
CP
If we use Option 2, the design for LDR and HDR can be unified and the IDFT durations are aligned
HDR
LDR
2s
CP
CP
Time
Option 1 for LDR:
Option 2 for LDR:
Time
CP
CP
CP
CP
2s
4s

## Slide 10: TX Diagram for FDMed LDR and HDR WUSs
Manchester-coded bits across the channels |  |  |  | 
0000 |  |  |  | 
1000 |  |  |  | 
0100 |  |  |  | 
0010 |  |  |  | 
0001 |  |  |  | 
1100 |  |  |  | 
0110 |  |  |  | 
0011 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
0101 |  |  |  | 
0111 |  |  |  | 
1110 |  |  |  | 
1011 |  |  |  | 
1101 |  |  |  | 
1111 |  |  |  | 
Manchester-coded bits across the channels |  |  |  | 
0000 |  |  |  | 
1000 |  |  |  | 
0100 |  |  |  | 
0010 |  |  |  | 
0001 |  |  |  | 
1100 |  |  |  | 
0110 |  |  |  | 
0011 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
0101 |  |  |  | 
0111 |  |  |  | 
1110 |  |  |  | 
1011 |  |  |  | 
1101 |  |  |  | 
1111 |  |  |  | 
2s
IDFT
CP+
7
Manchester-coded bit: 0
Channel 1
7
Manchester-coded bit: 1
Channel 2
7
Manchester-coded bit: 1
Channel 3
7
Manchester-coded bit: 0
Channel 4
CP
CP
CP
CP
CP
CP
CP
CP
CP
CP
CP
CP
Time
Time
Time
Time
CP
CP
CP
CP
Ch #1 (HDR)
Ch #2 (HDR)
Ch #3 (LDR)
Ch #4 (HDR)
Example tone indices for : [-3:3]-48
Example tone indices for : [-3:3]-16
Example tone indices for : [-3:3]+16
Example tone indices for : [-3:3]+48
Not Golay sequences but low PAPR
0
1
0
1
Rate: 1 symbol/2s

## Slide 11: Simulation Assumptions
We simulate 5 different cases considering various FDMed WUSs with HDR and LDR (the results for different cases are given in appendix)
AP: 80 MHz sample rate
  PA: Rapp model with the smoothness factor of 3, 4x oversampling
WURx:
  Envelope detector (i.e., samples the accumulated the sum of absolutes of I- and Q- branches), 5th order Butterworth filter, ideal synchronization
We compare the MC-OOK proposals in the following contributions for HDR and LDR with the Golay sequences are given in Slide 10
  Option 1: Golay-based (QPSK)
  Option 2: LDR/HDR: IEEE 802.11-18/0479r2 (256 QAM)
  Option 3: LDR: IEEE 802.11-18/0421r0/HDR: IEEE 802.11-18/0492r0 (BPSK)
  Option 4: LDR/HDR: IEEE 802.11-18/0421r0 (BPSK)
We apply phase rotations for the channels as described in IEEE 802.11ac for 492, 479, and 421
  Extra phase rotations for different channels are not needed for Golay sequences

## Slide 12: Numerical Analysis (2 HDRs, 2LDRs)
LDR
HDR
HDR
HDR
Time domain signal
Legacy
SYNC

## Slide 13: Numerical Analysis (2 HDRs, 2LDRs)
LDR
HDR
HDR
HDR
Time domain signal
Legacy
SYNC

## Slide 14: Numerical Analysis (2 HDRs, 2LDRs)
LDR
HDR
HDR
HDR
Time domain signal
Legacy
SYNC

## Slide 15: PAPR Results (2 HDRs, 2LDRs)
Rates: | L L H H |  | 
Probability: | .5 | .8 | .99
Option 1 (Golay) | 6.61 | 6.61 | 6.67
Option 2 (256QAM) | 7.37 | 9.55 | 9.80
Option 3 (BPSK) | 8.99 | 11.08 | 11.13
Option 4 (BPSK) | 8.22 | 10.60 | 10.67

## Slide 16: PAPR Results for Different Cases
The probability of sample power being 9.55 dB, 12.39 dB, and 10.77 dB higher than the average is 0.2 for Option 2, 3, and 4, respectively, in some cases (see appendix for details)
The instantaneous power is less than 6.67 dB above the average for Option 1 (Golay sequences) for all cases with .99 probability
 | Case 1 |  |  | Case 2 |  |  | Case 3 |  |  | Case 4 |  |  | Case 5 |  |  | 
Rates: | _ _ H H |  |  | H H H H |  |  | L L H H |  |  | L L L H |  |  | H H L H |  |  | 
Probability: | .5 | .8 | .99 | .5 | .8 | .99 | .5 | .8 | .99 | .5 | .8 | .99 | .5 | .8 | .99 | Worst @ 0.8
Option 1 (Golay) | 6.02 | 6.02 | 6.02 | 6.01 | 6.67 | 6.67 | 6.61 | 6.61 | 6.67 | 6.62 | 6.67 | 6.67 | 6.01 | 6.62 | 6.67 | 6.67
Option 2 (256QAM) | 6.60 | 6.60 | 6.60 | 7.12 | 7.12 | 7.12 | 7.37 | 9.55 | 9.80 | 7.37 | 7.46 | 9.91 | 7.24 | 9.29 | 9.71 | 9.55
Option 3 (BPSK) | 9.38 | 9.38 | 9.38 | 9.89 | 12.39 | 12.39 | 8.99 | 11.08 | 11.13 | 8.39 | 8.59 | 10.63 | 9.72 | 11.36 | 11.41 | 12.39
Option 4 (BPSK) | 8.25 | 8.25 | 8.25 | 8.77 | 8.77 | 8.77 | 8.22 | 10.60 | 10.67 | 8.18 | 8.18 | 10.69 | 8.77 | 10.77 | 10.86 | 10.77

## Slide 17: Spectral Growth under PA Impairment
Option 1 (Golay) causes less spectral growth for OBO = 5 dB as compared to other options

## Slide 18: BER Results
When the samples are clipped heavily because of PA, the sum of absolute values can decrease and WUSs can interfere with each other
  Saturation can degrade the BER performance at WURx (e.g., Option 3)
  Golay-based WUS provides robustness against PA non-linearity by minimizing the fluctuation in time for FDMed OOK symbols
Golay-based WUS is robust
Similar performance
w/o PA

## Slide 19: Conclusion
The PAPR can be significantly large when WUSs are FDMed
  Without taking any precautions, it can reach 10-13 dB or higher, which limits the coverage range of 802.11ba in some regions
The PAPR minimization for FDMed WUSs is an intractable problem due to the large number cases possible in an FDM scenario
  The phase rotations in IEEE 802.11ac cannot address all cases and they are a function of the sequence
  A scalable solution is needed
Existing Golay sequences can address the PAPR issue as the corresponding signals are always bounded by 3 dB
  We show that the PAPR gain can reach more than 3 dB in some cases
  Golay sequences are publicly available
    Known since 1960s
    Heavily-used in 802.11ad/ay
    Used for PAPR minimization, coding, etc. in academic studies

## Slide 20: Appendix

## Slide 21: PAPR
[1]: IEEE 802.11-18/0492r0
[2]: IEEE 802.11-18/0479r2
Mean power
6.4 dB [1]
3.6 dB [2]
While PAPRs are 3.4 and 0.6 dB for 2 s duration for the waveform in 492 and 479, respectively, they increase by 3 dB for a measurement at 4 s duration since there is no energy for the OFF durations in the corresponding waveforms
This means that if the ON period is generated via a Golay sequence, the PAPR will be limited to 6 dB for a measurement which covers both ON and OFF durations

## Slide 22: PAPR Results – Case 1
 | Case 1 |  | 
Rates: | _ _ H H |  | 
Probability: | .5 | .8 | .99
Option 1 (Golay) | 6.02 | 6.02 | 6.02
Option 2 (256QAM) | 6.60 | 6.60 | 6.60
Option 3 (BPSK) | 9.38 | 9.38 | 9.38
Option 4 (BPSK) | 8.25 | 8.25 | 8.25

## Slide 23: PAPR Results – Case 2
 | Case 2 |  | 
Rates: | H H H H |  | 
Probability: | .5 | .8 | .99
Option 1 (Golay) | 6.01 | 6.67 | 6.67
Option 2 (256QAM) | 7.12 | 7.12 | 7.12
Option 3 (BPSK) | 9.89 | 12.39 | 12.39
Option 4 (BPSK) | 8.77 | 8.77 | 8.77

## Slide 24: PAPR Results – Case 3
 | Case 3 |  | 
Rates: | L L H H |  | 
Probability: | .5 | .8 | .99
Option 1 (Golay) | 6.61 | 6.61 | 6.67
Option 2 (256QAM) | 7.37 | 9.55 | 9.80
Option 3 (BPSK) | 8.99 | 11.08 | 11.13
Option 4 (BPSK) | 8.22 | 10.60 | 10.67

## Slide 25: PAPR Results – Case 4
 | Case 4 |  | 
Rates: | L L L H |  | 
Probability: | .5 | .8 | .99
Option 1 (Golay) | 6.62 | 6.67 | 6.67
Option 2 (256QAM) | 7.37 | 7.46 | 9.91
Option 3 (BPSK) | 8.39 | 8.59 | 10.63
Option 4 (BPSK) | 8.18 | 8.18 | 10.69

## Slide 26: PAPR Results – Case 5
 | Case 5 |  | 
Rates: | H H L H |  | 
Probability: | .5 | .8 | .99
Option 1 (Golay) | 6.01 | 6.62 | 6.67
Option 2 (256QAM) | 7.24 | 9.29 | 9.71
Option 3 (BPSK) | 9.72 | 11.36 | 11.41
Option 4 (BPSK) | 8.77 | 10.77 | 10.86

## Slide 27: BER (Case 3)
Golay-based WUS is robust
Golay-based WUS is robust

## Slide 28: SP
Do you agree that the method of OOK waveform generation based on Golay sequences described in the Slide 10 can be included in the 802.11ba spec as an example for implementing the frequency domain multiplexed WUS?
Y
N
A